## Slide 1: Analysis on options for I-SMF insertion for Local Offloading Management
Nokia
Document for: Discussion Agenda Item: 19.9 Work Item / Release: eEDGE_5GC_Ph3 / Rel-19
SA WG2 Meeting #166 S2-2412255
18 – 22 November, 2024, Orlando, US

## Slide 2: Background
In SA2#164 meeting, two options on I-SMF insertion for Local Offloading Management are proposed.
In SA2#165 meeting, the common parts of both options are captured in the agreed CRs.
The main difference on how to trigger I-SMF insertion is left open and going to be handled in this meeting.
Overall, the two options can be summarized as follows:
  Option 1: AMF performs I-SMF insertion based on Local Offloading allowed indication as part of SMF Subscription data (S2-2409762). This option mimics HR-SBO procedures defined in clause 6.7.2 of TS 23.548. Therefore, it requires to select two SMFs (I-SMF and SMF) in HPLMN during the PDU session establishment for non-roaming scenario.
  Option 2: SMF triggers I-SMF insertion based on Local Offloading allowed indication as part of SM Subscription data (S2-2410600). This option reuses the existing procedure on SMF triggered I-SMF selection and removal in clause 4.23.5.4 of TS 23.502. SMF sends Local Offloading Allowed indication to AMF together with a target DNAI, and AMF selects I-SMF.

## Slide 3: Possible cases
Case #1: UE is inside one SMF service area (during PDU session establishment)
Case #2: UE is inside two SMFs service area (during PDU session establishment)
Case #3: UE moves outside of the anchor SMF service area (after PDU session establishment)
Case #4: UE is in roaming (during PDU session establishment) (e.g., HR-SBO)
Case #5: UE is inside the anchor SMF service area but the target DNAI is not served by the anchor SMF (after PDU session establishment)
Case #6: UE is inside the anchor SMF service area but the target DNAI is not served by the anchor SMF (during PDU session establishment)

## Slide 4: Possible cases
Case #1: UE is inside one SMF service area (during PDU session establishment)
  Follows the existing SMF selection functionality at AMF (clause 6.3.2 of TS 23.501)
  AMF selects SMF A as the anchor SMF
SMF A
Service Area
Existing procedure, not related with the ongoing discussion.

## Slide 5: Possible cases
Case #2: UE is inside two SMFs service area (during PDU session establishment)
  Follows the existing SMF selection functionality at AMF (clause 6.3.2 of TS 23.501)
  AMF selects only one of the SMFs based on UE location, together with other criteria as in clause 6.3.2 of TS 23.501.
    For both cases, either SMF A or SMF B becomes the anchor SMF
SMF A
Service Area
SMF B
Service Area
SMF A
Service Area
SMF B
Service Area
Case #2.1
Case #2.2
The existing procedure/SMF selection functionality enables AMF to select a proper anchor SMF during PDU session establishment.
Option 1 contradicts with the existing procedure

## Slide 6: Possible cases
Case #3: UE moves outside of the anchor SMF service area (after PDU session establishment)
  Pre-condition: An anchor SMF (SMF A in the figure) has already been selected by the AMF.
  AMF determines that the UE has moved outside of the anchor SMF service area.
  AMF selects an I-SMF that can serve the UE location and S-NSSAI or relocates the anchor SMF.
    When AMF selects an I-SMF, DNN and subscription information from UDM
    are not considered (clause 6.3.2 of TS 23.501).
    SMF B becomes the anchor SMF OR I-SMF (depending on SMF relocation or I-SMF insertion case).
SMF A
Service Area
SMF B
Service Area
SMF A
Service Area
SMF B
Service Area
Case #3.1
Case #3.2
For the I-SMF insertion case, in order to enable Local Offloading Management, AMF needs to select an I-SMF that supports Local Offloading Management capability.
Already captured in SA2#165 agreed CR - S2-2410930

## Slide 7: Possible cases
Case #4: UE is in roaming (during PDU session establishment) (e.g., HR-SBO)
  Pre-conditions:
    SMF A is part of UE’s HPLMN whereas SMF B is in VPLMN.
    HPLMN and VPLMN have an agreement on the support of the local traffic routing.
    Service area of different PLMNs does not overlap (SMF A and SMF B has disjoint service areas, hence, the UE is outside of H-SMF service area).
  During PDU session establishment, the AMF selects both an SMF in VPLMN and additionally, an SMF in the HPLMN for the PDU Session.
    SMF B is selected as V-SMF, and SMF A is selected as H-SMF.
SMF A
Service Area
(HPLMN)
SMF B
Service Area
(VPLMN)
Existing procedure, not related with the ongoing discussions.
Roaming scenario is out of scope of Rel-19 KI#1/WT#1.

## Slide 8: Possible cases
Case #5: UE is inside the anchor SMF service area but the target DNAI is not served by the anchor SMF (after PDU session establishment)
  Pre-condition: An anchor SMF (SMF B in the figure) has already been selected by the AMF and the target DNAI can be served by the anchor SMF.
  The anchor SMF receives/decides (based on UE mobility and/or AF traffic influence request) a new target DNAI that is not served by the anchor SMF. The anchor SMF provides the target DNAI to AMF.
  AMF selects an I-SMF based on the target DNAI and supported DNAI(s) of (I)-SMF (clause 5.34 of TS 23.501).
    For Case #5.1 and Case #5.2, SMF B is the anchor SMF, and SMF A becomes the I-SMF.
    For Case #5.3, SMF A is the anchor SMF, and SMF B becomes the I-SMF.
SMF A
Service Area
SMF B
Service Area
Case #5.1
Case #5.2
SMF A
Service Area
SMF B
Service Area
Case #5.3
SMF A
Service Area
SMF B
Service Area
In order to enable Local Offloading Management, the anchor SMF should provide Local Offloading Allowed indication to AMF together with the target DNAI.
Option 2 proposes/enables this

## Slide 9: Possible cases
Case #6: UE is inside the anchor SMF service area but the target DNAI is not served by the anchor SMF (during PDU session establishment)
  Follows the existing SMF selection functionality at AMF (clause 6.3.2 of TS 23.501)
  AMF selects only one of the SMFs
    For both cases, either SMF A or SMF B becomes the anchor SMF
  During PDU session establishment, the anchor SMF decides a target DNAI that is not served by the anchor SMF. The anchor SMF provides the target DNAI to AMF.
  AMF selects an I-SMF based on the target DNAI and supported DNAI(s) of (I)-SMF (clause 5.34 of TS 23.501).
    For both cases, either
      SMF B is the anchor SMF, and SMF A becomes the I-SMF; or
      SMF A is the anchor SMF, and SMF B becomes the I-SMF.
SMF A
Service Area
SMF B
Service Area
Case #6.1
Case #6.2
SMF A
Service Area
SMF B
Service Area
In order to enable Local Offloading Management, the anchor SMF should provide Local Offloading Allowed indication to AMF together with the target DNAI.
Option 2 proposes/enables this

## Slide 10: Observations
During PDU session establishment for non-roaming scenario, AMF selects only one SMF (cf., Case #2).
I-SMF insertion is triggered by AMF if the UE is outside of the SMF service area or if the target DNAI cannot be served by the selected anchor SMF. Therefore, the AMF should select an anchor SMF first.
  During I-SMF insertion, AMF considers either SMF service area (if UE moves out the anchor SMF service area) or target DNAI and supported DNAIs (if the anchor SMF provides a target DNAI).
During PDU session establishment for home routed roaming scenario, AMF selects both V-SMF and H-SMF (cf., case #4).
  This would fit the case “if the UE is outside of the SMF service area” as the UE is in roaming, meaning that the UE is outside of the HPLMN service area.
During PDU session establishment, AMF is not aware of a target DNAI as the target DNAI is obtained by the anchor SMF, meaning that after the anchor SMF selection.
The existing SMF selection functionality at AMF and I-SMF insertion mechanism can support all the given cases.
  The required enhancements to enable Local Offloading Management are highlighted for each case.

## Slide 11: Observations
During PDU session establishment for a non-roaming scenario, AMF selecting two SMFs (an anchor SMF and I-SMF for local offloading management) is not supported today and would require too many changes to the existing I-SMF procedures. Moreover, it will not bring any benefit on neither enabling I-SMF to select and configure EASDF nor the configuration needed to be available at the anchor SMF.
  The anchor SMF still needs to perform target DNAI selection, irrespective of whether I-SMF based local offloading management applies or not, for all other UEs that it serves.
  The anchor SMF and I-SMF would anyway need to have DNAI mapping.
  AMF, on its own, cannot indicate I-SMF to select and configure an EASDF.
  In order to ensure that the DNS request is sent to EASDF or DNS resolver that is provided by the operator, the UE should support EDC functionality. The UE capability to support EDC functionality is provided to the anchor SMF via PCO. In other words, the (anchor) SMF is the only 5GC entity that is aware of the UE capability and can be the decision point to use EASDF.
  In case the selected I-SMF does not support a given target DNAI, it needs to be removed. In other words, it will be selected and then removed with no use, and extra signalling would be required to remove unused I-SMF.
    Hence, Option 1 would lead to unnecessary signaling.

## Slide 12: Proposal
During PDU session for a non-roaming scenario, AMF performs the SMF selection based on the existing mechanisms – selects only one SMF that is going to be the anchor SMF.
In order to enable Local Offloading Management, the selected anchor SMF should decide whether I-SMF should be inserted during or after PDU session establishment.
If the anchor SMF evaluates the following points and determines that I-SMF should be inserted, the anchor SMF may trigger I-SMF insertion.
  UE is allowed for Local Offloading Management (based on SM subscription data),
  UE capability supports EDC functionality, and
  there is a need to offload Edge Computing related information management.
The anchor SMF should provide Local Offloading Management allowed indication (retrieved from SM Subscription data) to AMF, so that AMF would provide the indication to the selected I-SMF to enable I-SMF to select and configure EASDF.