## Slide 1: Analysis on 5G_Femto WT#1 – Access to Local services via Femto Nokia
3GPP TSG SA2 Meeting #166 18 – 22 November 2024, Orlando, US
S2-2412278
TSG SA2#166, 18 – 22 Nov 2024
Document for: Discussion Agenda Item: 19.12 Work Item / Release: 5G_Femto / Rel-19

## Slide 2
WT#1: Based on the “Conclusion and Recommendation for NR Femto” captured in clause 6.2 of TR 38.799, evaluate the functional and procedural enhancements (including Access to Local Services aspects, see clause 5.4 of TR 38.799) and specify them to support the 5G NR Femto deployment.
Rel-19 RAN SI on Femto has the objective:
  Clarify the access to local services from the 5G Femto via collocated local UPF and identify issues, if any [RAN3].
RAN3 has concluded:
  NR Femto nodes reuse LADN and edge computing functionality as specified in TS 23.501 and TS 23.548.
RAN3 also identified the following open issues that should be further studied in SA2:
  Aspect #1: Scalability of local UPF discovery e.g. when using mobile edge computing solutions,
  Aspect #2: N4 interface switch-on/off,
  Aspect #3: N4 interface aggregation.
WT#1 in SP-241327
TSG SA2#166, 18 – 22 Nov 2024

## Slide 3: Scenarios to consider on access to local services from the 5G Femto via co-located local UPF
Scenario 1: access to local services from the 5G Femto via co-located local UPF
  Assumption: Each NR Femto node is assigned with a unique CAG ID or list of CAG IDs.
Scenario 2: access to local services from the 5G Femto via standalone UPF
  Assumption: NR Femto nodes share the same CAG ID or list of CAG IDs for a given environment.
NR Femto Node
UPF
NR Femto Node
UPF
NR Femto Node
UPF
NR Femto Node
UPF
NR Femto Node
UPF
NR Femto Node
NR Femto Node
NR Femto Node
NR Femto Node
NR Femto Node
NR Femto Node
NR Femto Node
UPF
UPF
CAG ID 1
CAG ID 2
CAG ID 3
CAG ID 4
CAG ID 5
CAG ID 6
CAG ID 6
CAG ID 6
CAG ID 6
CAG ID 7
CAG ID 7
CAG ID 7
TSG SA2#166, 18 – 22 Nov 2024

## Slide 4: Issues with RAN3 conclusions
Reusing LADN on access to local services from the 5G Femto via co-located local UPF:
  Based on 23.501 § 5.6.5:
    The access to a DN via a PDU Session for a LADN is only available in a specific LADN service area. A LADN service area is a set of Tracking Areas.
    LADN service area and LADN DNN are configured in the AMF on a per DN basis, i.e. for different UEs accessing the same LADN, the configured LADN service area is the same regardless of other factors (e.g. UE's Registration Area or UE subscription).
  Issue:
    As the LADN service area has tracking area granularity, it cannot be used for cell-level access to local services via 5G Femto.
    Considering the high number of deployments with NR Femto nodes:
      For Scenario 1: having configuration in the AMF on a per DN basis will not scale and will be hard to manage such configuration in the AMF.
      For Scenario 2: re-configuring a tracking area (or smaller tracking area) for a specific campus deployment is not easy for an operator and restricts any uncoordinated deployment solution.
        This was discussed during slicing feature on non-uniform supporting TA and precluded.
        High number of tracking areas with small size impacts Paging and Mobility Registration Update signalling.
        Small size tracking area would also mean lots of additional tracking areas (on top of overlay/macro cell) to manage for the operator.
TSG SA2#166, 18 – 22 Nov 2024

## Slide 5: Issues with RAN3 conclusions
Reusing Edge Computing functionality on access to local services from the 5G Femto via collocated local UPF:
  Based on 23.501 § 6.3.3.3, the following information may be used for UPF selection:
    Information related to user plane topology and user plane terminations, that may be deduced from:
      5G-AN-provided identities (e.g. CellID, TAI), available UPF(s) and DNAI(s)
  Based on 29.510 § 6.1.6.1, 6.2.6.1 and 6.1.6.2.13, there is no CellID (cf., C4-186263).
  Issue:
    As the existing UPF profile information has tracking area granularity, it cannot be used for cell-level access to local services via 5G Femto.
    Considering the high number of deployments with NR Femto nodes, having cell ID granularity as part of UPF profile in NRF will not scale as cell ID would represent any cell including the macro/micro cells without any access control.
    Using Cell ID would be fine for Scenario 1. However, it would create some issues for Scenario 2 as follows:
      For Scenario 2, using a CAG ID instead of cell ID would prevent introducing the same message for all NR Femto nodes deployed in the campus environment
        For example, instead of sending the same information from 10s of NR femto nodes deployed in the campus, it will be represented by single CAG ID information.
      For Scenario 2, using CAG ID instead of cell ID would enable flexibility on cell management – adding/removing cells to be part of allowed CAG ID.
TSG SA2#166, 18 – 22 Nov 2024

## Slide 6: Options to enable access to local services from the 5G Femto via co-located local UPF
Option 1: Providing relevant CAG information using node level signaling via N4 association [SA2#165, S2-2410849 and S2-2410848]
Option 2: Providing relevant CAG Information using node level signaling via NRF related procedure
Option 3: Providing relevant CAG information using UE associated signaling
Option 4: Configuring LADN DNN and associated CAG ID information and S-NSSAI location availability information [SA2#165, S2-2410360 and S2-2410368]
TSG SA2#166, 18 – 22 Nov 2024

## Slide 7: Options to enable access to local services from the 5G Femto via co-located local UPF
Option | Summary | Impacts
Option 1: Providing relevant CAG information using node level signaling via N4 association | SMF learns the IP address of the co-located UPF and locally stores the IP address associated with the CAG Information that the co-located UPF provided via N4 association setup/update message. | AMF provides CAG ID to SMF during PDU session establishment/modification. N4 association setup/update includes associated CAG ID(s). UDM/SM subscription data is updated with local breakout info of corresponding CAG ID.
Option 2: Providing relevant CAG Information using node level signaling via NRF related procedure | When co-located UPF registers its UPF profile to the NRF, the CAG Information is provided among other UPF profile information. NRF provides the co-located UPF profile including the CAG information to SMF. | AMF provides CAG ID to SMF during PDU session establishment/modification. NRF UPF profile includes associated CAG ID(s). UDM/SM subscription data is updated with local breakout info of corresponding CAG ID.
Option 3: Providing relevant CAG information using UE associated signaling | During Initial UE message or UL NAS Transfer message, it is the NR Femto node providing the IP address of co-located UPF and the association with CAG ID to the AMF. AMF provides the co-located UPF IP address and CAG information to SMF. | AMF provides CAG ID to SMF during PDU session establishment/modification. Initial UE message or UL NAS Transfer message includes the IP address of co-located UPF that is associated to the CAG ID that UE accesses. UDM/SM subscription data is updated with local breakout info of corresponding CAG ID.
Option 4: Configuring LADN DNN and associated CAG ID information and S-NSSAI location availability information | LADN DNN is configured as associated with CAG ID(s) in the NEF or UDM (i.e. the associated LADN information such as LADN DNN and LADN service area per DNN and S-NSSAI). In order to enable NR Femto node/cell granularity, the associated NSSAI location availability information is configured by AMF or OAM configuration. | AMF is configured with both LADN DNN and associated CAG ID(s) as well as S-NSSAI location availability information. Requires support of both LADN and S-NSSAI location availability features in the network and UE. UDM/AM subscription data is updated with local breakout/LADN info of corresponding CAG ID.
TSG SA2#166, 18 – 22 Nov 2024

## Slide 8: Observations
For all the given options, UDM/subscription data needs to be updated.
  Session Management data for Options 1, 2, 3 and Access and Mobility data for Option 4.
Options 1 and 3 enable SMF to locally store the co-located UPF and CAG ID information, and Option 2 enables NRF to store the information.
  Whereas Option 4 does not define the retrieval of co-located UPF information and only enables/focuses on Scenario 2 defined in slide #3.
Option 1, 2 and 3 enable access to local services from the NR Femto node independent from the deployment scenario (i.e., Scenario 1 and Scenario 2 in slide #3).
  Furthermore, Options 1, 2 and 3enable dynamic handling of co-located UPF and associated CAG information change (adding/removing CAG IDs).
Option 4 has dependency on supporting LADN as well as S-NSSAI location availability information (introduced in Rel-18) both at the network and UE sides.
  Moreover, as it relies on configuration at AMF, handling dynamic changes and supporting Scenario 1 deployments are not straightforward.
In case multiple UEs are accessing local services via NR Femto node, the same information will be sent to AMF for these UEs in Option 3.
TSG SA2#166, 18 – 22 Nov 2024

## Slide 9: Proposed Way Forward
Consider either
  Option 1 – N4 (S2-2412279/S2-2412280); or
  Option 2 – NRF (S2-2412285/S2-2412286)
  to enable access to local services from the 5G Femto via co-located or standalone local UPF.
These options has no UE impact.
TSG SA2#166, 18 – 22 Nov 2024