## Slide 1: Discussion on the VFL feature alignment
OPPO
S2-240XXXX
SA2#166

## Slide 2: Status for the feature registration and alignment
Observation：
Based on the above ENs, two issues need to be considered.
  Whether and how to register the feature related info to the NRF and consider the feature info for each client when perform the VFL client discovery?
  Whether the feature related info need to be negotiated between the server and clients during the preparation phase to perform the feature alignment?
The following editor’s notes are captured in TS 23.288 or approved CR:
  Editor's note: Details regarding features alignment functionality or whether the functionality needs to be specified are FFS. (CR: 2411195 – KDDI; Clause 5.4)
  Editor's note: Whether additional selection criteria are required is FFS (e.g. vendor information and feature related information). (CR: 2411193 – vivo; Clause: 6.2H.2.1.2)
  Editor's note: Details of ML Model handling, supported features, Feature alignment are FFS. (CR: 2411193 – vivo; Clause: 5.2)
  Editor's note: Whether the VFL Interoperability information (e.g. type of supported VFL training method(s), vendor information, and feature related information) needs to be part of the NF profile registered in NRF is FFS. (CR: 2411193 – vivo; Clause: 5.2)

## Slide 3: What is the feature means and the needed for the Feature alignment
Feature is a measurable property of some sample that is used as input for a ML model for training and inference
  For example, for the existing Observed Service Experience related network data analytics, in order to support the request Service Experience analytics for a UE or for a group of UE, many parameters from different entity(e.g. AF, AMF, SMF, UPF) for the UEs are considered.
  UE is the sample and the different parameters for that UE will be treat as the feature of that sample.
  Some of the parameters can be collected and provided by different NWDAFs and AFs, therefore, the parameters may have overlap in different entities.
  VFL need the different entities have the same samples but different feature. The feature alignment is needed.

## Slide 4: Feature info register to the NRF
Case 1 Only the feature info register to NRF is enough to support the feature alignment
  Considering the feature is a sensitive information, and it is vender specific information, a feature ID could be used to represent the feature info supported by different entity.
  Feature ID is a vender specific information.
  Feature ID will be register to the NRF which will be a part of the VFL interoperability information in order to let different venders (which are interoperable between each other) can understand what the feature ID means.
  Server can based on the discovery procedure to get the feature info supported by the discovered entity and determine which feature will be used.

## Slide 5: Feature alignment based on the negotiation
Case 2 The feature alignment is based on the negotiation between the different entities
  Considering the feature maybe dynamic and it is related to the sample. Register to the NRF may cause NRF overload and need frequent update.
  Feature info should be negotiated between the VFL server and VFL client.
  VFL server will send the feature alignment request to the client which include the target feature information. Client will response to the Server what feature the client can supported.

## Slide 6: Combine both case 1 and case 2
Case 3 The feature alignment is based on the registration and discovery and further negotiated between the different entities
  Different VFL client can register to the NRF with the feature ID based on historic data it can be collected. Feature ID is a part of the VFL interoperability info. Consider the feature ID is based on the historic feature info, it maybe quite stable.
  Since the feature ID can only reflect what the feature the entity can support to be collected in the historic. It can not ensure for the current VFL operation, those feature can be collected. Therefore, only depend on the feature ID register in the NRF is not enough to support the feature alignment.
  After performing the VFL client discovery base on the feature ID, server sends the VFL preparation request to the client which include the target feature information represented by the feature ID.
  Client will response to the server what feature the client can supported with the feature ID.

## Slide 7: Companies views for case 1,2,3
Companies | Case 1 (feature ID registration) | Case 2 (feature info negotiation) | Case 3 (Combine) | Other case
OPPO |  |  | Preferred. VFL client can register to the NRF what the feature it can support to be collected using the feature ID. It will help the server to first select the client which can possibly provided the target feature. Then based on the negotiation, server and client can align the current feature used by different entity. | 

## Slide 8: Way forward
Depending on the outcome for the companies views in page 7