## Slide 1: SUCI Error paper compilation

## Slide 2
SUCI Error background
CT6 CR- C6-240155 Summary: CR is agreed with the text if information like “SUPI Type”, “HN ID”, “RID” etc required for the SUCI calculation is not correctly configured in the USIM, the USIM shall return an error status word.
CT1 LS- C1-245039
Summary: In C6-240155 (CR #1030 for TS 31.102) CT6 clarified that in case the information required for the SUCI calculation is not correctly configured in the USIM, USIM shall return an error status word. However it is unclear how the UE shall behave in this case in order to get service either in 5GC or EPC.
ACTION: CT1 kindly asks SA3 to discuss the topic and provide feedback how the UE should handle the described SUCI calculation failure.

## Slide 3
Scenarios
Scenario | Consequence
Scenario#1: Home network updates the configuration related to SUCI but after that the UE moves to unregistered state. Therefore, no security context in NAS or in AS is available. | UE tries to trigger the registration request towards the 5GC but fails because SUCI calculation fails. So, UE cannot get the 5GC service.
Scenario #2:UE is registered and authenticated in 5GC. NAS and AS has the security context. Home network updates the configuration related to SUCI and now the SUCI cannot be calculated (registered state). | In this case, UE can report the error to the network and network can correct the issue. Therefore, NULL scheme setting may/may not be required
Scenario#3: Home network updates the configuration related to SUCI and then UE moves to EPC/4G. UE comes back in 5GC but registration to 5GC fails because SUCI calculation fails | UE can still use the EPC service, not 5GC

## Slide 4
Scenarios
Company\ solution | Concrete proposal | Disable N1 | NULL scheme solution |  |  | Remark
Apple- S3-244711 | Yes | Yes | No |  |  | 
Samsung- S3-245045 | Yes | - | Yes |  |  | Proposal: (avoid MitM attack) SUCI with NULL scheme should be calculated in USIM. Allow timer to avoid again and again reconfiguration
QualcommS3-244949 | Yes |  | Yes |  |  | 
Deutsche Telekom AG-S3-244605 | Yes | - | No: Against NULL scheme |  |  | 
VivoS3-244730 | Yes |  | Yes |  |  | (NULL scheme based on user permission)
Nokia S3-244708 | No |  |  |  |  | Mini WID proposed to address this in next meeting..
Huawei- S3-244897 | No |  | Yes ? |  |  | (we are in favor of allowing the UE to continue accessing 5G and investigate how such a failure is communicated to the network as early as possible in order for the network to act accordingly.)