3GPP TSG-SA3 Meeting #116	S3-241838

Jeju, South Korea,  20th - 24th May 2024

# Source:	Thales

# Title:	Key Issue #1: conclusion

# Document for:	Approval

Agenda Item:	5.6

# 1	Decision/action requested

This contribution proposes a conclusion for the Key Issue #1 of TR 33.701.

# 2	References

[1]	3GPP TR 33.701	v0.2.0

# 3	Rationale

This contribution proposes to conclude for Key Issue #1 that the solution #X "configuration in UE per country", described in contribution S3-241837, is used as baseline for normative phase.

The rationale for such a conclusion is that this solution relies only on information stored in the UE: configuration information stored on the USIM and location information determined by the UE. This solution avoids relying on information sent by a base station, as this base station could potentially be a false base station providing for example fraudulent SMS or phone call.

# 4	Detailed proposal

It is proposed that SA3 review and approve the following pseudo-CR to TR 33.701 [1].

*** START of CHANGE ***

# Y	Conclusions

## Y.1	Conclusions on KI #1

Solution #X "configuration in UE per country" is used as baseline for normative phase.

*** END of CHANGE ***