3GPP TSG-SA3 Meeting #116	draft_S3-242557-r1

Jeju, South Korea,  20th - 24th May 2024

# Source:	ZTE

# Title:	New solution for SUPI privacy issue

# Document for:	Approval

Agenda Item:	5.3

# 1	Decision/action requested

This contribution proposes to add a new solution for SUPI privacy issue

# 2	References

# 3	Rationale

The contribution proposes to add a new solution for SUPI privacy issue.

# 4	Detailed proposal

It is suggested to approve the following change.

*************** Start of the change ****************

## 7.Y	Solution #Y:Use a new PLMNNPN UE ID to resolve the SUPI privacy issue

### 7.Y.1	Introduction

This solution address the key issue#3 SUPI privacy issue in PLMN hosting NPN scenario.A Security for PLMNNPN Network Function(SPNF) is designed to conceal/de-conceal PLMNNPN UE ID

### 7.Y.2	Solution details

- The AMF/SEAF may initiate an authentication with the UE during any procedure establishing a signalling connection with the UE, according to the AMF/SEAF's policy. The UE shall use SUCI or 5G-GUTI in the Registration Request.

- The AMF/SEAF in the customer premises invoke the Namf_Commuincation_N1Message Notify service by sending a Namf_Commuincation_N1Message Notify message to an AMF which is located in the operator premises. If AMF/SEAF in the customer premises has the UE context, the AMF/SEAF in the customer premises replace the 5G-GUTI to PLMNNPN UE ID. The Namf_Commuincation_N1Message Notify message at least include SUCI or PLMNNPN UE ID, SN name, PLMNNPN service indication.

- Based on the PLMNNPN service indication, the AMF/SEAF in the operator premises knows the AMF/SEAF in the customer premises wants to trigger the primary authentication. The AMF/SEAF in the operator premises shall invoke the Nausf_UEAuthentication service by sending a Nausf_UEAuthentication_Authenticate Request message to the AUSF when receive the Namf_Commuincation_N1Message Notify message in the step 2.

- The Nausf_UEAuthentication_Authenticate Request message shall contain either SUCI or PLMNNPN UE ID. Nausf_UEAuthentication_Authenticate Request message may further contain the serving network name. Nausf_UEAuthentication_Authenticate Request message may further contain a PLMNNPN service indication.

- Upon reception of the Nudm_UEAuthentication_Get Request, the UDM shall invoke SIDF if a SUCI is received. SIDF shall de-conceal SUCI to gain SUPI before UDM can process the request. UDM shall invoke Security for PLMNNPN Network Function(SPNF) if a UE ID which is used in a customer premises is received. Security for PLMNNPN Network Function(SPNF) shall return SUPI. Based on the PLMNNPN UE ID generation method, the SPNF de-conceal PLMNNPN UE ID or find the mapping(SUPI, PLMNNPN UE ID). For each Nudm_Authenticate_Get Request, the UDM/ARPF shall create an authentication vector. If a SUCI is received, Nudm_Authenticate_Get Response may further contain a new PLMNNPN UE ID.

- The AUSF sends a AV in Nausf_UEAuthentication_UEAuthentication message to the AMF in the operator premises.

- The AMF/SEAF in the operator premises forward the Nausf_UEAuthentication_UEAuthentication message in step 6 to the AMF in the customer premises, then the AMF/SEAF in the customer premises sends the Authentication request message to UE.

- UE response an authentication response message with RES*, then the AMF/SEAF in the customer premises sends an authentication response message to the AMF in the operator premises.

- The AMF/SEAF in the operator premises sends a Nausf_UEAuthentication_Authenticate Request message with RES* to AUSF.

- The AUSF shall indicate to the AMF/SEAF in the Nausf_UEAuthentication_Authenticate Response whether the authentication was successful or not from the home network point of view. If the authentication was successful, the KSEAF shall be sent to the AMF/SEAF in the Nausf_UEAuthentication_Authenticate Response. In case the AUSF received a SUCI or PLMNNPN UE ID from the AMF/SEAF in the authentication request, and if the authentication was successful, then the AUSF shall also include the PLMNNPN UE ID in the Nausf_UEAuthentication_Authenticate Response message if received from UDM.

- The AMF/SEAF in the operator premises generate the Kamf and deleted the SUPI in Nausf_UEAuthentication_Authenticate Response message then sends an Namf_UEcontext transfer message to the AMF in the customer premises. The message at least include one of the followings: Result, PLMNNPN UE ID, Kamf, Result, etc.

- The AMF in the customer premises registers with the UDM using Nudm_UECM_Registration for the access to be registered. The message include the PLMNNPN UE ID, AMF ID.

- The UDM decide whether the AMF can use SUPI based on the AMF ID. If the AMF can use SUPI (e.g due to LI concern ), the UDM sends a SUPI to AMF.

- The AMF/SEAF in the customer premises sends UE a registration accept message to UE if the authentication is passed.The AMF/SEAF assign a new 5G-GUTI for the UE.

### 7.Y.3	Evaluation

TBD

Editor’s Note: whether the solution fulfill the requirement of key issue #3 is FFS.

Editor’s Note: The impact on LI is FFS.

*************** End of the change ****************