## Slide 1: Discussion Paper on Ultra Low Bitrate Codecs For Voice Call using GEO satellite access
China Mobile，vivo，Spreadtrum, Fraunhofer IIS
2024.11
3GPP TSG SA WG4#130
Orlando, USA, 18-22 November 2024
Tdoc S4-241928

## Slide 2: Content
Background and motivation
1
Objectives
3
Proposal and Time plan
4
Justifications
2

## Slide 3: Background and motivation
  Proprietary solutions
    Commercialized GEO satellites and existing smartphone products supporting GEO satellite direct communication can provide SMS and voices services. GEO satellite access as a complement to terrestrial network coverage, brings new values and opportunities to various market segments including IoT and smartphones.
  Standard solutions
    For terrestrial and non-terrestrial convergence, ITU-T Y.3200 and Y.3201 have proposed fixed, mobile and satellite converged network architectures including satellite-based and land-based network architectures. 3GPP also has been working on IoT-NTN since Rel-17 targeting direct communication over GEO satellites.
    3GPP SA1 has studied the IMS voice support over GEO satellite in Rel-20 since Mar. 2024. The use case has been well justified with corresponding requirements in TR 22.887.
Multi-access UE
(ng-)eNB
EPC or 5GC
GEO
Notes: 1、TR 38.811

## Slide 4: Background and motivation
NB-IoT access
  Half duplex (UE side)
  Bandwidth (DL): 180kHz
  Bandwidth (UL): 3.75kHz, 15kHz (single-tone), 180kHz (12-tone)
Data rate:
  ~1kbps data rate @ GEO + 23dBm phone(Realistic)
Commercialized services:
  SMS, Non-IP data transmission, etc.,
  Voice services is expected to start in Rel-20
  To support GEO satellite access, transparent payload is discussed in 3GPP standards (Rel-17, Rel-18). NB-IoT (GEO) satellite access is often preferred . This is due to NB-IoT‘s narrow bandwidth, ranging from 3.75 kHz to 180 kHz (as specified in TS 36.213), which is more compatible with the high altitude of GEO satellites.
Scenario | UE type | Transmission data rate |  | Call setup time
 |  | UL | DL | 
IMS voice call using GEO | Handheld | [1-3] kbit/s | [1-3] kbit/s | [4-30] s
SA4: It is expected to set up an ultra low bitrate codec work for voice call based on IoT-NTN(NB-IoT) using GEO satellite

## Slide 5
Background and motivation
China Mobile has organized a laboratory verification of IMS voice call based on IoT-NTN, through UE direct connection to GEO satellite in July 2024.
SA4 scope
Preferred performance
Bitrate: 0.4∼1.2Kbps
Mouth-to-ear delay: 2~3s
Quality >= AMR 4.75 kbp

## Slide 6: Justifications
codec | Bitrate | Source
MELP/ MELPe | 0.3Kbps, 0.6Kbps， 1.2Kbps,2.4Kbps | https://melp.org/ https://www.compandent.com/about-melpe/
AMBE/AMBE-LR | 1.6~1.8Kbps, 2.4~4.8Kbps | https://www.dvsinc.com/software/technology.shtml#ambelr
MPEG-HVXC | 1.2 ~ 1.7 Kbps 2.0Kbps,4.0Kbps | https://www.iso.org/obp/ui/en/#iso:std:iso-iec:14496:-3:ed-5:v1:en:sec:1.3
Codec 2 | 0.7~3.2Kbps | https://github.com/drowe67/codec2
For GEO satellite access speech, ultra low bitrate encoders are as follows, none of which has formed a standard in the field of mobile communication.
Existing IMS voice codecs in 3GPP cannot meet the low rate requirements:AMR-NB supports 8 encoding rates (4.75~12.20kbps) and AMR-WB supports 9 encoding rates (6.6~23.85kbps).EVS supports NB, WB, SWB, FB minimum coding rate of 5.9kbps. Developing IVAS supports more than 13.2kbps.

## Slide 7
Objectives
In addition to traditional LPC-based speech codecs, AI-based codecs can achieve better coding quality at very low rates, but also face the challenges of complexity.
Codec below 1.2kbps | LPC-based | AI-based
Performance |  | +
Complexity | + | 
Robustness |  | +
Security |  | +
Other | Codec2, for example, is an already defined LPC-based codec for low bit rate VoIP. But some parameters such as formant are difficult to reduce. | AI-based codec can extract high dimensional parameters and achieve better quality with less bandwidth.
Objective#1: Define performance requirements of ultra low rate codec for narrowband communications like IoT-NTN(NB-IoT) using GEO satellite access, considering bit rate, complexity, robustness to weak network, coding quality, security, etc.
Objective#2: Define an ultra low rate codec general framework ( LPC-based or AI-based codecs ) , considering above performance requirements as well as industry support.

## Slide 8: Objectives
 | Scenarios | Requirement
S1 | Satellite access terminal calling | Transcoding Default codec settings Optimize transmission efficiency
S2 | Satellite access terminal called | 
To achieve integration with the terrestrial voice communication system (4G/5G IMS architecture), it is necessary to develop transcoding functions on the network or UE side to complete the conversion of the ultra low rate speech codec and existing audio codecs.
Objective#3: Considering the interoperability between GEO satellite and terrestrial networks, implement IMS voice call transcoding function with existing audio codecs AMR,EVS, and explicit handle nodes.
Objective#4: Determine the appropriate ptime and packet headers to optimize transmission efficiency.

## Slide 9: Objectives
Quality testing
encoder
decoder
transcoder
Channel simulation
Objective#5: Enhance coding quality, leading to improved user experience, especially in terms of perception and complexity.
As a supplement to the terrestrial communication network, satellite communication service pays more attention to the ubiquitous connection. The evaluation and metrics of the codec also have some changes with different network condition. And perception and coding complexity may be more essential.
 | Metrics
Subjective quality | Perceptual evaluation of Speech Quality (e.g., P.800 ACR/DCR, BS.1534)
 | Perceptual evaluation of Speech intellegibility (e.g. P.807)
Objective quality | Objective evaluation of Speech Quality (e.g. PESQ, POLQA)
 | Objective evaluation of Speech Intelligibility (e.g. STOI, Articulation Index)
Other objective metrics | Processing delay
 | Complexity (e.g. real-time factor, MACs, MIPS, WMOPS)
 | Memory demand (RAM, ROM)
 | Preservation of loudness/gain

## Slide 10
Proposal and Time Plan
The overall objective is proposed to develop a codec for voice call services using GEO satellite access. The developments under this work should lead to a set of new specifications.
Date | Milestone
SA4#130 (18th – 22nd November 2024) | Discussion by SA4 on justifications and requirements of ultra low rate speech codec.
SA4#131 (17th – 21st February 2025) | Review and agreement by SA4 of the WID “Ultra low rate speech codec”
SA4#131-bis-e (11st – 17th April 2025) | Start definition of P-docs: performance requirements, design constraints, test plan, processing plan, selection rules & deliverables
SA4#132 (19th – 23nd May 2025) | Agreement of P-docs: performance requirements & design constraints Submission of LoI for candidates
SA4#133-e (21st – 25th July 2025) | Continue work on remaining P-docs.
SA4#134 (17th – 21st November 2025) | Agreement of all remaining P-docs: test plan, processing plan, selection rules & deliverables Candidate submission for codec selection
SA4#135 (9th – 13nd February 2026) | Selection completed Selection of “Ultra low rate speech codec” and approval of initial specifications
TSG SA#111 (10th – 13nd March 2026) | Approval by TSG SA (SA#111)

## Slide 11
Thank you!