## Slide 1: Discussion Paper on Available Capabilities and Information for XR Services
Jing Yue
Ericsson

## Slide 2: Agenda
Use Cases/Applications
Background
AIML Capability for XR Services
Available 5G Network Information for XR Services
Proposed solution
Summary

## Slide 3: XR Use Cases/Applications
  Entertainment and Gaming
    Gaming, virtually experience live music and sporting events.
    XR-film, virtual space where the viewer is physically part of the film, combination of the real world and virtual elements.
  Virtual try-on technology
    Virtual try-on technology to create Makeup Genius, a virtual mirror app for trying on makeup shades.
    Virtual closet experience, digital clothing on.
  Virtual test drives
    Transform an empty parking lot into a futuristic city landscape.
    Drive the new car model virtually.

## Slide 4: XR Use Cases/Applications
  Configuration / Virtual Showrooms
    Virtual car showroom.
    Virtual aircraft, configure the aircraft, including layout, materials, colors, and finishes.
  Virtual tours
    Virtual tours of stores in addition to virtual try-out features and interactive coupons.
    Virtual factory tour to showcase the manufacturing process.
  Virtual space
    Enabling consumers to view 3D models of various products in their space, furniture and home improvement.
  More: Healthcare, engineering and manufacturing, food, education, etc.

## Slide 5: Background – FS_XRApp
FS_XRApp - TR 23.700-23 v19.0.0
  4.4 - Key issue 4: Application enablement layer capabilities usage to supporting the XR services
    To support online AR gaming, the following capabilities could be leveraged (with potential enhancements): AI/ML may be required for Image & Object Recognition.
    It is proposed to study the following open issues:
    Whether and how the identified application enablement capabilities could be utilized to jointly support the XR service.
    Whether and how the application enablement architecture could support the XR service taking advantage of the identified application enablement capabilities.

## Slide 6: AIML Capability for XR Services
Consumer (e.g. VAL server) decides split image/video processing for a XR service, SEALDD server support data delivery for the XR service
AIMLE Server Assists Split AI/ML Operations
  Discovery split nodes - AIMLE server assists VAL server for discovery of split endpoints to take the split tasks on e.g. AI/ML image/video processing
  AI/ML task delivery - AIMLE server provides assistance information to SEALDD server for supporting the data delivery
    Time point/time window for data delivery with QoS requirement.
    Achievable QoS with current configuration of session between UE and AF (e.g. the consumer).
    Suggestion of QoS values for each flow of the session in order to satisfy application requirement.

## Slide 7: AIML Capability for XR Services
The assistance information from the AIMLE server can be used by the SEALDD server
  Time point/time window for data delivery with QoS requirement:
    Can be used to decide the time for data delivery/distribution and satisfy QoS requirement.
  Achievable QoS with current configuration of session between UE and AF (e.g. the consumer)
    Can be used to decide whether update of the current configuration is needed or not.
  Suggestion of QoS values for each flow of the session in order to satisfy application requirement
    Can be used to decide the configuration of each flow of the session.
The assistance information can be used separately or jointly depends on need at the SEALDD server.

## Slide 8: Available 5G Network Information for XR Services
Available 5GC information for XR data delivery
  E2E data volume transfer time analytics:
    A pre-configured data size (or data size range) may be used in the analytics request.
    The pre-configured data size may be the data size provided by the consumer, or be decided by the SEALDD server according to the data size range and based on its local policy.
    The predictions of E2E data volume transfer time for uplink/downlink given data volume can be used by the SEALDD server to set the individual QoS parameters (e.g. Requested 5GS Delay).
    The analytics subscription may be updated when the actual data size changed.

## Slide 9: Data Size
XR traffic is characterized by multiple service flows, and a wide variation in data sizes, etc.
In the request from the consumer to SEALDD server, assume that data size of the data to be delivered is contained.
  Consumer can estimate the data size according its previous applications with the same XR service. An estimated data size or a range of data size of the data to be delivered is provided by the consumer.
  If such information is not contained in the request, the SEALDD server rejects the service request from the consumer.
  The data size may be updated when actual data size changed. The actual data size may be obtained via measurement described in Sdd_TransmissionQuality Management API.

## Slide 10: Proposed Solution
All described use cases have implementations available at the XR market.
For the study aspect in key issue #4:
  Whether and how the identified application enablement capabilities could be utilized to jointly support the XR service. Following changes to FS_XRApp TR 23.700-23:
  Add solution on application enablement layer AIML capabilities for supporting XR services
The proposed changes provide solutions to address the study aspects in key issue #4, complete the study of corresponding key issue for FS_XRApp.

## Slide 11: Summary
This discussion paper proposes solutions to
  Address the study aspects of key issues #4 in clause 4.4 of TR 23.700-23 v19.0.0.
  Complete the study of corresponding key issues for FS_XRApp.
  It is proposed to discuss and agree on CR S6-244309 (CR#0002) that provides implementation of the solution described in the discussion paper.