## Slide 1: Discussion on how capture location reporting configuration in the user profile
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: Current status
In TS 23.280 v19.4.0, section 10.9.2.1, the LMS passes the location reporting configuration to the location management client.
  This configuration includes either or both emergency and non- emergency location information as optional elements.
  Currently there is no separate indication for the minimum time between consecutive reports for emergency and non-emergency cases.
  We would propose to include this.
Information element | Status | Description
MC service ID | M | Identity of the MC service user to which the location reporting configuration is targeted.
Requested non-emergency location information | O (see NOTE 1) | Identifies what location information is requested, except for emergency or imminent peril calls or emergency alerts
Requested emergency location information | O (see NOTE 1) | Identifies what location information is requested, for emergency or imminent peril calls or emergency alerts
Triggering criteria in non- emergency cases | O (see NOTE 1) | Identifies when the location management client will send the location report in non-emergency cases
Handling criteria in not reporting location information cases | O | Identifies when the location management client will store location information (e.g. never, off-network, IOPS)
Triggering criteria in not reporting location information cases | O (see NOTE 2) | Identifies the causes when the location management client will generate location information
Minimum time between consecutive reports | O (see NOTE 1) | Defaults to 0 if absent and 0 for emergency calls, imminent peril calls and emergency alerts
Triggering criteria in emergency cases | O (see NOTE 1) | Identifies when the location management client will send the location report in emergency cases
NOTE 1: If none of the information elements is present, this represents a cancellation for location reporting based on Triggering criteria in emergency and non-emergency cases, if configured. NOTE 2: If not present, location information is generated based on Triggering criteria in emergency and non-emergency cases, if configured. |  | 
Table 10.9.2.1-1: Location reporting configuration

## Slide 3: Proposal I
ESN proposal is to use the same configuration as in Table 10.9.2.1-1 as the ‘default’ location reporting configuration and store this in the user profile.
The emergency reporting configuration could be made mandatory (M) or optional (O) depending upon the requirements of the organization.
  This would also cover a scenario that for some users the default configuration is mandatory but for others it is optional, within the same organization.
An authorized user could apply a default or temporary reporting configuration to multiple users with the use of group ID, where these users are affiliated to.
This default configuration can be temporarily overridden by another reporting configuration applied through location reporting trigger (next slide).
  This temporary configuration would cancel once the location reporting trigger is cancelled as per section 10.9.3.4a. Thereafter, the default reporting configuration, if present, will be enforced.

## Slide 4: Proposal II
ESN further proposes that a temporary reporting configuration (applied through location reporting trigger) could contain either emergency or non-emergency related IE’s (of Table 10.9.2.1-1) or both.
In cases where the temporary reporting configuration contains only the emergency or non-emergency related IE’s:
  If the emergency related IE’s are not contained in the temporary reporting configuration, the emergency reporting should be done as per the related IE’s contained in the default location reporting configuration.
  If the non-emergency related IE’s are not contained in the temporary reporting configuration, the non-emergency reporting should be done as per the related IE’s contained in the default location reporting configuration.
An ‘authorized user’ who can apply a default or temporary reporting configuration, can hold administrative or operational roles within the user organization.

## Slide 5: Proposal II
If a temporary location configuration is applied to a user group with the use of Group ID:
  Any users with late affiliation to this group should also receive this temporary location configuration and should start reporting as per this configuration.
  Any users who de-affiliate from this group (before the location reporting trigger cancellation) should have this temporary reporting configuration cancelled and should revert to their default reporting configuration (if this had been applied).