## Slide 1: Exposure of User Sensitive Information
Walter Featherstone
Apple

## Slide 2: Outline
SA3 feedback resulting from SA6 LS
Authorization scope enhancement
Scope in SA3 and stage 3 and the alignment with SA6 spec
Summary including conclusion

## Slide 3: SA3 feedback: S3-244306
Reply LS to SA6 on obtaining user consent for the exposure of User Sensitive Information
Q1.Is capturing user consent for exposure of user sensitive information by a requesting entity (i.e., client) already supported within the existing security frameworks specified by SA3 or not, for example CAPIF RNAA? If not, would SA3 consider providing such mechanism in Rel-19?
SA3 Answer: SA3 interprets the “user consent” in the question as “authorization by the resource owner”, i.e. the permission given by the end user, subscriber or enterprise.
CAPIF RNAA Rel-18 allows the client application running on an external server (e.g. game server) to access the sensitive information from the resource server upon authorization by the resource owner. CAPIF RNAA Rel-18 also allows the client application running on the UE to access the sensitive information related to that UE upon authorization by the resource owner.
A new Rel-19 study is ongoing to enhance CAPIF mechanisms of resource owner authorization. SA3 will keep SA6 updated.

## Slide 4: Authorization scope enhancements
TR 23.700-22 Solution #9 and TR 33.700-22 Solution #29 on enhancing authorization through finer granularity access token
  Solution highlight that the specifics of the granularity are yet to be defined
TR 23.700-21 Solution #14 on signalling of user consent
  It is proposed in this solution that such a mechanism could be leveraged to not only request the scope of (server resource) access, but also the scope of what the client itself can expose whilst requesting such access.
  Note: Enhancing scope field is within SA3 scope.

## Slide 5: Access token profile, TS 33.122
Table C.2.2-1: Access token standard claims
Table C.2.2-1: Access token customized claims
Parameter | Description
exp | REQUIRED. The expiration time of the access token. Implementers MAY provide for some small leeway, usually no more than a few minutes, to account for clock skew (not to exceed 30 seconds).
client_id | REQUIRED. The identifier of the API Invoker making the API request as previously established with the CAPIF Core Function through onboarding.
scope | REQUIRED. A string containing a space-delimited list, comprising of the following as scopes associated with this token: - List of Services per AEF (e.g. “AEF1:Service1,Service2,Service3,...,ServiceX; AEF2:Service1,Service2,Service3,...,ServiceZ”)
Parameter | Description
resOwnerId | OPTIONAL. Resource owner ID.
The ‘exp’and ‘scope’ parameters of the access token shall be determined by the CAPIF core function based upon the client_id of the API Invoker provided in the Access Token Request message.
The scope parameter ‘List of Services per AEF’ shall contain a full or partial list of services which the API Invoker is permitted to access at each AEF.

## Slide 6: AccessTokenReq, TS 29.222
Table 8.4.2.6-1: Definition of type AccessTokenReq (subset of attributes)
Table C.2.2-1: Access token customized claims
Parameter | Description
resOwnerId | OPTIONAL. Resource owner ID.
The ‘exp’and ‘scope’ parameters of the access token shall be determined by the CAPIF core function based upon the client_id of the API Invoker provided in the Access Token Request message.
The scope parameter ‘List of Services per AEF’ shall contain a full or partial list of services which the API Invoker is permitted to access at each AEF.
Attribute name | Data type | P | Cardinality | Description | Applicability
client_id | string | M | 1 | This attribute shall contain the API invoker Identifier. (NOTE 3) | 
resOwnerId | ResOwnerId | O | 0..1 | Contains the identifier of the resource owner. This attribute shall be present only when the access token request is used for RNAA. | RNAA
scope | string | O | 0..1 | This attribute when present shall contain a list of AEF identifiers and its associated API names for which the access_token is authorized for use. It takes the format of 3gpp#aefId1:apiName1,apiName2,…apiNameX;aefId2:apiName1,apiName2,…apiNameY;…aefIdN:apiName1,apiName2,…apiNameZ Using delimiter "#" after the discriminator "3gpp", ":" after AEF identifier, "," between API names and ";" between the last API name of the previous AEF identifier and the next AEF identifier. (NOTE 2) Example: '3gpp#aef-jiangsu-nanjing:3gpp-monitoring-event,3gpp-as-session-with-qos;aef-zhejiang-hangzhou:3gpp-cp-parameter-provisioning,3gpp-pfd-management' | 

## Slide 7: Accessing service API, TS 23.222
8.11 API invoker obtaining authorization to access service API
  Step 1: The API invoker sends an obtain service API authorization request to the CAPIF core function for obtaining permission to access the service API by including the API invoker identity information and any information required for authentication of the API invoker. The request may include desired Network Slice Info of the service API.
8.31 API invoker obtaining authorization from resource owner
  Step 1: The API invoker requests to obtain resource owner authorization information to invoke the service API exposed by the API exposing function. The authorization function provides the authorization by interacting with the resource owner via the resource owner function.

## Slide 8: Service API invocation request, TS 23.222
Table 8.16.2.1-1: Service API invocation request
Consistent with the parameter of the access token, specifically API invoker identifier (OAuth 2.0 client-id) and Service API identification (OAuth 2.0 scope)
Information element | Status | Description
API invoker identity information | M | The information that determines the identity of the API invoker
Authorization information | O (see NOTE) | The authorization information obtained before initiating the service API invocation request
Network Slice Info | O (see NOTE) | The desired network slice information of the service API
Service API identification | M | The identification information of the service API for which invocation is requested. The service API identification is part of the specific service API invocation request.
NOTE: The inclusion of this information element depends on the chosen solution for authorization. |  | 

## Slide 9: Summary
Highlighted the use of OAuth “scope” to indicate services the API invoker wishes to access when requesting authorization
Highlighted relevant Release 19 solutions relevant to the requested scope when requesting authorization
Proposal to account for the potential exposure of user sensitive information by the API invoker when requesting authorization