## Slide 1: Way forward on testing of FR2 beam correspondence for initial access
Huawei, HiSilicon, Apple, Keysight, Qualcomm, Samsung
3GPP TSG-RAN5 Meeting #103
Fukuoka, Japan, 20 - 24 May 2024
R5-24xxxx

## Slide 2
1> How to activate/deactivate beam lock function in IDLE mode
Option a: Activation in RRC_CONNECTED mode, then UE send the activation complete message and memorize the activation status when it enters RRC_IDLE mode. Beam lock function has to be sent per DL link polarization and per measurement grid point.
  Option a-1: Deactivation sent in RRC_CONNECTED mode, then UE send the deactivation complete message.
  Option a-2: When UE couldn’t return to RRC_CONNECTED mode successfully, UE will automatically deactivate the beam lock function in FFS seconds since FFS time point.
  Option a-3: UE automatically deactivate beam lock function when it enters RRC_CONNECTED mode.
  Option a-4: Other method.
Option b: Activation in RRC_CONNECTED mode, UE memorizes the activation status when UE switches between RRC_CONNECTED mode and RRC_IDLE mode until:
i) deactivation command is received, or
ii) other agreed condition among Option b-1/b-2/b-3 is met.
Beam is only locked in RRC_IDLE mode, and will be automatically unlocked in RRC_CONNECTED mode. Beam lock function is sent only once
  Option b-1: Deactivation sent in RRC_CONNECTED mode, then UE send the deactivation complete message.
  Option b-2: When UE couldn’t return to RRC_CONNECTED mode successfully, UE will automatically deactivate the beam lock function in FFS seconds since FFS time point.
  Option b-3: Other method.
Way forward:
Continue discussion on all options. Method without test function is not precluded.

## Slide 3
2> Beam refinement process
Option a: TE sends paging as a trigger for UE beam refinement. UE needs to compare all the potential beams and decide the optimal one before the first preamble transmission. Beam is locked for future preamble transmissions.
Option b: UE could perform beam refinement between the preamble transmissions, i.e. the basic RAN1/RAN2 process
Way forward:
Option a.

## Slide 4
3> Beam refinement time needed
Option a: 3s as a starting point
Option b: Further optimize beam refinement time to <3s
Way forward:
Take option a as a starting point to evaluate the feasibility for preamble formats and preamble index, and the test time.

## Slide 5
4> Whether the beam lock function could be extended to UE’s power setting behavior
Option a: Extending the beam lock function to force UE to transmit at the Pcmax level.
Option b: Don’t use beam lock function to control UE’s power setting
Option b-1: With power ramping
Option b-2: Without power ramping
Way forward:
Continue discussion on all the options.