## Slide 1: Input questions for DualSteer NWM discussion
Nokia

## Slide 2: Question on Simultaneous transmission
Discussion
We have not yet settled the discussion on the term “DualSteer” and what does the SA1 text “DualSteer device with 2 UEs” mean from SA2 pov. The SID assumes no RAN impact, however for DualSteer device with 2 UEs there are potential impacts on RAN e.g.:
  If both the SUPIs of the DualSteer device are accessing the same frequency band (e.g. FR1) there may be a need for coordination in RAN for UpLink transmission power control in the UE.
  There is potential impact on RAN scheduler also to support simultaneous transmission, specifically e.g. if Dynamic Spectrum Sharing is used with one SUPI registered in LTE and the other in NR of the same RAN.
Supporting 2 types of DualSteer device (one with simultaneous transmission and 2nd without simultaneous transmission) comes with additional complexities in the design i.e. providing policies accordingly and enforcing the restriction from network side etc. Considering that we are already consuming TU from the normative phase for study it would be beneficial to focus on only one type of DualSteer device.
In Active/Standby mode of operation we do not need simultaneous transmission? All traffic will use active access and when active access is not available, they will be switched to the standby access. Even in the case of steering modes like smallest delay, the general expectation is that all traffic will be sent via the access with smallest delay always. As redundant steering mode and splitting are not in scope there is NO real scenario where simultaneous transmission of application traffic via both 3GPP access is required.
Question 1: Given the above can we move forward with below compromise conclusion?
“All application traffic from/to the DualSteer device is always sent/received via a single 3GPP access. When switching is applied, all application traffic of all the PDU Sessions of the DualSteer device are switched from the first 3GPP access to the second 3GPP access.”

## Slide 3: Steering and Switching policy
Discussion
The SA1 requirement is that for a particular service all traffic is transmitted via one 3GPP access which is essentially one UE/SUPI. That means for transmitting any application traffic detected by the DualSteer device, the DualSteer layer needs to first determine which UE/SUPI to use. So, the steering and switching rules needs to be provided at UE level e.g. as part of UE policy.
Question: Whether there is a need to provide steering and switching rules at flow level?
- If YES, what is that use case?
- If NO, can the steering and switching rules be provided at UE level e.g. as an enhancement to URSP or introducing a new UE policy for DualSteer

## Slide 4: Support for MPTCP and MPQUIC
Discussion
Since splitting is not required (i.e. traffic splitting and aggregation functionality is not needed) and also all traffic of an application is always sent via one UE/SUPI (i.e. redundant steering mode is not required) there is no need to use sophisticated application layer steering functionalities like MPTCP and MPQUIC.
Moreover, MPTCP and MPQUIC steering functionality cannot be used if DualSteer device does not support simultaneous transmission.
Question: Whether and why MPTCP and/or MPQUIC steering functionalities are needed?

## Slide 5: PDU Session management and switching
Discussion
There are two types of solutions proposed for switching, 1) in which the PDU Sessions are pre-established on both the 3GPP access, and when the UE decides to switch the traffic to the second access the UE only activates the PDU Session to start sending/receiving UL/DL PDUs on the second access and 2) the PDU Session on the second access is established after the switching decision is made by the UE.
With the solution type 2), it will require more time to establish the N3 tunnel when compared with the solution type 1) where the PDU Sessions are pre-established.
With solution type 2), there can be scenarios, where it may not be possible to select the same SMF that was handling the PDU Session on the first access (e.g. for various reason like overload etc). In such case this may lead to switching failure or additional delay in switching. With solution 1), this problem is eliminated as the 2 PDU Session are pre-established before the application traffic is routed i.e. before the switching decision was made.
Question: In order to provide best switching experience and avoid longer service interruption, can we agree to specify solution type 1) i.e. PDU Sessions are pre-established on both the 3GPP access and linked together as DualSteer PDU Sessions?

## Slide 6: How to identify the Active/Standby path
Discussion
For active/standby steering mode, the DualSteer layer of the DualSteer device needs identify the UE/SUPI for steering and switching decision. The UE/SUPI could be identified by e.g. having a unique identity for each UE/SUPI or assigning primary/secondary role to each SUPI. What benefits do we get by using access descriptor instead to identify the access? Each access belongs to different SUPI, so identifying the UE/SUPI to be used for steering and switching is sufficient.
Question: Which approach is more beneficial and what are those benefits over the other?  a) using Access Descriptor in the rules or b) uniquely identify each UE/SUPI in the rules