## Slide 1: Technical Questions for DualSteer New NWM Discussion
MediaTek Inc.

## Slide 2: 1.3 Session management aspects for DualSteer
ATSSS-like solutions
  UE establishes two PDU Sessions (i.e. AN resources for two PDU Sessions are set up)
  Receive dualsteer policy for duasteer traffic steering/switching
    Steering mode: active-standby, smallest RTT
  PDU Session not available = issues to AN resource of the PDU Session of the SUPI
  E.g., Active-standby switch
    Active = PDU Session of SUPI 1 (Standby = PDU Session of SUPI 2)
    Active = PDU Session of SUPI 2 (Standby = PDU Session of SUPI 1)
    Active = PDU Session of SUPI 1 (Standby = none) cannot be existed
    Active = PDU Session of SUPI 2 (Standby = none) cannot be existed
  E.g., Steer
    Only establish PDU Session of SUPI 1 (Active = PDU Session of SUPI 1 (Standby = none) )
    Only establish PDU Session of SUPI 2 (Active = PDU Session of SUPI 2 (Standby = none) )
    Establish two PDU Sessions of SUPI 1 and SUPI 2 if it supports switching
  E.g., Smallest RTT steer/switch
    SA2 does not have discussion on PMF function and on steering functionalities (e.g. MPQUIC/MPTCP proxy can be used to determine RTT)

## Slide 3: 1.3 Session management aspects for DualSteer
PDU Session handover-like solutions
  UE establishes one PDU Session
  Receive dualsteer policy for dualsteer traffic steering/switching
  (3GPP) AN resource not available (of the PDU Session) of the SUPI
  Similar to active-standby:
  E.g., steer/switch
    Active = PDU Session of SUPI 1 (Standby = PDU Session of SUPI 2) establish PDU Session of SUPI 1 (if available), if not available (SUPI 1), establish PDU Session of SUPI 2
    Active = PDU Session of SUPI 2 (Standby = PDU Session of SUPI 1)  establish PDU Session of SUPI 2 (if available), if not available (SUPI 1), establish PDU Session of SUPI 1
    Active = PDU Session of SUPI 1 (Standby = none)  Only establish PDU Session of SUPI 1
    Active = PDU Session of SUPI 2 (Standby = none) cannot be existed Only establish PDU Session of SUPI 2

## Slide 4: Summary
Switching policy is same/similar but the difference is whether the timing of establishing second PDU session by dualsteer device
  ATSSS-like establishes two PDU sessions before switching
  PDU Session handover like establishes when switching

## Slide 5: Questions for KI#1.3
1) Whether AN resource of two PDU Session is setup when established?
  Yes: the AN resources of two PDU Sessions are setup when established
  No: only one AN resource of two PDU Session is setup based on the steer/switch policy
2) For dualsteer traffic steering/switching conditions for the services/application not conflict, do services/applications transmitted on same DS PDU Session have same steer/switch conditions?
  Yes: Services/applications transmitted on same DS PDU Session shall have same steer/switch conditions
  No: no such restrictions
3) For 2), if No, are there any priorities among the services/applications (for non-simultaneous UE) on which PDU Session is selected for tranmission?
  Yes: the services/applications have different priorities provided by network
  No: (frequently switching between two PDU Sessions). No solutions address this issue

## Slide 6: Questions for KI#1.4
1) Does network provide dualsteer policy for steering before PDU Session establishment procedure?
  Yes: provide it before PDU Session establishment
  No: when and how the dualsteer device decides which SUPI(s) is used to establish PDU Session is not clear in current solutions of TR
2) Does network provide dualsteer policy for switching before PDU Session establishment procedure?
  Yes: provide it before PDU Session establishment at the same time as steering policy
  No: when and how the network is triggered to provide/update the switching policy is not clear in current solutions of TR
3) Does the dualsteer device evaluate URSP rules before deciding which SUPI is used to establish the PDU Session ?
  Yes: common URSP rules which is different from current per UE/SUPI URSP rules
  No: how to determine the URSP rules of which SUPI is firstly used for PDU Session establishment is not clear in current solutions of TR