## Slide 1: R19 Energysys-Solutions proposed in TR and in August meeting
China Mobile
2024 August

## Slide 2: Summary of solutions- General on calculations
Per UE EC= ECRAN,UE +∑ECupf,UE
EECF, CHF or OAM do the calculation.
Approach 1: data volume and NF EC information ECupf,ue=*ECupf， ECran,ue= *ECran
  ECupf , DVran, ECran are from OAM,
  DVupf, ue=DVran,ue are from UPF
  Approach 2:data volume, UPF EC information, and RAN reporting
  ECupf,ue=*ECupf, ECran,ue=RAN reporting
  ECupf is from OAM.
  DVupf, ueare from UPF
It is OAM providing the EC information with time stamp to show the reporting time.

## Slide 3: Summary of solutions- 5GC functionality-determined by SA2
New NF EECF
New NEF exposure services
EECF do the calculation.
Approach 1: data volume and NF EC information ECupf,ue=*Ecupf， ECran,ue= *ECran
  ECupf , DVran, ECran are from OAM, and the SMF ID is provided from UDM to EECF. RAN ID is provided from AMF to EECF.
  DVupf, ue=DVran,ue are from UPF(I-UPF and PSA UPF)
  Approach 2:data volume, UPF EC information, and RAN reporting
  ECupf,ue=*ECupf, ECran,ue=RAN reporting
  ECupf is from OAM, and the SMF ID is provided from UDM to EECF(SMF knows the UPF/I-UPF which supporting the UE). RAN ID is provided from AMF to EECF.
  DVupf, ueare from UPF(I-UPF and PSA UPF)
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
EECF
UE
NEF
UE
AF
UE
OAM
UE
UDM
UE
5GCNF
Architecture of 5GC supporting EnergySys

## Slide 4: Summary of solutions- OAM based solution-determined by SA5
Per UE EC= ECRAN,UE +∑ECupf,UE
OAM do the calculation.
Formula the same as the slide 2 approach 1, except the CHF provides the DVupf,UE=DVran,ue
SBMA to support per UE EC information exposure to NEF/5GC NF.
Observation:
One problem: CHF does not have I-UPF information. Therefore the OAM cannot generate the I-UPF EC of the UE.
Currently, the OAM manage object focus on NF or NS, not per UE.
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NEF
UE
AF
UE
CHF
UE
OAM
UE
5GCNF
How to calculate the I-UPF EC of UE is FFS

## Slide 5: Summary of solutions- CHF based solution
No new NF, enhancements to existing NFs
CHF to calculate the EC information per UE
  The CHF provides the DVupf,UE=DVran,ue
  OAM provides ECupf, ECran, DVupf, DVran
  SMF provides UPF IDs to CHF
  ULI reporting is used to provide RAN IDs
Significant OAM capacity needed to provide ECupf and ECran (approach 1) measurement/estimations to CHF
  Same for all solution in these slides
CHF is enhanced to support to UE EC exposure to NEF/NF.
Problem: CHF does not have I-UPF information. Therefore the CHF cannot generate the I-UPF EC of the UE.
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NEF
UE
AF
UE
CHF
UE
5GCNF
CHF expose the EC of UE to NEF/NF
UE
OAM

## Slide 6: Summary
Solution# | Per UE EC calculation | Evaluation
5GC New functionality | Approach 1 RAN, I-UPF, PSA-UPF Node level EC from OAM; RAN node level DV from OAM DVupf,ue=DVran,ue Approach 2 ECran,ue reporting from RAN | EC ran, EC-upf, DV-ran from OAM New NF Corresponding exposure service, Decided by SA2.
OAM | Formula the same as the Sol#1 approach 1, except the CHF provides the DVupf,UE=DVran,ue SBMA to support per UE EC information exposure to NEF/5GC NF. DV from CHF but without I-UPF related information | Specification enhancement in SA5 is needed to support the I-UPF EC information calculation. Currently, the OAM manage object focus on NF or NS, not per UE. Decided by SA5.
CHF | Formula the same as the Sol#1 approach 1, except the CHF provides the DVupf,UE=DVran,ue CHF needs to get the ECupf, ECran, DVupf, DVran from OAM DV from CHF but without I-UPF related information | Specification enhancement in SA5 to support the I-UPF EC information calculation New exposure service to support CHF information exposure Interface between CHF and OAM to support CHF getting the ECupf, ECran, DVupf, DVran from OAM Decided by SA5.

## Slide 7: SoH Questions
Q1: No new NF, enhancements to existing NFs
CHF to calculate the EC information per UE
  The CHF provides the DVupf,UE=DVran,ue
  OAM provides ECupf, ECran, DVupf, DVran
  SMF provides UPF IDs to CHF
  ULI reporting is used to provide RAN IDs
Significant OAM capacity needed to provide ECupf and ECran (approach 1) measurement/estimations to CHF
  Same for all solution in these slides
For roaming, the V-CHF may report the per UE EC of VPLMN to H-CHF by enhancing the existing roaming interface.
CHF is enhanced to support to UE EC exposure to NEF/NF.
Problem: CHF does not have I-UPF information. Therefore the CHF cannot generate the I-UPF EC of the UE.