## Slide 1: A (Possible) Alternative way forward for FS_Energy: NWDAF-based EC Estimation/Calculation
NTT DOCOMO

## Slide 2: DCM’s view on current situation
Two different directions
  OAM/CHF based solution by SA5
  New network function/functionality by SA2
It seems none of the directions is agreeable
  Some companies has strong concern on introducing new NF for energy
  Some companies raised concern on CHF-based solution
A (possible) alternative solution
  Do not introduce new NF, do not touch CHF, use as much as possible existing features
  NWDAF would be responsible for estimating EC in different granularities

## Slide 3: Architecture
Estimation/Calculation formulas are the same as other solutions
  Alternative formulas are FFS.
NWDAF collects
  NF/NS/gNB level EC information OAM
    Already supported, no further enhancement is needed
  Data volume information directly from UPF (via SMF)
    In different level of granularities (UE, PDU, QoS Flow)
NWDAF estimates/calculates EC in UE, PDU, QoS Flow levels
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NWDAF
UE
NEF
UE
AF
UE
OAM
UE
5GCNF

## Slide 4: Possible Advantages
No (significant) architectural impact
  No new function,
  No new interface between CHF & OAM
  No new interface/service between CHF and other NFs
NWDAF already collects a wide range of data from various entities
  Collecting data volume in different levels is supported / is feasible without significant changes
NWDAF already collects information from OAM
  Collecting the existing EC information from OAM is already supported
Other NFs (PDF/NEF/SMF/AMF) already gets analytics from NWDAF for control plane decision making
  Getting EC information from NWDAF is not a significant changes in other NFs
NWDAF already supports storing long-term data in ADRF
  EC information can also be stored in the same way, no need to introduce new capability

## Slide 5: Obvious Disadvantages
NWDAF supports statistics and predictions, but EC needs computing
  However, implementing the calculation formula seems much simpler than ML models for the predictions  hopefully not significant implementation effort
It is FFS whether the existing service operations can support EC estimation or new services are needed
Other (technical) disadvantage?!! Please comment

## Slide 6
Thank you.