## Slide 1: ATSSS_Ph Capability handling

## Slide 2: A. IP PDU Sessions Capabilities
Rel-18:
  MPTCP and MPQUIC-UDP support are bundled with support for ATSSS-LL with Active-Standby. The reason is to support non-MPTCP and non-MPQUIC traffic in the same MA PDU Session.
Options for rel-19:
  Alt A1: MPQUIC-IP is bundled with support for ATSSS-LL with Active-Standby
    This allows a mix of MPQUIC-IP and LL traffic on the same MA PDU Session
    It would also allow a fallback to ATSSS-LL Active-Standby in case there is a mismatch between UE and NW capabilities (e.g. UE only supports MPQUIC-UDP and NW supports only MPQUIC-IP)
  Alt A2: MPQUIC-IP is not bundled with ATSSS-LL with Active-Standby
    All traffic would use MPQUIC-IP
    If there is a mismatch between UE and NW capabilities, the PDU Session is rejected
  Alt A3: Both Alt 1 and Alt 2 is possible, i.e. UE and NW can support Alt 1 and/or Alt 2.

## Slide 3: B. Ethernet PDU Sessions Capabilities
Rel-18:
  ATSSS-LL with any Steering mode is mandatory, since it is the only supported Steering Functionality for Ethernet PDU Sessions
Options for rel-19:
  Alt B1: ATSSS-LL with any Steering mode is mandatory also in rel-19. UE and NW may optionally support MPQUIC-E in addition
  Alt B2: ATSSS-LL with any Steering mode is optional. MPQUIC-E is bundled with ATSSS-LL Active-Standby
    It would also allow a fallback to ATSSS-LL Active-Standby in case there is a mismatch between UE and NW capabilities (e.g. UE only supports MPQUIC-E + LL with Active-Standby, and NW supports only ATSSS-LL with any SM)
  Alt B3: ATSSS-LL with any Steering mode is optional. MPQUIC-E can be supported as only Steering Functionality
    If there is a mismatch between UE and NW capabilities, the PDU Session is rejected

## Slide 4: C. Ethernet PDU Sessions Usage in a MA PDU Session
Rel-18:
  Only ATSSS-LL used in a MA PDU Session
Options for rel-19 in case both ATSSS-LL and MPQUIC-E are supported by UE and NW:
  Alt C1: PCF ensures that either ATSSS-LL or MPQUIC-E is used in the MA PDU Session, i.e. all PCC rules indicates the same Steering Functionality
    In this case, SMF sends either Ethernet (if ATSSS-LL is used) or IP (if MPQUIC-E is used) as PDU Session Type to RAN
  Alt C2: It is possible to use both ATSSS-LL or MPQUIC-E is used in the MA PDU Session, i.e. PCC rules indicates either ATSSS-LL or MPQUIC-E
    In this case, SMF sends either Ethernet (if ATSSS-LL is used) or IP (if MPQUIC-E is used) or Unstructured (if bot ATSSS-LL and MPQUIC are used) as PDU Session Type to RAN
    In case of Unstructured, PCF/SMF needs to ensure that only a single QoS Flow is used