3GPP TSG-SA3 Meeting #116	S3-241803r1

Jeju, South Korea,  20th - 24th May 2024			merger of S3-241802, S3-242016, S3-242143, S3-242144

# Source:	Nokia

# Title:	pCR on conclusion for KI1 and KI3 with only Fast BSS

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

The discussion paper S3-241509 was endorsed in the last meeting. As per the discussion paper:

- A fast BSS based solution will be concluded in the May meeting for IEEE 802.11. Other solutions are up for further discussion.

Therefore, proposing the FBB based conclusion for the KI1 and KI3

# 4	Detailed proposal

**** START OF CHANGE ****

# 7	Conclusions

Editor’s Note: This clause contains the agreed conclusions that will form the basis for any normative work.

## 7.x	Key issue #1: Security aspect of UE connecting to a new TNAP within the same TNGF

It is concluded to use a fast BSS transition-based solution 3 as a base for the normative work. The R0KH holder may be collocated with TNGF or may be a separate entity.

Editor’s Note: Conclusion on other non-3GPP trusted access technologies is FFS.

## 7.y	Key issue #3: Security aspect of N5CW device connecting to a new TWAP within the same TWIF

It is concluded to use a fast BSS transition-based solution 7 as a base for the normative work. The R0KH holder may be collocated with TWIF or may be a separate entity.

Editor’s Note: Conclusion on other non-3GPP trusted access technologies is FFS.

**** END OF CHANGE ****