3GPP TSG-SA3 Meeting #116	draft_S3-242529_r1

Jeju, Korea, 20th -24th May 2024                               revision of S3-242071

# Source:	China Telecom

# Title:	New Solution on Security of multi-hop UE-to-UE Relay Communication

# Document for:	Approval

Agenda Item:	5.12

# 1	Decision/action requested

This contribution proposes to add new Solution on Security of multi-hop UE-to-UE Relay Communication.

# 2	References

[1]	3GPP TR 23.700-03: " Study on system enhancement for Proximity based Services (ProSe) in the 5G System (5GS); Phase 3".

# 3	Rationale

The contribution proposes to add new Solution on security of multi-hop UE-to-UE relay communication without network assistance.

# 4	Detailed proposal

It is suggested to approve the following change.

*************** Start of the change ****************

## 6.Y	Solution #Y: Solution of multi-hop UE-to-UE Relay Communication

### 6.Y.1	Introduction

This solution addresses key issue #2.

For the use of multi-hop UE-to-UE relays, multi-hop UE-to-UE relays can be within or outside the 3GPP coverage range. When the multi-hop UE-to-UE relay is without 3GPP coverage, this solution provides a mechanism for the PC5 security setting process between the Source End UE or the Target End UE and the multi-hop UE-to-UE Relay.

### 6.Y.2	Solution details

The security procedure in clause 6.2 is used to establish a secure PC5 link between the End UE and the 5G ProSe Layer-3 multi-hop UE-to-UE Relay and between multiple 5G ProSe Layer-3 multi-hop UE-to-UE Relays without network assistance with the following modifications.

-	The RSC is included in the DCR message.

-	The DCR message is protected based on the security mechanism defined in clause 6.3.5 with a modification that the length of the UP-PRUK ID/CP-PRUK ID is set to zero in clause 6.3.5.2.

### 6.Y.3	Evaluation

TBD

*************** End of the change ****************