# 3GPP TSG-SA3 Meeting #116	draft_S3-242585-r2

# Jeju, South Korea,  20th - 24th May 2024	revision of S3-242086

# Source:	vivo, InterDigital, China Mobile, Huawei, HilSIlicon, OPPO

# Title:	New key issue on security of VFL training

Document for:	Approval

Agenda Item:	5.13

# 1	Decision/action requested

Approve the pCR on new key issue on security of VFL training.

# 2	References

# 3		Rationale

This contribution proposes a new key issue on security of VFL training. This contribution is the same with latest r3 version of SA3#115Adhoc-e meeting.

# 4	Detailed proposals

Start of Change

## 5.X	Key issue #X: Security of communication data used in VFL training process

### 5.X.1	Key issue details

Vertical federated learning (VFL) allows the cooperation of multiple NWDAF(s) and/or AF(s) to cooperate to train models locally where no raw data need to be exchanged.

After the selection of VFL clients and the completion of data and feature alignment procedures, the VFL training will commence between the VFL clients and VFL server. During this process, the VFL clients and VFL server will exchange intermediate results such as activations and gradients. Following the training, distinct local models will be present on both the VFL server and VFL clients, with the global model on the VFL server serving as the final output of the training process.

### 5.X.2	Security threats

Editor’s Note:	The details of security threat need to be added.

### 5.X.3	Potential security requirements

TBA.

End of Change