3GPP TSG-SA5 Meeting #155 	S5-243040

Jeju, South Korea, 27 - 31 May 2024

# Source:	Nokia, Huawei, Ericsson

# Title:	Rel-19 DP CAPIF Charging Topics

# Document for:	Discussion

Agenda Item:	7.5.2

# 1	Decision/action requested

This discussion paper provides a view on the topics to be covered in the CAPIF Charging Study.

# 2	References

[1]	3GPP TS 23.222: "Common API Framework for 3GPP Northbound APIs"

# 3	Rationale

The following topics are seen as relevant to study, in order to assess, the Charging architecture taking in account the existing Charging requirements from 3GPP TS 23.222 [1]. Therefore, clause B.2 of 3GPP TS 23.222 [1] details CAPIF architecture and its relation with 3GPP 5GS Network Exposure (NEF). The following table summarizes the current CAPIF deployment models which will be pursue to support the topics proposed.

| Aspects | CAPIF | 5GS network exposure |
| --- | --- | --- |
| Entity providing the APIs to external or 3rd partyapplications | AEF | NEF |
| Entity providing framework related services to the applications (discovery, authentication, authorization, etc) | CAPIF core function | NEF (Not specified yet) |
| Entity representing the external or 3rd party applications | API invoker | AF |
| Entity providing framework related services to support the APIs operation and management (publish, policy enforcements, charging) | CAPIF core function | NEF (Not specified yet) |
| Interface/Reference point for exposing network capabilities as APIs | CAPIF-2 and CAPIF-2e (Do not include the service specific aspects) | Nnef |
| Interface/Reference point for exposing framework services as APIs to the applications | CAPIF-1 and CAPIF-1e | Nnef (Not specified yet) |
| Interface/Reference point for framework services to support the APIs operation and management | CAPIF-3, CAPIF-4 and CAPIF-5 | Internal to NEF |

Table 1 : CAPIF relationship with 3GPP 5GS network exposure (Table B.2.1-1 of 3GPP TS 23.222)

Clause C.1. of TS23.222 provides a view on the CAPIF role in charging, but its quite high level and it’s not covering Converged Charging and its charging scenarios (PEC, IEC, SCUR, ECUR).

Figure 1 - CAPIF Role in Charging (Figure C.1-1 of TS 23.222 [1])

NOTE: Table 1 and Figure 1 are informative in 3GPP TS 23.222 [1]

# 4	Proposal

Please add the following topics to the new CAPIF Charging TR.

First change

# X	CAPIF Charging Scenarios and Key Issues

## x.y	Topic #1: CAPIF Converged Charging support of Service APIs Operation and Management

### x.y.z	General description and assumptions

Informative Annex B.2.2 of 3GPP TS 23.222 [x] describe on how the NEF can implement the specific service aspect and how its aligned with the CAPIF Architecture. Therefore, it would be necessary to evaluate the possibility to support Converged charging in those deployment models.

### x.y.z	Potential charging requirements

### x.y.z	Key Issues

### x.y.z	Possible Solutions

### x.y.z	Evaluation

### x.y.z	Conclusion

## x1.y1	Topic #2:	CAPIF Converged Charging of multiple API Providers

### x1.y1.z1	General description and assumptions

Informative Annex B.3.2 of 3GPP TS 23.222 [x] describe on how the NEF (and SCEF) can implement the specific service aspect and how its aligned with the CAPIF Architecture. Therefore, it would be necessary to evaluate the possibility to support Converged charging in those deployment models.

### x1.y1.z1	Potential charging requirements

### x1.y1.z1	Key Issues

### x1.y1.z1	Possible Solutions

### x1.y1.z1	Evaluation

### x1.y1.z1	Conclusion

End of changes