3GPP TSG-SA5 Meeting #155 	S5-242668

Jeju, South Korea, 27 - 31 May 2024

# Source:	Nokia

# Title:	Rel-19 pCR Usecase, requirement and solution for extension for cell energy saving analytics

# Document for:	Approval

Agenda Item:	6.19.2

# 1	Decision/action requested

In this box give a very clear / short /concise statement of what is wanted.

# 2	References

# 3	Rationale

This pCR to propose usecase, requirement and solution for extension for cell energy saving analytics.

# 4	Detailed proposal

Start of first change

### 5.1.N	Use case 2: Extension of Cell Energy Saving analytics

#### 5.1.N.1	Description

Energy efficiency can be achieved by moving certain cells to energy saving state (see TS 28.104). When moved to energy efficiency state, the different such cells or beams will have different impacts to the neighbour cells depending on how much the coverage of those cells overlap

RAN3 has a use case to configure unified mapping rule for a group of cells. This implies that a mapping rule related to EE are same across a group of cells for a given area. It is desirable to use MDA analytics to get a group of cells that should be managed together for energy saving, computed, or learned depending on their proximity and likely impact on one another. Then, for the cells in the group, it is desirable to use MDA analytics to get the sequence in which the beams can be switched off/on in order to maximize the throughput of the users while minimizing the energy consumption. Note that the sequence in which the beams are switched off and switched on are necessarily not in the same sequence.

The sequence of switching the beams on/off matter in real time scenarios. For instance, there are 4 beams in a cell serving the same geo area at different directions. If it has been decided to switch two beams off for energy saving purposes, the order in which the beams are switched off is important. \

The enabling data of this use case may include Mobility Management related measurements (clause 5.1.1.6 from TS 28.552) including intra and inter gNB handovers. These also include handover measurements per beam (in clauses 5.1.1.6.1.12 and 5.1.1.6.1.13 from TS 28.552) and intra-NR cell SSB beam switch measurements (in clause 5.1.1.21 from TS 28.552).

Editor’s note 1: The realization of the beam aspects of this use case depends on the definition of beam specific energy saving mechanism.

Editor’s note 2: The realization of the grouping discussed in this use case depends on the agreement in Energy Saving study.

Editor’s note 3:

In RAN3 LS R3-240998, as a response to Q3, RAN3 has explained the need for configuring a unified mapping rule among gNBs. These set of gNBs to which unified mapping rule to be applied form a group of cells that need to be managed together for energy efficiency purposes. The figure from the LS is attached below for reference.

Figure 1 Example of Energy Cost exchange between gNBs.

#### 5.1.N.2	Potential requirements

REQ-TLM-FUN-01: MDA capability for energy saving analysis shall include providing, for a given area, the recommended grouping of cells that should be managed together for energy saving.

REQ-TLM-FUN-02: MDA capability for energy saving analysis shall include providing the recommended sequence in which the beams are switched off/on in order to maximize the throughput of the users while minimizing the energy consumption.

End of changes