# 3GPP TSG SA WG5 Meeting #155	S5-242903                 	           S5-241202

# Jeju, Korea (Republic Of), 27th May 2024 - 31st May 2024

# Source:	Ericsson

# Title:	pCR TR 28.914 Add use case, requirement and solution for IDMS utility function support

# Document for:	Approval

Agenda Item:	6.19.3

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP TS 28.312: "Management and orchestration; Intent driven management services for mobile networks"

[2]	TMF TR291I “Utility Extension Model”, v3.5.0 DRAFT

[3]	SP-231737 "Study on intent driven management services for mobile network phase 3"

[4]	TMF TR292H “Mathematical Functional Ontology”, v3.4.0

[5]	TMF TR292C “Function Definition Ontology”, v3.4.0

# 3	Rationale

Intent Driven Management Service (IDMS) consumers use intents to express their requirements, goals and constraints for a specific service or network management workflow. Intents may provide additional information such as performance objectives which can be used by the IDMS producer to evaluate and report on the level of intent fulfilment.

Fulfilment evaluation is defined as requirements (e.g. targets based on quantifiable network data such as ULLatency, DLLatency, NumberofUEs) defined by the consumer against which the producer reports the achieved fulfilment levels.  This target definition is sufficient for simple intents and systems where IDMS producers have sufficient resources to fulfill all requirements.  However, in cases where decisions may need to be made to prioritize resources it is important for the IDMS producer(s) to understand the consumers view of the relative importance (the “business value”) of their requirements.  Such information needs to be expressed within the intent itself and an IDMS solution needs a method to quantify business value to enable such decision-making.

This proposal introduces such information based on “utility functions” within intents.  This allows intent consumers to supplement their requirements with information regarding the relative business value of potential outcomes.  For individual consumers this provides a method to express the relative importance of their intent requirements.  For intent producer(s) this provides additional information to assess potential outcomes as in some cases, the relative business value may be the differentiating factor defining acceptability from consumer(s) perspective.

Intent utility functions are mathematical expressions that quantify the satisfaction or utility derived from the degree of fulfilling various network intents.  The basic components of which include:

- Variables:  to quantify specific aspects of the fulfilment, e.g. network performance

- Weights: to define the relative importance of each variable, e.g. for network performance a variable representing low latency might be assigned higher weight than throughput

- Function:  the mathematical functions to be applied to the variables, e.g. linear, logarithmic, polynomial applied to the variables

- Result:  the output of the function.  The value of which represents the utility level achieved, i.e. the satisfaction of the current fulfilment based on consumer’s definition of acceptability

A simplified example of a network performance “Latency Utility Function” (i.e. a method to quantify the intent with higher business value relative to latency) could be:

U(A) = w1⋅A + w2⋅B − w3⋅C

Where:

- U(A) is the utility function

- throughput, latency, and packet loss are variables representing different aspects of network performance

- w1, w2, and w3 are weights assigned to B, C, and D

- functions used to produce a value representative of A

- with this function the value increases as the latency decreases, providing a means “to quantify the intent’s relative business value is higher when the latency is lower”

The current document proposes the addition of Intent Utility Function support to solution defined in [1].

Utility functions may be defined by the consumer and provided as part of the intent itself, i.e. the function is defined as part of the intent.  A consumer may also specify that an existing (i.e. predefined) utility function be used.  Predefined utility functions may be vendor specified and/or specified by consumer.

It is important that a consistent method for consumers and producers to add utility information be defined.  Taking work done in other SDOs into consideration helps to ensure consistency and interoperability, in particular in multiple domain deployments.  As such, inputs from work in TM Forum on intent utility extension modeling [2] are considered.

This contribution is related to WT-4.

# 4	Detailed proposal

1st Change

## 5.X Use case#X: Utility function support

## 5.X.1 Description

Intent Utility Function defines a method by which consumers can express the relative business value to assist the IDMS producer(s) in fulfilling their intents in the most acceptable manner.

Intent producer(s) can use such utility information to assess the acceptability of potential outcomes, in addition to information such as resource availability and performance targets.

### 5.X.2 Potential requirements

REQ-Intent_UTI-1: The intent driven MnS producer should have the capability to advertise its support for utility function.

REQ-Intent_UTI-2: The intent model should have the capability to allow an MnS consumer to express the relative business value of its requirements, defined as utility function(s), within an intent.

REQ-Intent_UTI-3: The intent driven MnS producer should have the capability to support assessment of potential outcomes with consideration for utility function(s) contained within an intent.

REQ-Intent_UTI-4: The intent driven MnS producer should have the capability to report potential outcomes including consideration of utility function(s) contained within an intent.

REQ-Intent_UTI-5: The intent driven MnS producer should allow a consumer to specify a utility function to be used as part of the intent, i.e. by defining the function as part of the intent.

REQ-Intent_UTI-6: The intent driven MnS producer should allow a consumer to indicate an existing utility function be used, i.e. by id/reference.

### 5.X.3 Potential solutions

A key consideration for potential solutions is the extent to which utility functions must be modelled in the solution to support the above requirements.  The flexibility in defining the utility function(s) themselves, the granularity of applying them to different parts of the intent model, and the level of reporting required all affect the potential solutions.

#### 5.1.3.1 Potential solution #1

This solution proposes support for utility function(s) be added in a relatively simple manner.  This is via new attributes added to the intent common model to express intent utility and report the impact of utility on intent fulfilment.

The goal of this solution is simple implementation and vendor flexibility.  The new attributes are defined simply as strings and are left to vendor-definition.

A new attribute utilityFunction is added to allow consumers to express relative business value within intents.

Utility functions can be defined at various levels within the intent:

- For the entire intent or a set of expectations in the intent based on criteria.  The Intent IOC is updated to support such utility functions.

- For a specific expectation, the IntentExpectation datatype is updated to support such utility functions.

A method to report the impact of utility function(s) on the fulfilment is required.  The ExpectationFulfillmentResult is updated to allowing reporting of the evaluation of the utility function(s).

Potential updates to [1] are show below, using clause numbers and headers from it.  Modified text is shown in bold:

##### 6.2.1.2	Class definition

###### 6.2.1.2.1	Intent <<InformationObjectClass>>

###### 6.2.1.2.1.1	Definition

This IOC represents the properties of an Intent driven management information between MnS consumer and MnS producer.

The Intent IOC contains one or multiple IntentExpectation(s) which includes MnS consumer's requirements, goals and contexts given to a 3GPP system.

The Intent IOC also contains intentAdminState to support intent lifecycle management. In case MnS consumer wants to suspend an intent, MnS consumer can request MnS producer to configure attribute intentAdminState with the value "DEACTIVATED". A suspended intent means this intent is not considered for fulfillment. In case MnS consumer wants to resume an intent on the MnS producer side when the intent is suspended, MnS consumer can request MnS producer to configure attribute intentAdminState with the value "ACTIVATED".

The attribute "observationPeriod" indicates the time period for which the fulfilment process is observed and at the end of which the fulfilmentInfo for corresponding ExpectationTargets, IntentExpectations and Intent is updated. The observation period can be set by the MnS consumer or by the MnS producer if the MnS consumer does not provide a value.

The Intent IOC includes the attribute objectClass and objectInstance from the TOP IOC. The value of attribute objectClass is "Intent" and the value of attribute objectInstance is the DN of the instance of Intent IOC.

The Intent IOC includes contextSelectivity respectively used to define how to select among the stated intentContexts

The utilityFunction is used to specify a utility function for the Intent.

The utilityFunctionRef is used to reference a utility function for the Intent, which is specified elsewhere.

###### 6.2.1.2.1.2	Attributes

The Intent IOC includes attributes inherited from Top IOC (defined in 3GPP TS 28.622 [6]) and the following attributes.

Table 6.2.1.2.1.2-1

| Attribute Name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| intentExpectations | M | T | T | F | F |
| userLabel | M | T | T | F | F |
| contextSelectivity | O | T | T | F | F |
| intentContexts | O | T | T | F | F |
| observationPeriod | O | T | T | F | F |
| intentPriority | O | T | T | F | T |
| intentAdminState | CM | T | T | F | F |
| intentPreemptionCapability | CM | T | T | F | F |
| utilityFunction | CM | T | T | F | F |
| utlityFunctionRef | CM | T | T | F | F |
| Attribute related roles |
| intentReportReference | M | T | F | F | F |

###### 6.2.1.2.1.3	Attribute constraints

| Name | Definition |
| --- | --- |
| intentAdminState Support Qualifier | Condition: MnS consumer-suspension mechanism is supported. |
| intentPreemptionCapability Support Qualifier | Condition: The preemption mechanism is supported. |
| utilityFunction | Condition: Intent utility function definition capability is supported. |
| utilityFunctionRef | Condition: Intent utility function reference capability is supported. |

###### 6.2.1.2.1.4	Notifications

The common notifications defined in clause 6.2.1.5 are valid for this IOC. In addition, the following set of notifications is also valid.

| Name | S | Notes |
| --- | --- | --- |
| notifyMOIChanges | M | -- |

##### 6.2.1.3	 DataType definition

###### 6.2.1.3.1	IntentExpectation <<dataType>>

6.2.1.3.1.1	Definition

IntentExpectation <<dataType>>represents MnS consumer's requirements, goals and contexts given to a 3GPP system.

The IntentExpectation <<dataType>> includes contextSelectivity used to define how to select among the stated expectationContexts.

The IntentExpectation <<dataType>> includes utilityFunction used to optionally define the business value of the stated expectationTargets.

6.2.1.3.1.2	Attributes

The IntentExpectation includes the following attributes.

Table 6.2.1.3.1.2-1

| Attribute Name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| expectationId | M | T | T | T | T |
| expectationVerb | O | T | T | T | F |
| expectationObject | M | T | T | F | F |
| expectationTargets | M | T | T | F | F |
| contextSelectivity | O | T | T | F | F |
| utilityFunction | O | T | T | F | F |
| expectationContexts | O | T | T | F | F |
| NOTE: The scenariospecific IntentExpectations in clause 6.2.2 are defined utilizing the constructs of this generic IntentExpectation <<dataType>>. |

6.2.1.3.1.3	Attribute constraints

None.

6.2.1.3.7	 ExpectationFulfilmentResult <<dataType>>

6.2.1.3.7.1	 Definition

ExpectationFulfilmentResult <<dataType>> includes the expectationFulfilmentInfo and targetFulfilmentResults for each IntentExpectation.

The expectationFulfilmentInfo describes status of fulfilment of an intentExpectation and the related reasons for the infeasible status.

The utilityFunctionResult describes the impact of the utility function on the fulfilment.

6.2.1.3.7.2	Attributes

The ExpectationFulfilmentResult includes the following attributes.

Table 6.2.1.3.7.2-1

| Attribute Name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| expectationId | M | T | F | T | T |
| expectationFulfilmentInfo | M | T | F | F | T |
| targetFulfilmentResults | O | T | F | F | T |
| utilityFunctionResult | O | T | T | F | F |

6.2.1.3.7.3	 Attribute constraints

None.

##### 6.2.1.4	Attribute definition

Table 6.2.1.4-1

| Attribute Name | Documentation and Allowed Values | Properties |
| --- | --- | --- |
| utilityFunction | Logical expression of a utility function. The syntax and capabilities of utilityFunction are vendor specified. An empty string is not allowed. allowedValues: N/A | type: String multiplicity: 0..1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |
| utilityFunctionResult | The result of the evaluation of a utility function. The syntax and values are vendor specified. allowedValues: Not Applicable | type: String multiplicity: 0..1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |

#### 5.1.3.1 Potential solution #2

The proposal is similar to solution #1 but enhances the definition of the attribute utilityFunction by defining the semantics by which the consumer can express their utility function towards intent producers.

The goals with this approach are to better support multi-vendor interoperability and interaction with intent handling functions in other non-3gpp management domains.

##### 6.2.1.3.x	UtilityFunction <<dataType>>

6.2.1.3.x.1	Definition

The UtilityFunction <<dataType>> represents a utility function.

This representation includes attributes to support a utility function, result, and/or error information.  The function is a series of arguments and operations defined as ordered lists.

An optional attribute functionDefinition is also included to support vendor defined formats.

Editor’s Note:  For this solution the detailed definitions of the arguments, operations, and functions will need to be defined to ensure the required functions can be properly expressed.  Other formats, e.g. key-value pairs <argument, operand> and support for parenthesis, may be required.

6.2.1.3.x.2	Attributes

UtilityFunction includes the following attributes:

Table 6.2.1.3.4.2-1

| Attribute Name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| argumentName | O | T | T | F | F |
| argumentType | O | T | T | F | F |
| argumentWeight | O | T | T | F | F |
| operation | O | T | T | F | F |
| function | O | T | F | F | F |
| result | O | T | F | F | F |
| error | O | T | F | F | F |
| functionDefinition | O | T | T | F | F |

6.2.1.3.x.3	Attribute constraints

None.

##### 6.2.1.4 	Attribute definition

Table 6.2.1.4-1

| Attribute Name | Documentation and Allowed Values | Properties |
| --- | --- | --- |
| utilityFunction | Logical expression of a utility function. allowedValues: N/A | type: UtilityFunction multiplicity: 0..1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |
| argumentName | An ordered list which contains one entry per argument. allowedValues: a defined expectationName.targetName in the intent Editor’s Note: This definition likely has a dependency on the note in [1], clause 6.2.2.1.3.3 as measurements/KPI will need to be referenced in the functions. | type: String multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| argumentType | An ordered list which contains one entry per associated argumentName. allowedValues: objectType of the argumentName | type: String multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| argumentWeight | Relative weight of the associated argument. Default value is 1. allowedValues: value between 0 and 1. | type: Real multiplicity: 1 isOrdered: True isUnique: N/A defaultValue: 1 isNullable: False |
| operation | An ordered list which contains the function operations. allowedValues: PLUS, MINUS, MULTIPLY_BY, DIVIDE_BY, LOG, MIN, MAX, MEAN | type: Enum multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| function | The mathematical function. Comprises the combination of the list of arguments (* by their weight) and list of operations defined for the utility function. | type: String multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| result | Relative weight of the associated argument. Default value is 1. allowedValues: N/A | type: Real multiplicity: 0..1 isOrdered: False isUnique: N/A defaultValue: 1 isNullable: False |
| error | Error string. allowedValues: N/A | type: String multiplicity: 0..1 isOrdered: False isUnique: N/A defaultValue: None isNullable: False |
| functionDefinition | String representation of a utility function. The syntax and evaluation of the string are vendor defined. An empty string is not allowed. allowedValues: N/A | type: String multiplicity: 0..1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |

#### 1.3.1 Potential solution #3

On the assumption being that Intent Handlers, including an SA5 IDMS Producer, are likely participating in a multi-domain deployment and would benefit from a consistent format for expressing utility functions.  For example, TMF defined intents available in the deployment defined in [1], F.3 “Management interactions for Intent-CSC between CSC and CSP” would define utility function in RDF.

This proposed solution emphasizes close alignment with the functional ontology defined by TMF in [4].

This could be achieved by modifying potential solution #2 to align with functional definitions in [4], clause 11.  Some attributes (e.g. arityMin, artiyMax) are excluded as those are not required.

In addition to the attributes defining the function, the attribute sourceDefinition maintains the original input in its native format.

##### 6.2.1.3.x	UtilityFunction <<dataType>>

6.2.1.3.x.1	Definition

The UtilityFunction <<dataType>> represents a utility function.

This representation includes attributes to support a utility function, result, and/or error information.  The attribute nativeRepresentation provides the utility function in its native format.

Editor’s Note:  this approach could be further defined to support additional functions such as those defined in [4] and [5].   The mapping of expectations and targets current defined in [1], Annex C may also require update to better align with latest TMF spec versions and to ensure it is sufficient for the argument/property mappings.

6.2.1.3.x.2	Attributes

UtilityFunction includes the following attributes:

Table 6.2.1.3.4.2-1

| Attribute Name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| argumentNames | O | T | T | F | F |
| argumentTypes | O | T | T | F | F |
| error | O | T | F | F | F |
| operation | O | T | F | F | F |
| function | O | T | F | F | F |
| result | O | T | F | F | F |
| resultType | O | T | F | F | F |
| nativeRepresentation | M | T | T | F | F |
| nativeFormat | M | T | T | F | F |

6.2.1.3.x.3	Attribute constraints

None.

##### 6.2.1.4 	Attribute definition

Table 6.2.1.4-1

| Attribute Name | Documentation and Allowed Values | Properties |
| --- | --- | --- |
| utilityFunction | Logical expression of a utility function. allowedValues: N/A | type: UtilityFunction multiplicity: 0..* isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |
| argumentNames | An ordered list which contains the function arguments. allowedValues: a defined expectationName.targetName in the intent Editor’s Note: This definition likely has a dependency on the note in [1], clause 6.2.2.1.3.3 as measurements/KPI will need to be referenced in the functions. | type: String multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| argumentTypes | An ordered list which contains one entry per associated argumentName. allowedValues: objectType of the argumentName | type: String multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| operation | An ordered list which contains the function operations. allowedValues: PLUS, MINUS, MULTIPLY_BY, DIVIDE_BY, LOG, MIN, MAX, MEAN | type: Enum multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| function | The mathematical function. Comprises the combination of the list of arguments (* by their weight) and list of operations defined for the utility function. | type: String multiplicity: 1..* isOrdered: True isUnique: N/A defaultValue: None isNullable: False |
| result | Result of the function evaluation. allowedValues: N/A | type: Real multiplicity: 0..1 isOrdered: False isUnique: N/A defaultValue: N/A isNullable: False |
| resultType | Type of the result. allowedValues: <Whether this attribute is needed, and what values it would allow depends on which functions are supported> | type: Enum multiplicity: 0..1 isOrdered: False isUnique: N/A defaultValue: N/A isNullable: False |
| error | Error string. allowedValues: N/A | type: String multiplicity: 0..1 isOrdered: False isUnique: N/A defaultValue: None isNullable: False |
| nativeRepresentation | String representation of a utility function in its native format. An empty string is not allowed. allowedValues: N/A | type: String multiplicity: 0..1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |
| nativeFormt | The format of the natively defined utility function. An empty string is not allowed. allowedValues: N/A | type: String multiplicity: 0..1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |

### 5.X.4 Evaluation of potential solutions

TBD

End of changes

# Comments

Performance objectives of the´ network? Are these not part of the targets in the intent?

Why business value? How do we know it is business value?

One could argue that this is internal consumer’s information. Why should the consumer share it with the producer?

It may be the case that the consumer only shares such data if needed, i.e. when the producer is completely unable to support the consumer’s intent. So it should be allowed that the producer indicates this complete inability to support the intent. And it should still be the case that the consumer may chose not to share that information.

MnS consumer?

The consumer may also instead provide information on their evaluation (their satisfaction level) of what has been achieved by the producer instead of divulging their internal information.

MnS producers?

Mhh? What are these?

Is there supposed to be some sort of dimensions matching?

Where do these appear in the function above?

Not in equation above!

What does this mean?

Strings are not useful at all. They are as good as having nothing

Is it allowed to use a ref for an object that is a  not IOC? i.e. ref toa string?

This structure does not show the relation between  arguments and their weights. Isn’t it better to have a datatype for an argument which then is a child element of utility function?