3GPP TSG-SA5 Meeting #155 	S5-242962

Jeju, South Korea, 27 May - 31 May 2024

# Source:	Ericsson

# Title:	pCR TR 28.875 PDU session based solution to support IAB node connectivity to OAM system

# Document for:	Approval

Agenda Item:	6.19.16

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP TR 28.875 v0.1.0 Study on management of IAB nodes

# 3	Rationale

This contribution adds new solution to TR 28.875 [1] about PDU session based solution to support IAB node connectivity to OAM system.

# 4	Detailed proposal

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[x]	3GPP TS 28.315: “Management and orchestration; Plug and Connect; Procedure flows”.

[y]	3GPP TS 23.501: “System architecture for the 5G System (5GS)”.

…

2nd Change

# 6	Potential solutions

### 6.x	Potential solutions #x PDU session based solution to support IAB node connectivity to OAM system.

According to TS 28.315 [x], the initial IP configuration for OAM connectivity includes basic IP configuration information (e.g., IP address, netmask, default gateway, domain name, IP address(es) of DNS servers, time servers) or together with information such as IP address or FQDN of CA/RA server, IP address or FQDN of SeGW, IP address or FQDN of SCS, etc.

IAB node can get the initial IP configuration via PDU session that setup between IAB-MT and 5GC, using this connectivity IAB node can obtain the initial IP configuration provided by IP autoconfiguration service (e.g., DHCP server), and additionally may perform DNS query depends on the operator’s deployment scenario.

With initial IP configuration obtained as above, IAB node can proceed Plug and Connect procedures to connect to OAM system.

End of change