3GPP TSG-SA5 Meeting #155 	S5-243082

Jeju, South Korea, 27 - 31 May 2024

# Source:	Nokia

# Title:	Rel-19 pCR Usecase, requirement and solution for Handover and service data correlation analytics

# Document for:	Approval

Agenda Item:	6.19.2

# 1	Decision/action requested

In this box give a very clear / short /concise statement of what is wanted.

# 2	References

# 3	Rationale

This pCR to propose Usecase, requirement and solution for Handover and service data correlation analytics.

# 4	Detailed proposal

Start of first change

### 5.3.K	Use case K:	Handover and service data correlation analytics

#### 5.3.K.1	Description

Handover performance may be affected by multiple aspects including:

- Signal measurements, either as measured in the network or as predicted.

- User speeds which may be measured or predicted.

- User paths or trajectories, by predicting the likely destination based on the user current path and learning from previous user trajectories.

- Service characteristics, such as QoE

These may be combined in different forma to either derive the optimal handover settings or to also determine the related service configurations. It is desired that the MDA supports analytics that enables the consumer to request analytics on real or predicted signal measurements, on real or predicted user speeds, on learned and predicted user trajectories or paths, on user service characteristics or any combination of these aspects.

Figure 5.3.K.1-1: Examples of various context information and HO performance metrics can be used for handover optimization through different combinations A1 to A5.

#### 5.3.K.2	Potential requirements

REQ-MDA-CORR-1:	The MDA producer for handover and service data correlation analytics should have a capability of allowing the use the predicted signal measurements, predicted user speeds and predicted user trajectories for providing recommendations for Handover analytics.

REQ-MDA-CORR-2:	The MDA producer for handover and service data correlation analytics should have a capability of allowing the consumer to use the service characteristics such as QoE for providing recommendations for handover analytics.

#### 5.3.K.3	Potential solutions

##### 5.3.K.3.1	Possible solution for handover and service data correlation analytics

- Extend the existing usecase on Handover optimization analytics by enhancing the enabling data to include predicted signalling measurements, predicted user trajectories and predicted signal measurements.

- Extend the existing usecase on Handover optimization analytics by enhancing the enabling data to include service characteristics such as QoE.

#### 5.3.K.4	Evaluation of solutions

End of changes