3GPP TSG-SA5 Meeting #155	S5-242777

Jeju, Korea, 24 - 28 May 2024

# Source:	China Mobile, Ericsson, Intel, NEC, CATT, Nokia, Nokia Shanghai Bell, ZTE, HUAWEI, Verizon

# Title:	Rel-19 Add use case of ML fine-tuning

# Document for:	Approval

# Agenda Item:	6.19.1

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1] 	3GPP TR 28.908-018 “Study on Artificial Intelligence/Machine Learning (AI/ ML) management”.

[2] 			3GPP TR 28.9xx-00 “Study on Artificial Intelligence/Machine Learning (AI/ ML) Lifecycle Management (LCM) Phase 2”.

# 3	Rationale

ML fine-tuning refers to train an ML model not from scratch by only training a small set of parameters which might be a subset of the existing model parameters or a set of newly added parameters. The ML model would be trained in a very efficient way and applied to specific tasks.

# 4	Detailed proposal

Start of modification

# 5	Use cases, potential requirements and possible solutions

## 5.1	Management Capabilities for ML training

5.1.X 	ML fine-tuning

### 5.1.X.1 	Description

ML fine-tuning refers to training an already trained ML model (e.g. a pre-trained model) with a reduced scope.

Inference type is not changed when re-training a model, while fine-tuning of a pre-trained model means that the ML model will be trained with focus on a specific inference type.

The fine-tuning process will be a part of ML Training step as defined in TS 28.105.

#### 5.1.X.2	Use cases

5.1.X.2.1		ML fine-tuning for a pre-trained ML model

In this typical use case, a pre-trained ML model has been trained by the dataset that covers more than one inference type.

Therefore, the consumer may fine-tune a pre-trained ML model for the purpose of a specific inference type.

#### 5.1.X.3	Potential requirements

REQ-ML_ TRAIN-MLFT-1: The ML training MnS producer shall have a capability to enable an authorized consumer to request the fine-tuning of a pre-trained ML model for a specific inference type.

Editor note: It is for further discussion if the same requirements in existing TS 28.105 Table 6.2a.1.3-1 related to training function also applies for fine-tuning.

END of modification