3GPP TSG-SA5 Meeting #155 	S5-243171

Jeju, South Korea, 27 - 31 May 2024                                             Revision of S5-242345

# Source:	Huawei, Deutsche Telekom, Ericsson

# Title:	pCR TR 28.915 Solution for RAN energy saving policy verification

# Document for:	Approval

Agenda Item:	6.19.5

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]		3GPP TR 28.915: " Study on management aspects of Network Digital Twin"

# 3	Rationale

It’s proposed to add solution for use case RAN energy saving policy verification as described in clause 5.1 of [1]

# 4	Detailed proposal

This document proposes the following changes in TR 28.915.

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[a]	3GPP TS 28.310: " Management and orchestration; Energy efficiency of 5G".

[b]	3GPP TS 28.541: "Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3".

Next Change

## 5.1	Use case 1: Network management policy verification using NDT

### 5.1.1	Description

A typical example for policy verification is RAN energy saving policy verification as introduced below.

When configuring the energy saving for RAN, normally the policy is applied in execution with monitoring and optimization loop to minimize the influence on network service quality. That’s to say, there could be multiple ES policies executed iteratively in actual mobile network until the network performance, e.g., energy efficiency of NG-RAN, UE throughput in gNB, etc., meets certain requirements from operators.

This may bring two problems from network management perspective:

-	Redundant ES policies configurations due to conservative adjustment on ES policy for each iteration.

-	Risk of unexpected deterioration in actual mobile network performance.

The digital twin technology may be used to evaluate the impact of RAN ES policy while satisfying simulation performance requirements (e.g., precision, maximum run time, etc).

The consumer could request the NDT to verify the impact of behaviour (e.g., the configuration of RAN energy saving policies) and receive the report of simulated impact generated by NDT.

### 5.1.2	Potential requirements

REQ-NDT-FUN-01 The NDT shall have the capability to estimate the impact of network management policies.

REQ-NDT-FUN-02 The NDT shall have the capability allowing the consumer to configure the network management policies.

REQ-NDT-FUN-03 The NDT shall have the capability to report the simulated impact of network management policies.

Editor’s Note: This UC currently only focuses on RAN. The energy saving policy verification for other part of the network is FFS.

### 5.1.3 Potential solutions

Figure 5.1.3-1: procedure of RAN energy saving policy verification

- MnS consumer requests MnS producer (the entity who provides the NDT for network simulation) to create/active an NDT with simulation requirements. Simulation requirements are used to specify the scope and time of the simulated network in NDT.

- Simulation scope: the area of actual mobile network or the managed object that needs to be simulated in NDT. For instance, a geography area, a network slice, etc.

- Simulation time: the timestamp indicates if the simulation is for the past, present, or future.

- Simulation data: the data that collected for NDT simulation, e.g., PM data as defined in TS 28.552/28.554, CM data as defined in TS 28.541/28.622, etc.

- Based on the simulation requirements given in step 1, NDT collects the data from the managed entities within the specified simulation scope, time and data. If the Simulation time indicates the timestamp in the past, NDT collects the historical network data. If the Simulation time indicates the timestamp in the present, NDT collects the data from live network. If the Simulation time indicates the timestamp in the future, NDT collects the data based on prediction.

- MnS producer receives the simulation requirements for NDT and create/activate the NDT capability. MnS producer notifies MnS consumer that the NDT capability is ready.

- MnS consumer makes analysis and generates network management policy. For instance, MnS consumer collects and analyses energy saving related performance measurements and notices that the energy consumption is too high. MnS consumer decides to lower the energy consumption and generates RAN energy saving policies. A simple example of RAN energy saving policy could be the configuration on certain NR capacity booster cells which specifies to enter the energySaving state or not.

- MnS consumer requests NDT to verify the policy in the simulated network which synchronizes with actual mobile network. The request parameters may include:

- Policy: the relevant policy for a certain use case. For example, the policy for RAN ES policies verification use case could be the ES policy as described in TS 28.310.

- Impact detectors: specified performance metrics and/or alarm types that needs to be collected and reported by NDT after the behaviour happens in NDT.

- Performance requirements: the expected network simulation performance of NDT. For instance, the time spent for the network simulation, the expected proximity between the network simulation results and the actual network execution outcome.

- NDT executes network management policy according to the performance requirements and collects its impact on the simulated network. The impact could be performance measurement or alarm reporting from simulated network.

- MnS producer reports the simulated impact and result to MnS consumer. The report content may include the impact which is a key-value list where the keys contain the impact detectors specified in step5. Alarms are reported if any raised. Possibly an indicator, which shows whether the performance of the network simulation satisfies the performance requirements or not, is also reported.

End of change