3GPP TSG-SA5 Meeting #154 	S5-243172

Jeju, South Korea, 27 - 31 May 2024

# Source:	ZTE Corporation

# Title:	pCR TR 28.915 Update the description on Use case 2 Signaling storm analysis

# Document for:	Approval

Agenda Item:	6.19.5

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

- 3GPP TR 28.915: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Study on management aspects of Network Digital Twin (Release 19) "

# 3	Rationale

The use case and potential requirements about network signaling storm are described in clause 5.2.1 and 5.2.2 in TR 28.915 [1], It is recommended to add additional potential requirements to be aligned with the description.

# 4	Detailed proposal

1st Change

# 5	Use cases

## 5.2 Use case 2: Signaling storm analysis

### 5.2.1 Description

Signaling storm refers to the situation where a large number of signaling messages suddenly surge in the mobile communication network, resulting in the network processing capacity overload, thus affecting the network performance and stability. Signaling storm may be caused because of big event happened that too many users request service at the same time, or by network failure, configuration error or malicious attacks. During this period, users will repeatedly try to establish the connection until reconnected, thus generating a large number of signaling messages surge suddenly, causing signaling storm.

Using the NDT, by simulating various network signaling storm scenarios such as network failure or large amount of user subscribes at the same time because of big event, the impact of the network signaling storm could be evaluated. Furthermore, possible network optimization policies and solutions for mitigating the impact of network signaling storm, e.g. flow control optimization policy, could also be evaluated and verified. In this way, the network operator can determine whether the current network can defend against if signaling storm happened, and find out the way to prevent network failure when network signaling storm happens.

### 5.2.2 Potential requirements

REQ-SIMULATION_NDT-01: The NDT should have a capability allowing the consumer  to request evaluation of the impact of the network signaling storm.

REQ-SIMULATION_NDT-02: The NDT should have a capability to provide the results of network simulation for signaling storm analysis.

### 5.2.3 Potential solutions

End of changes