3GPP TSG-SA5 Meeting #155 	S5-243188d2

Jeju, South Korea, 27-31 May 2024

# Source:	NTT Docomo

# Title:	pCR 28.869 Telco PaaS use case description

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

[1]	3GPP TR 28.869 v0.1.0 Study on cloud aspects of management and orchestration

# 3	Rationale

This contribution proposes to add the description of a new use case for Telco PaaS in clause 5.2 in [1].

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change (Void)

2nd Change

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in 3GPP TR 21.905 [1] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in 3GPP TR 21.905 [1].

<ABBREVIATION>	<Expansion>

CaaS	Containers as a Service

IaaS	Infrastructure as a Service

LCM	Life Cycle Management

PaaS	Platform as a Service

2nd Change

## 5.1	Use of VNF generic OAM functions

### 5.1.x	Relationship between VNF generic OAM functions and a Telco PaaS

A Telco Platform as a Service (PaaS) is a set of cloud services (related to compute, network, storage, and management) that facilitate the deployment and operation of Network Functions, as software applications, on an underlying generic and decoupled cloud infrastructure.

Although ETSI NFV framework supports containerized VNF deployments since Release 4, 3GPP management system specifications, like TS 28.526 [ref-ts28526], lack support for cloud-native NFs that are deployed as containerized workloads, since they still reference Release 2 specifications from ETSI NFV.

When considering cloud-native NFs operations, a Telco PaaS can be used to address fundamental problems like the scalability issue. For example, using entirely separate monitoring tools for storage resources, network resources, and NF application metrics creates scalability issues from the perspectives of both the 3GPP management system and the cloud infrastructure. In addition, a Telco PaaS can be used to support functionalities such as centralized platform management, centralized logging, continuous integration and continuous delivery pipelines and cloud native NF health management. A Telco PaaS can also offer support for different cloud IaaS platforms. This can also enhance portability of Network Functions from one cloud environment to another one. Additional examples of Telco PaaS include services offering management of DNS, generic repository, authentication, monitoring, load balancing, firewall and connectivity, such as service meshes.

From the 3GPP management system perspective, besides the benefits mentioned above, the use of a Telco PaaS can conceal numerous additional challenges, for example, how backwards compatibility can be preserved, how Telco PaaS can interact with other cloud management systems and where the demarcation point for NF management resides when considering existing solutions like NFV-MANO.

The VNF generic OAM functions and other PaaS services framework developed in ETSI GS NFV-IFA 049 [2] can be understood as a Telco PaaS.

End of Changes