3GPP TSG-SA5 Meeting #155 	S5-243181

# Jeju, South Korea, 27 - 31 May 2024

# Source:	Microsoft, Rakuten Mobile, AT&T

# Title:	pCR 28.869 New use case on creation of cloud native NFs

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

[1]	3GPP TR 28.869 v0.2.0 Study on cloud aspects of management and orchestration

# 3	Rationale

This contribution proposes to add a new use case on creation of cloud native network functions.

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change

## 5.2	Use of industry solutions for management of cloud-native network functions

Editor's Note: This clause describes the use cases, issues, requirements, and solutions related to WT-2.

### 5.2.x	Use case #x: Creation of a cloud-native network function instance

### 5.2.x.1	Description

In this use case the 3GPP management system interacts with an orchestration and management entity for creation of a cloud-native NF instance.

In order to deploy a cloud-native NF instance the 3GPP management system conveys the description of the NF requirements and parameters to the orchestration and management entity.  The collection of this information, referred to as descriptor, includes all necessary information  needed by the orchestration and management entity to select and configure the appropriate cloud resources and to deploy the cloud-native NF instance.

The 3GPP management system needs to be able to request an orchestration and management entity to create a cloud-native NF instance. Different orchestration and management entities use different interfaces (including declarative and imperative APIs) and different information and data models for the descriptor.

Editor’s note: The term “cloud-native NF” is not yet defined.

### 5.2.x.2	Potential requirements

REQ-1: The xyz reference point should have the capability enabling the 3GPP management system to request creation of a cloud-native NF instance based on cloud-native NF-specific requirements.

REQ-2: The xyz reference point should have the capability enabling the orchestration and management entity to inform the 3GPP management system of the result of the request for creation of a cloud-native NF instance.

Editor’s note: The term “cloud-native NF” is not yet defined.

### 5.2.x.3	Potential solutions

##### 5.2.x.3.1 	Use of xyz reference point

In this solution the 3GPP management system interacts with an orchestration and management entity using the xyz reference point as described in clause 5.2.1.3 for creation of a cloud-native NF instance.

Figure 5.2.x.3.1-1 depicts a high-level view of proposed procedure for creation of a cloud-native NF instance.

Figure 5.2.x.3.1-1. High level procedure for cloud-native NF creation procedure

The 3GPP management system requests creation of a cloud-native NF instance from an orchestration and management entity for LCM of cloud-native NFs over xyz reference point, and receives the result of the request for creation of the cloud-native NF instance form the orchestration and management entity.

Annex <X> provides an example scenario using interactions with orchestration and management entity for creation of cloud-native NFs. If the orchestration and management entity is ETSI NFV MANO, the interactions over xyz reference point are as specified in clause 7.10 of 28.531[7].

Editor’s note: The term “cloud-native NF” is not yet defined.

### 5.2.x.4	Evaluation of solutions

2nd Change

### Annex <X>: Example scenario using interactions with orchestration and management entity for creation of cloud-native NFs

Figure <X>-1 depicts an example scenario for interaction with orchestration and management entity for cloud-native NF for creation of a cloud-native NF instance.

An authorized MnS Consumer requests creation of a cloud-native NF instance from an MnS producer in a management function which supports interaction with an orchestration and management entity for LCM of cloud-native NFs, by sending a createMOI request with cloud-native network function related requirements.

Figure X-1. Example scenario for interaction with orchestration and management entity for cloud-native NF creation procedure

The management function invokes interactions with an orchestration and management entity for creation of a cloud-native NF instance. Following the completion of the required interactions with the orchestration and management entity, the MnS producer creates the MOI for the managed function and configures new MOI with corresponding information and sends the createMOI response to the MnS Consumer with the DN of the MOI for MangaedFunction.

Note: If the orchestration and management entity is ETSI NFV MANO, the interactions over xyz reference point are as specified in clause 7.10 of 28.531[7].

Editor’s note: The term “cloud-native NF” is not yet defined.