3GPP TSG-SA5 Meeting #155 	S5-24xxxx

Jeju, Korea, 27-31 May 2024

# Source:	Rakuten Mobile, Nokia

# Title:	Adding solutions and requirements for data streaming for cloud native NFs

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

# 3	Rationale

This contribution proposes to add a new use case on data streaming for cloud native network functions.

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change

### Annex <X>:

The figures from A.X-1 to A.X-3 below illustrate three different example implementation scenarios based on the potential solution proposed, for data streaming for cloudified network function. In scenario 1, figure A.X-1, NF directly produce data into message bus and MnF retrieves data from message bus (solution set A). In scenario 2, Figure A.X-3, MnF collect data directly from NF via HTTP (solution set B). In scenario 3, figure A.X-2, there is a data scraper collects and aggregates data from NF via HTTP first before making the data available to message bus for MnF to consume (combination of solution set A and B).  Any implementation scenario is allowed using different combinations of the solution set A and B to meet the various requirements of different deployment scenarios of the cloud-native applications which are explained further below.

Figure A.X-1 Example implementation scenario 1, NF stream data to MnF directly via message bus (solution set A only)

Figure A.X-2 Example implementation scenario 2, NF stream data to MnF directly via HTTP (solution set B only).

Figure A.X-3 Example implementation scenario 3, scraper collect and aggregate the data first via HTTP before producing it to message bus (solution set A and B).

The figure A.X-4 below illustrates another implementation example based on scenario 1 above, using the solution set A for scenarios require parallel data streaming from NFs with transport scaling and resiliency. As shown in figure A.X-4, the containerized workloads of NFs produce data in parallel to a message bus while the containerized workloads of a management function consume the data in parallel from the message bus. The number of parallel workload instances and streaming connections with the message bus may scale in and out dynamically depending on the real-time demand. Furthermore, multiple parallel message bus workload instances may exist which duplicate the connections with MnS procedures and consumers to scale up the transport capacity or provide transport resiliency. The capability for automatic handling of the dynamic scaling, load balancing and resiliency may be provided by along with the message bus implementation. This example may be applied to any deployment scenarios, e.g. at either edge, regional or central cloud.

Figure A.X-4 parallel data streaming based scenario 1.

The figure A.X-5 below illustrates another implementation example based on scenario 3 above, using a combination of solution set A and set B. In this case, the data scrapers collect and aggregate the data first before making the data available to the message bus for consuming by the MnF. At certain scrapping interval, a data scrapper collects the performance metrics data from the workloads of single or multiple NFs and aggregates it as per a configured aggregation time interval. At the expiry of the aggregation time interval, the data scrapper delivers the aggregated data to the message bus. This example implementation may be applied to any deployment scenarios with some examples shown in figure A.X.5. In example 1, the HTTP based data streaming (solution set A) is used between edge cloud and central cloud, and the message bus based data streaming (solution set B) is used only within central cloud. In example 2, the HTTP based data streaming is used only within edge cloud and the message bus based data streaming is used between edge cloud and central cloud.

Figure A.X-5 parallel data streaming based on scenario 3.

A message sequency diagram showing more implementation details related to implementation scenario 3 involving all function entities is shown in figure A.X-6 for information.

Figure A.X-6 example message sequence diagram showing more implementation details in scenario 3.