3GPP TSG-SA5 Meeting #155 	S5-243196

Jeju, South Korea, 27 - 31 May 2024

# Source:	Microsoft, Rakuten Mobile, AT&T

# Title:	pCR 28.869 New use case on termination of cloud-native NFs

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

[1]	3GPP TR 28.869 v0.2.0 Study on cloud aspects of management and orchestration

# 3	Rationale

This contribution proposes to add a new use case on termination of cloud native network functions.

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change

## 5.2	Use of industry solutions for management of cloud-native network functions

Editor's Note: This clause describes the use cases, issues, requirements, and solutions related to WT-2.

### 5.2.x	Use case #x: Termination of a cloud-native network function instance

### 5.2.x.1	Description

In this use case the 3GPP management system interacts with an orchestration and management entity for deletion of a cloud-native NF instance.

A deployed cloud-native network function instance can be terminated by the 3GPP management system. In order to terminate a cloud-native NF instance there is the need to request the termination of the NF instance from the orchestration and management entity.

The 3GPP management system needs to be able to request an orchestration and management entity to terminate a 3GPP cloud-native NF instance.

### 5.2.x.2	Potential requirements

REQ-1: The xyz reference point shall have the capability enabling the 3GPP management system to request deletion of a cloud-native NF instance.

REQ-2: The xyz reference point shall have the capability enabling the orchestration and management entity to inform the 3GPP management system of the result of the request for deletion of a cloud-native NF.

Editor’s note: The term “cloud-native NF” is not yet defined.

### 5.2.x.3	Potential solutions

##### 5.2.x.3.1 	Use of xyz reference point

In this solution the 3GPP management system interacts with an orchestration and management system using the xyz reference point as described in clause 5.2.1.3, for termination of a cloud-native NF instance.

Figure 5.2.x.3.1-1 depicts a high-level view of proposed procedure for termination of a cloud-native NF instance.

Figure 5.2.x.3.1-1. High level procedure for cloud-native NF termination procedure

The 3GPP management system requests termination of a cloud-native NF instance from an orchestration and management entity for LCM of cloud-native NFs over xyz reference point, and receives the result of the request for termination of the cloud-native NF instance form the orchestration and management entity.

Annex X provides an example scenario using interactions with orchestration and management entity for termination of cloud-native NFs. If the orchestration and management entity is ETSI NFV MANO, the interactions over xyz reference point are as specified in clause 7.12 of 28.531[7].

Editor’s note: The term “cloud-native NF” is not yet defined.

### 5.2.x.4	Evaluation of solutions

2nd Change

### Annex <X> (Informative):	Example scenario using interactions with orchestration and management entity for termination of cloud-native NFs

Figure <X>-1 depicts an example scenario for interaction with orchestration and management entity for cloud-native NF for termination of a cloud-native NF instance.

Figure <X>-1: Example scenario for interaction with orchestration and management entity for cloud-native NF for modification of a cloud-native NF instance

An authorized MnS Consumer requests termination of a cloud-native NF instance from an MnS producer in a management function which supports interactions with an orchestration and management entity for LCM of cloud-native NFs, by sending a deleteMOI request with DN of ManagedFunction MOI.

The management function invokes interactions with an orchestration and management entity for termination of the cloud-native NF instance. Following the completion of the required interactions with the orchestration and management entity, the MnS producer deletes the MOI for the managed function and sends the deleteMOI response to the MnS Consumer with the DN of the MOI for MangaedFunction.

Note: If the orchestration and management entity is ETSI NFV MANO, the interactions over xyz reference point are as specified in clause 7.12 of 28.531[7].

Editor’s note: The term “cloud-native NF” is not yet defined.