3GPP TSG-SA5 Meeting #155 	S5-243205

Jeju, South Korea, 27 - 31 May 2024

# Source:	Huawei

# Title:	Update UC for discovery of management capabilities of provisioning MnS supported by a MnS Producer

# Document for:	Approval

Agenda Item:	6.19.8

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]		3GPP TR 28.871 v0.1.0: Study on Service Based Management Architecture (SBMA) enhancement phase 3

# 3	Rationale

This contribution proposes update UC for discovery of management capabilities of provisioning MnS supported by a MnS Producer in TR 28.871 [1].

# 4	Detailed proposal

This document proposes the following changes in TR 28.871 [1].

1st Change

## 5.3	Discovery of management capabilities of MnS supported by a MnS Producer

### 5.3.1 Description

The use cases and requirements for discovery of Management Services are described in TS 28.537 [3], which includes:

-	MnS Consumer retrieves management service information from MnS registry

-	MnS Consumer retrieves detailed capabilities about management service

In TS 28.622 [2], MnsInfo IOC is introduced to describe the management service information and detailed capabilities about management service, which includes:

| Attribute name | S | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| mnsLabel | M | T | F | F | T |
| mnsType | M | T | F | F | T |
| mnsVersion | M | T | F | F | T |
| mnsAddress | M | T | F | F | T |
| mnsScope | M | T | F | F | T |

The model driven approach (i.e. usage of provisioning MnS operations specified in TS 28.532 [14] and NRM fragments) can be used to support various types of management capabilities in SBMA. MnS consumer may need to get management capability information of the MnS in a convenient way. For example, MnS consumer may need to query which MnS can provide the threshold control capability. The current MnSType attribute in MnSInfo IOC cannot be used to represent the management capability information of MnS.

### 5.3.2 Potential requirements

REQ-DMS-1: The 3GPP management system should provide capabilities allowing MnS consumers to retrieve the management capability information for MnS .

End of change