3GPP TSG-SA5 Meeting #155 	S5-243208

Jeju, South Korea, 27 - 31 May 2024

# Source:	Huawei

# Title:	Update Support IOCs in SBMA

# Document for:	Approval

Agenda Item:	6.19.8

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]		3GPP TR 28.871 v0.1.0: Study on Service Based Management Architecture (SBMA) enhancement phase 3

# 3	Rationale

This contribution proposes update on clause Support IOCs in SBMA in TR 28.871 [1].

# 4	Detailed proposal

This document proposes the following changes in TR 28.871 [1].

1st Change

## 5.4	<<SupportIOC>> instances in SBMA

### 5.4.1	Description

SBMA is based on data that is visible, readable, and depending on its nature, potentially writable using the CRUD operations defined in TS 28.532 [3].  <<SupportIOC>> instances, see <<SupportIOC>> defined in TS 32.156 [2], cannot be handled by the CRUD operations.

The only reason to model data is because that data is available in the MnS producer. While it is possible to provide this information via notifications, files or to set the data via dedicated operations SBMA follows the principles:

- if the data is interesting for the consumer, it should be readable via CRUD, because the consumer might not be available when the data is produced. The consumer should be able to fetch the data on demand when the consumer needs it and when the consumer is capable of receiving it.

- it is easier for a consumer to handle a few simple CRUD operations with configuration specific data models than to implement and handle a potentially big number of different dedicated operations and access methods.

Based on the above CRUD operations should be available for modelled data. CRUD operations are available for <<InformationObjectClass>> instances but not for <<SupportIOC>> instances, hence specifying new <<SupportIOC>> definition should be avoided.

Removing existing <<SupportIOC>> definition (if any) is out of scope for the present document.

### 5.4.2 	Potential requirements

NA.

### 5.4.3	Potential solutions

Clarify in TS 32.156 [2] that  <<SupportIOC>> instances are not used when an MnS is designed based on a model driven approach using a NRM and CRUD operations.

End of change