## Slide 1: Input to Joint SA5-NFV workshop on June 5, 2024: Information on Rel-18 and Rel-19 Study and Work Items relevant to management of containerized network functions

## Slide 2: Completed Rel-18 study and work items
Rel-19 study item on management of cloud-native Virtualized Network Functions (VNF)
  Study captured in 3GPP TR 28.834 analysed use cases, requirements, and solutions related to the management of cloud-native virtualized network functions including use of VNF generic OAM functions
    Refer to the next slide for the list of use cases and summary of the conclusions
Rel-18 work item on management of cloud-native Virtualized Network Functions (VNF)
  Based on the conclusions from the study, TS 28.531 (provisioning) and TS 28.533 (architectural framework) were modified to refer to ETSI NFV release 4 specifications for management of cloud-native VNFs.

## Slide 3: Rel-18 study on management of cloud-native Virtualized Network Functions (VNF)
Studied use cases:
  Use case# 1: Configuration of the cloud-native VNF using generic OAM functions
  Use case# 2: Traffic management of the cloud-native VNF using generic OAM
  Use case# 3: Performance monitoring of the cloud-native VNF using generic OAM
  Use case# 4: Failure of VNFC within cloud-native VNF
  Use case# 5: NF creation as a cloud native VNF
  Use case# 6: Scaling of cloud-native VNF
  Use case# 7: Healing of cloud-native VNF
  Use case# 8: VNF package update of the cloud-native VNF
  Use case# 9: VNF package management of the cloud-native VNF
Conclusions and recommendations:
“Some of the use cases are related to VNF generic OAM functions. For the potential solutions about the VNF generic OAM functions see clause 6.1. The potential impact of different solutions on the 3GPP management system is briefly analysed in clause 6.2. It is recommended that the further normative work should take into account the relevant progress from ETSI NFV.”

## Slide 4: On-going Rel-19 study on cloud aspects of management and orchestration
The study item is described in SP-231781
The study includes 3 Work Tasks (WTs):
  WT-1: Analyse the use cases which utilize the VNF generic OAM functions (specified in ETSI) and their potential impacts when applied to the 3GPP management system and study whether and how to incorporate the VNF generic OAM functions into the 3GPP management system, i.e., the requirements and the potential solutions.
  WT-2: Study the use cases that utilize the newly developed industry solutions for management of cloud native network functions which leverage industry standards not limited to ETSI NFV MANO; study the potential impact of supporting such use cases on the 3GPP management system, i.e., the potential requirements and solutions.
    Note: WT-2 includes studying the terminology to determine the appropriate term and definition for cloud native network functions for use in the 3GPP management system.
  WT-3: Study the use cases, potential requirements and possible solutions for 3GPP management system to support different cloud deployment scenarios, such as public-cloud, private-cloud, hybrid-cloud and multi-cloud deployment scenarios.

## Slide 5: WT-1 study captured in clause 5.1 of TR 28.869: Use of VNF generic OAM functions
Submissions are related to the following topics/use cases (up to SA5#155):
  VNF generic OAM functions and SBMA
  Notification management for the cloud-native VNF
  Software modification management for the cloud-native VNF
  VNF policy management using the Policy Agent
  VNF configuration using the VNF configuration manager
Please refer to the latest version of TR 28.869 for approved content

## Slide 6: WT-2 study captured in clause 5.2 of TR 28.869: Use of industry solutions for management of cloud-native network functions
Submissions are related to the following topics/use cases (up to SA5#155):
  Terminology
    Specifically, use of “cloud-native NF” vs. alternative terms
  Support of containers in NFV
  LCM of cloud-native NFs
  Data streaming for cloud-native NFs
  Telco PaaS
Please refer to the latest version of TR 28.869 for approved content

## Slide 7: WT-3 study captured in clause 5.3 of TR 28.869: Support of different cloud deployment scenarios
Submissions are related to the following topics/use cases (up to SA5#155):
  Various deployment scenarios
  Unified management for multiple clouds
  Placement of cloud-native NFs
  Homing of cloud-native NFs
Please refer to the latest version of TR 28.869 for approved content

## Slide 8: Timeline
  3GPP SA5 Rel-19 study item on cloud aspects of management and orchestration is to be completed by August 2024
  Normative phase to follow starting Sept. 2024 and to be concluded by Sept. 2025

## Slide 9: Discussion Items
  3GPP TR 28.834 (Release 18) and TR 28.869 (Release 19) specifications refer to ETSI NFV EVE019 and ETSI NFV IFA049 work regarding the VNF generic OAM functions framework developed by ETSI NFV. Please keep SA5 updated with the relevant progress in ETSI NFV.
  Discussions regarding alignment of 3GPP specifications with Release 4 specifications of ETSI NFV is on-going.

## Slide 10
Thank you !