3GPP TSG-SA5 Meeting #154 	S5-243217

Jeju, Korea (Republic Of), 27th May 2024 - 31st May 2024

# Source:	Nokia, Ericsson

# Title:	Rel-18 pCR 28.872 Add potential solution 2 for Managing planned configurations

# Document for:	Approval

Agenda Item:	6.19.9 - Study on Management of planned configurations

# 1	Decision/action requested

The group is requested to discuss and approve the pCR below.

# 2	References

[1]		3GPP TS 28.872: "Study on Management of planned configurations"

# 3	Rationale

None.

# 4	Detailed proposal

The following changes are proposed for TR 28.872[1].

Begin of modifications

#### 5.x.3.2	Potential solution #2: CRUD operations

In this solution a planned configuration is not represented by a data node tree. Instead, it is represented by a set of operations that, when applied to the current configuration (data node tree), transform the current configuration into the planned configuration.

HTTP/JSON

The operations are described by JSON Patch. JSON Patch is described in RFC 6902 and TS 32.158. A JSON Patch document is JSON array of JSON objects. Each object represents a single operation. Therefore, the operations in a JSON Patch document are ordered. They shall be applied sequentially in the order they appear in the array.

The first example shows how the first operation is created in a planned configuration.

PATCH 3gpp/ProvMnS/1900/plans/p1 HTTP/1.1 Host: example.org Content-Type: application/json-patch+json [ { "op": "add", "path": "/operations/-", "value": { "op": "add", "path": "/SubNetwork=SN1/ManagedElement=ME10", "value": { "id": "ME10", "attributes": { "userLabel": "Berlin NW 1", "vendorName": "Company XY", "location": "Castle Charlottenburg" } } } } ]

The operation in the request is stored in the planned configurations. Operations are also retrieved in that format.

{ "plans": { "p1": { here are some properties describing the planned configuration "operations": [ { "op": "add", "path": "/SubNetwork=SN1/ManagedElement=ME10", "value": { "id": "ME10", "attributes": { "userLabel": "Berlin NW 1", "vendorName": "Company XY", "location": "Castle Charlottenburg" } } } ] } } }

The next example shows how the value of the "location" attribute in the operation can be changed from "Castle Charlottenburg" to "Summer palace Charlottenburg".

PATCH 3gpp/ProvMnS/1900/plans/p1 HTTP/1.1 Host: example.org Content-Type: application/json-patch+json [ { "op": "replace", "path": "/operations/0/value/attributes/location", "value": "Summer palace Charlottenburg" } ]

End of modifications