3GPP TSG-SA5 Meeting #154 	S5-243222

Jeju, Korea (Republic Of), 27th May 2024 - 31st May 2024

# Source:	Nokia, Ericsson

# Title:	Rel-18 pCR 28.872 Add use case on Conditional activation of planned configurations

# Document for:	Approval

Agenda Item:	6.19.9 - Study on Management of planned configurations

# 1	Decision/action requested

The group is requested to discuss and approve the pCR below.

# 2	References

[1]		3GPP TS 28.872: "Study on Management of planned configurations"

# 3	Rationale

None.

# 4	Detailed proposal

The following changes are proposed for TR 28.872[1].

Begin of modifications

## 5.X	Use case #X: Conditional activation of planned configurations

### 5.X.1	Description

A planned configuration may have to be activated automatically when certain conditions are met. For example, performance metric collection jobs or assurance functions shall be created when metrics that are always collected cross some thresholds.

### 5.X.2	Potential requirements

Req-1: The 3GPP management system should allow MnS consumers to create conditions on MnS producers that specify when planned configurations are activated.

### 5.X.3	Potential solutions

MnS consumers can specify conditions on MnS producers. Planned configurations are automatically activated when the conditions evaluate to true.

Conditions shall be specified using the exact same mechanism as the "ConditionMonitor".

HTTP/JSON

The "configuration-conditions" collection resource is introduced. Conditions are specified using Jex. When the evaluation result of the condition transits from false to true the MnS producer shall automatically create configuration activation jobs for the planned configurations specified by "planIds".

Example:

POST 3gpp/ProvMnS/1900/configuration-conditions HTTP/1.1 Host: example.org Content-Type: application/json { "planIds": ["p1", "p7"], "cond1": "some Jex expression" }

After applying the POST request, the resource structure on the MnS producer looks as follows.

{ "configuration-conditions": { "c1": { "planIds": ["p1", "p7"], "cond1": "some Jex expression" } } }

End of modifications