3GPP TSG-SA5 Meeting #155 	S5-243302d1

Jeju, Korea, 27 - 31 May 2024

# Source:	China Unicom

# Title:	pCR 28.876 Concepts and background

# Document for:	Approval

Agenda Item:	6.19.17

# 1	Decision/action requested

The group is asked to discuss and approve.

# 2	References

[1]	Study on management aspects of RedCap feature v0.1.0

# 3	Rationale

This contribution proposes to add text for Clause 4 Concepts and overview in [1].

# 4	Detailed proposal

It proposes to make the following changes to TR 28.876 [1].

1st Change

# 4	Concepts and background

RedCap is a lightweight network access solution aiming at scenarios with relatively low cost, low energy consumption, and low data rate requirement, mainly applying to senecios such as industrial sensors, video surveillance, wearable scenarios, smart grid, etc.

During Rel-17 and Rel-18, lots of normative works have been finished in RAN and CN to support the RedCap features in 3GPP system, bringing some new requirements in management aspects. For example, access bandwidth of RedCap UEs is reduced from conventional UEs, so the management needs adapt accordingly. Besides, different types of RedCap UEs require different capabilities and features.. In the aspect of performacne, the key performance of RedCap service is different from the services such as eMBB, URLLC and MIoT (higher than MIoT but lower than URLLC and eMBB). In the aspect of energy consumption, 3GPP has introduced some complexity reduction features (such as bandwidth reduction and eDRX) for RedCap. These new features may have some impacts on the energy consumption of network which should be evaluated separately. Hence, corresponding performance measurements, KPIs, feature management are supposed to be studied.

End