3GPP TSG-SA5 Meeting #155 	S5-243306

Jeju, South Korea, 27 - 31 May 2024

# Source:	AsiaInfo

# Title:	pCR TR 28.876 Add use case and potential requirements on RedCap information exposure

# Document for:	Approval

Agenda Item:	6.19.17

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP TR 28.876 v0.1.0 Study on management aspects of RedCap feature

# 3	Rationale

This contribution adds use case and potential requirements on RedCap information exposure to TR 28.876 [1].

The Communication Service Customer(CSC) may need the network related performance index information which can only be obtained from the 3GPP management system according to different RedCap use cases and different deployment scenarios to provide better services for RedCap users.

This is related to WT- 4 Study what information about RedCap can be exposed between CSP and CSC, according to different RedCap use cases and different deployment scenarios.

# 4	Detailed proposal

1st Change

## 5.X Use case #A: RedCap Information Exposure

### 5.X.1 Description

RedCap is a lightweight network access solution aiming at scenarios with low-cost, low-power, low-energy-consumption and low-speed requirements, mainly applying to industrial sensors, video surveillance, wearable scenarios. To enabling the CSC to provide more customized and efficient services, the Communication Service Provider(CSP) needs to expose certain network information with accessed RedCap to the CSC. However, the specific information needs of CSC vary under different RedCap use cases and deployment scenarios.

For instance, in industrial sensor scenarios, the CSC (industrial enterprise) needs the CSP to monitor and expose network performance indicators related to RedCap (e.g., throughput, latency, packet loss rate), and dynamically adjust RedCap network configuration (e.g., bandwidth, resource allocation) based on production demands.

In video surveillance scenarios, the CSC (security company) also needs the CSP to monitor and expose network performance indicators related to RedCap and dynamically adjust network configuration based on surveillance demands.

### 5.X.2 Potential requirements

REQ-RedCap-Info-Exposure-1: The 3GPP management system shall be capable of providing RedCap information to the CSC based on different RedCap use cases and deployment scenarios.

Note:	this study will not discuss the contents of MEXPO.

End of change