## Slide 1: Documenting 5GSAT impacts to SA6 specifications
Basu Pattan,
Samsung, 5GSAT_Ph3_App Rapporteur

## Slide 2: Background
SA6 initiated FS_5GSAT_Ph3_App study to identify the impacts of considering Satellite Access for Application Enablement and Mission Critical Service
FS_5GSAT_Ph3_App study is completed and identified certain impacts to the specifications including:
  EDGEAPP in TS 23.558
  SEAL in TS 23.434
  MSGin5G Service in TS 23.554
  ADAES in TS 23.436
  Mission Critical in TS 23.280, TS 23.289
This is only first version on Satellite Access study in SA6 and may have more studies in future releases
How to document impacts due to Satellite Access in respective specifications?

## Slide 3: Examples of Satellite Access impacts
ECS on ground whereas EES and EAS are onboard satellite
Impacts EAS profile, EES profile, EAS discovery filters, EDN configuration information, Service Provisioning, EAS Discovery, Service continuity etc
UE is connected to a SEAL server via Satellite
Impacts SEAL NRM, SEALDD, SEAL Configuration Management, SEAL LMS, ADAE for supporting discontinuous coverage, Store and Forward, Analytics
Dynamic data is known to the MC service server and provided when requested
The dynamic data associated with a group can be enhanced to include whether the affiliated MC service IDs are connected via NTN.
Note more impacts are expected to be identified in future studies.
Dynamic data associated with a MC group
Parameter description
Status i.e. indication of potential emergency or in-peril status of the group, together with the identification of the user who has performed the last modification of this status.
Affiliation status of each MC service ID of the group corresponding to the MC service and the Contact URI(s) from which the user affiliated.
Contact URIs used for designation of the group e.g. aliases of group broadcast, group regroup group URIs.
Media description for group media, including transport and multiplexing information.
Group call ongoing.
Regroup status of group where regrouping using a preconfigured group is used, e.g. whether group is regrouped, MC service group identity of regroup group.
Functional alias binding information for each user within the group.

## Slide 4: Proposals to document Satellite Access Impacts (1/4)
Proposal 1: Embed Satellite Access impacts in the existing (applicable) procedures
  Example:
Note: For specifying new features/procedures, a new clause is created per feature/procedure.

## Slide 5: Proposals to document Satellite Access Impacts (2/4)
Proposal 2: Create a dedicated clause/normative Annex, profiling the existing (applicable) procedures
  Example:
Note: This proposal is applicable for specifying new procedures as well.
Existing TS
Information element | Status | Description
… | … | …
Dynamic service area indication | O | Indicates if the service area is dynamic or not. The service area is dynamic in case of EES on board a MEO or LEO satellite and not dynamic in case of a GEO satellite.
Satellite ID | O | The Satellite ID corresponding to the EAS.
Trajectory ID (NOTE 2) | O | For mobile EES, indicates the trajectory of the EES on board MEO and LEO satellites.
… NOTE 2: The assignment of the trajectory ID for the EES can be done by the operator and/or the satellite service provider. The trajectory and position of the satellite can be calculated for example based on instantaneous/osculating ephemeris versus using TLE-based mean orbital ephemeris. |  | 
Table X.Y-1: EES Profile Enhancements

## Slide 6: Proposals to document Satellite Access Impacts (3/4)
Proposal 3: Create a dedicated specification, profiling the existing (applicable) procedures
  Example:
Note: This proposal is applicable for specifying new procedures as well.
New TS
Information element | Status | Description
… | … | …
Dynamic service area indication | O | Indicates if the service area is dynamic or not. The service area is dynamic in case of EES on board a MEO or LEO satellite and not dynamic in case of a GEO satellite.
Satellite ID | O | The Satellite ID corresponding to the EAS.
Trajectory ID (NOTE 2) | O | For mobile EES, indicates the trajectory of the EES on board MEO and LEO satellites.
… NOTE 2: The assignment of the trajectory ID for the EES can be done by the operator and/or the satellite service provider. The trajectory and position of the satellite can be calculated for example based on instantaneous/osculating ephemeris versus using TLE-based mean orbital ephemeris. |  | 
Table X.Y-1: EES Profile Enhancements

## Slide 7: Proposals to document Satellite Access Impacts (4/4)
Proposal 4: Extension of Proposal 2, additionally specify Satellite IEs merged into existing IE tables
  Example:
Details of the steps of the procedure in context of the satellite.
Only additions of the IE and procedure modified as a result in Satellite dedicated clause
Note: If not modifying existing table then new IE table shall be added in the dedicated clause.

## Slide 8: Factors to consider for making decision
Precedence of documenting in such scenarios
  Proposal 1 (TS 23.501), Proposal 2 (TS 23.228), Proposal 3 (TS 23.289)
Readability of our specifications
  Proposal 2 (those not interested in Satellite Access can skip the entire clause)
  Proposal 4 (IEs specified once and used by multiple solutions, usage of those new Satellite related IEs at one place)
Future Stage-2 updates to main procedure
  Proposal 2 (satellite related enhancements will not be scattered across the whole TS)
  Proposal 4 (satellite related enhancements will not be scattered across the whole TS except for those new IEs)
Stage-3 convenience
  Proposal 2 (specifying IE applicability becomes easier to Stage-3)
  Proposal 4 (Listing of all IEs including satellite IEs in respective tables is easier to Stage-3 and also for IE applicability)

## Slide 9: Summary and Conclusion
Proposals:
  Proposal 1: Embed Satellite Access impacts in the existing (applicable) procedures
  Proposal 2: Create dedicated clause/normative Annex profiling the existing (applicable) or adding procedures
  Proposal 3: Create dedicated Specification profiling the existing (applicable) or adding new procedures
  Proposal 4: Extension to Proposal 2 where satellite IEs are merged into respective existing tables
Conclusion:
  Proposal 2 for documentation of Satellite Access impacts for all topics
    Following proposal 2 create dedicated clause for profiling of existing impacted procedures or adding new procedures