## Slide 1: 5G-MAG views on Media related topics for Rel-19 Service and System Aspects (SA)
5G MEDIA ACTION GROUP (5G-MAG)
www.5g-mag.com

## Slide 2: MEDIA + ICT + COLLABORATION
5G-MAG fosters collaboration and consensus towards the adoption of global Internet and 5G-based access technologies for Media.
These are our most recent ACTIVITIES and current AREAS OF WORK
As 3GPP Market Representation Partner, we:
  Inform the industry on technologies and features relevant for media
  Provide insight into specs towards development/implementation
  Foster industry engagement into applications and services
  Profile relevant standards to lower the entry barrier to complex technologies
  Support the 5G-MAG Reference Tools Development Programme
  Provide technical feedback to 3GPP and bring specifications to life

## Slide 3: 5G-MAG Reference Tools
5G-MAG is running the 5G-MAG Reference Tools Development Program
An OPEN PLATFORM to support the development of 3GPP media technologies
  Beyond the contributions announced under the Target 2023 roadmap, the successful progress allows us to announce the kick-off of an open-source XR Platform in the next few months.
We invite 3GPP members to join 5G-MAG and the 5G-MAG Reference Tools to add additional features and foster the 5G Media ecosystem
  https://developer.5g-mag.com

## Slide 4: Outline
The views towards 3GPP Release-19 work led by SA are described in slides 5-8 covering 9 key topics (in no specific priority order) on:
  AV Production: Registration and Dual Traffic Steering
  AV Production: live broadcast assurance
  Sustainability for Media over mobile networks
  XR & Metaverse enhancements
  MBS via NTN
  New immersive experiences
  Extensions to 5G Media Streaming
  Extensions to MBS
  AL/ML for Media

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | AV Production: Registration and Dual Traffic Steering | Registration and traffic steering via two 3GPP access paths for more reliable and flexible media production. Key objectives include: Enable additional 5GS tools, under MNO control/policy, to improve access/NW resources utilization, capacity, coverage, reliability and QoE, using dual 3GPP access Provide flexible user plane traffic aggregation, steering & switching at 3GPP layer, in particular for specific service flows, based on link quality or other criteria Interworking with non-3GPP access, e.g., switch one 3GPP path to non-3GPP access Enable dual registration via NR-NR, in TN and/or NTN, in a single PLMN, two PLMNs or one PLMN and one SNPN simultaneously Allow registration via non-3GPP access UE has subscription with one network only, may be dual radio capable but should work with single radio UE Roaming scenarios supported: one or two VPLMNs, HR or LBO cases |  | SA2 |  | 

## Slide 6: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
2 | AV Production: live broadcast assurance | On-demand guaranteed bit rate (GBR) and differentiated user experience to enhance live broadcast production Main objectives include: Study the optimization of NWDAF- vertical federated learning to improve the accuracy of NWDAF’s application service flow statistics and detection model Study the extension of NWDAF to support "Recommended Service" based on the "expected" output and model parameters, and close loop policy control |  | SA2 |  | 
3 | Sustainability for Media over mobile networks | Environmental sustainability is a key requirement for the media industry Main objectives include: Study the impact on the 3GPP system of normative outcomes of stage 1 work on “Energy Efficiency as service criteria”. | TR 22.882: Study on Energy Efficiency as Service Criteria | SA2 |  | 

## Slide 7: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
4 | XR & Metaverse enhancements | Extensions to system architecture to enhance XR awareness and QoS handling Key objectives include: further enhancements for RAN scheduling: Awareness of Application Layer Forward Error Correction (AL-FEC) at RAN PDU Set based QoS handling: Introduce PDU-Set delivery deadline (PSDD) as an alternative to PDU-Set delivery budget (PDB), and better adaptability of 5GS QoS level for XR traffic |  | SA2 |  | 
5 | MBS via NTN | Support of Multicast and Broadcast Services via NTN Key objectives include: Enhancements to support multicast/broadcast over a downlink only NTN and support for a heterogeneous return path (3GPP or non-3GPP access) Study of necessary architectural enhancements for 5G MBS via NTN |  | SA2 |  | 

## Slide 8: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
6 | New immersive experiences | Improvements of overall coding efficiency of 5G video services, including new video codecs (e.g. new profiles of HEVC, VVC) Improvements on description and transmission of new immersive and 3D experiences, including immersive video codecs considering appropriate solutions from (e.g., VDI, V3C MIV, MV-HEVC, V3C V-PCC, GPCC, Dynamic mesh) Improvements on description and transmission of avatars, including formats, codecs, protocols and associated metadata. |  | SA4 (see slide 9 - remarks) |  | 
7 | Extensions to 5G Media Streaming | Ad Insertion and Content Replacement Content Steering Digital Rights Management |  | SA4 (see slide 10) |  | 
8 | Extensions to MBS | Usage of MBS Service Layer for LTE-based 5G Broadcast |  | SA4 (see slide 10) |  | 
9 | AI/ML for Media | Understanding the potential of AI/ML for distribution and production of media services. |  | SA4 (see slide 10) |  | 
Items 6-9 are preliminary. 5G-MAG is in the process to identify substantial new work topics for SA4 Rel-19 after progressing with Rel-18.
Additional remarks in slide 9.

## Slide 9: Remarks
Remarks on SA4 discussions and planning
  5G-MAG acknowledges that:
    SA4 is currently working in Rel-17 maintenance work for MBS
    Rel-18 work is on-going, and
    Study/work items from other working groups (RAN and SA2) are expected to impact SA4 work
  Therefore:
    5G-MAG supports starting SA4 Rel-19 planning from December 2023.
    5G-MAG intents to provide input to the SA4 Rel-19 planning when these discussions start.

## Slide 10: Summary
In general, 5G-MAG supports work aimed at enhancing:
  Coverage (of services from all MNOs)
  Capacity (sufficient capacity both in High Density Demand areas and rural areas)
  Adoption (reducing barriers to uptake for consumers and MNOs -through widespread feature support, features that can be used across multiple services/verticals, cost reduction and a complete and supportive standards-based ecosystem, backwards compatibility)
  Environmental sustainability (through design, measurement and reducing impact)

## Slide 11: Thank you!
5G Media Action Group (5G-MAG)
www.5g-mag.com
  Activity Hub
  https://hub.5g-mag.com
  Developer Space
  https://developer.5g-mag.com
  Publications
  https://pub.5g-mag.com
  Academy
  https://academy.5g-mag.com
  Join our open communities Follow us