## Slide 1: View on SA2 Rel-19 package
Maria Pia Galante

## Slide 2: Develop Rel-19 along 3 directions…
Sustainable
Excellence in Operation​
Expansion
«Beyond Connectivity​»
Ambient IoT​
Integrated Sensing & Communication
Enhanced
«Telco Service» Experience ​
AI/ML for 5G Services​
Resilient (Dual)- connectivity​
Energy Efficiency
5G Core: UPF enhancement Ph2
IMS evolution: NG_RTC Ph2, exposure
User identities in the 5GS​
5G SA Roaming
Emergency SMS
Note: This is an initial scrutiny based on Rel-19 proposals submitted for information at SA2#157.
Justifications and details for each item are reported in the following slides.
Items are listed with no specific priority order.

## Slide 3: Overall View on Rel-19 Content (1/4)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Ambient IoT | For MNOs’ business expansion beyond connectivity and towards a more sustainable environment, it seems promising to support new classes of devices with no battery which rely on ambient energy harvesting. MNO networks could collect data from these device and securely expose them to 3rd parties in e.g. smart logistics, smart warehousing, smart homes, and smart cities, intelligent transportation,… It is recommended to start to study stage-2 architecture solutions to address the Ambient IoT service and system requirements identified by SA1 and RAN. | Yes, TR 22.840, Study on Ambient power-enabled Internet of Things | SA2 | Yes, alignment needed on the deployment options e.g. direct and/or indirect mode | SA3 - security implications on Identification /Authentication / SIMs for energy-constrained device
2 | Integrated Sensing & Communication | For business expansion beyond connectivity, it is interesting to study how the same 3GPP radio/core used for communication can generate sensing information relevant to 3rd parties for e.g. intruder detection, avoidance detection, disaster detection, … It is recommended to investigate the potential system enhancements to support and monetize the Integrated Sensing and Communication for SA1 use cases, in parallel to initial RAN studies. | Yes, TR 22.837, Study on Integrated Sensing and Communication | SA2 | Yes (Major) | SA3 for security and possible privacy implications.
3 | AI/ML for 5GS Service | Leverage AI/ML technologies to enable 5GC and Air interface Intelligence, by providing network automation and improving 5G system efficiency (e.g. detection of signalling storms, NWDAF-assisted energy saving, NWDAF-assisted policy recommandations, Support for AI/ML for air interface, …) | - | SA2 | Alignment | -

## Slide 4: Overall View on Rel-19 Content (2/4)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
4 | Resilient Connectivity (aka dual 3GPP access) | As emerged during recent devastating flooding in northeast Italy, disasters can cause interruption of communication services due to damage of infrastructure in several local PLMNs. In order to provide a lifeline in those circumstances and to facilitate recovery efforts, solutions are needed to improve communication resilience exploiting e.g. the satellite access as the primary path while the terrestrial access is temporarily unavailable. ATSSS provides potential to leverage multiple network paths simultaneously. It is recommended that existing ATSSS mechanisms are extended to support dual connectivity over two 3GPP accesses (e.g. satellite and terrestrial) for the same PDU session under the same MNO’s policy and control (single subscription). | Yes, TR 22.841 Study on Upper layer traffic steer, switch and split over dual 3GPP access | SA2 | Alignment | -
5 | Energy Efficiency | Next generation mobile communication systems are expected to accommodate more demanding services which will require much energy consumption at the device side as well as the network side. There is a need to improve the sustainability of the 3GPP ecosystem. It is recommended that SA2 investigates options for improved system behaviour aimed at overall energy saving, exploring the two following directions: Holistic solutions to further reduce system energy consumption, in collaboration with SA5 and RAN (i.e. provide same service more efficiently) Architecture impacts for Energy-aware services, (i.e. normative outcomes of the Stage 1 work on “Energy Efficiency as service criteria”) | Yes, TR 22.882 Study on Energy Efficiency as service criteria | SA2 | Alignment needed with RAN | Alignment needed with SA5
6 | 5G Core enh: UPEAS Ph2 | For flexible deployments, it is important that 1) User Plane handling can be made modular in order to be able to dynamically and flexibly insert only relevant functionality in the data path (e.g. NAT), 2) new UPF functions are defined in modular way and 3) UPF data/event exposure is enhanced. It is recommended to address remaining key issues not handled in Rel18 FS_UPEAS, to support better integration of UPF into the 5GC SBA. | no | SA2 – see Rel18 TR 23.700-62 | no | 

## Slide 5: Overall View on Rel-19 Content (3/4)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
7 | IMS evolution: NG_RTC Ph2, IMS exposure | As highlighted by GSMA, “The IMS Data Channel offers new communication modes enabling IMS intermodal and interactive services with active content execution. It is what is needed to enable innovation”. Based on NG_RTC in Rel-18, the Operators will be already able to provide Data Channel applications to the subscribers to enhance the experience of real-time communication in IMS network. It is recommended to study useful enhancements on top of that work such as providing data verified OIP (Originating Identification Presentation) service providing capability exposure to the enterprise/verticals for IMS existing communication services (e.g. simple VoLTE call) as well as for NG_RTC services | Yes, TR 22.873 Study on evolution of the IP Multimedia Subsystem (IMS) multimedia telephony service | SA2 | no | SA6 for CAPIF exposure framework
8 | User identities in the 5G System | By enhancing the 5G System to allow the creation and utilization of user-specific identities, operators will be able to provide enhanced user experience, optimized performance, and offer services to devices and users that are not part of the operator’s 3GPP network. This need dates back to Rel16 when stage 1 activity on TR 22.904 was completed and turned into normative requirements (but stage 2 has been systematically de-prioritized since then…). It is recommended to start a stage 2 study on e.g. the format of an operator assigned User Identifier, on new information to be stored as part of the user profile and how they are linked to a subscription, … | Yes, TR 22.904 Study on user centric identifiers and authentication | SA2 | NO | SA3 for security, SA5 for charging

## Slide 6: Overall View on Rel-19 Content (4/4)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
9 | 5G SA Roaming | Recent discussions in GSMA on 5G Roaming showed the importance to consider and preserve roaming ecosystem intermediaries such as Roaming Hub, IPX and RVAS Providers, when transitioning from 2G/3G/4G roaming to 5G with built-in E2E security. It is recommended to: In cooperation with GSMA, analyze requirements from use cases that are established in roaming currently and that should be provided for 5G SA roaming per the different roles of RH/IPX Provider/RVAS Provider, and provide any architecture enhancements to meet such requirements Offer solutions to enable provisioning of specific Roaming VAS, as per stage 1 requirements, by either the PLMN or by a fully-trusted roaming intermediary | Yes, stage 1 in TS 22.261. New requirements from GSMA to be evaluated by SA1 | SA2 | no | SA1, SA3 and GSMA 5GMRR Task Force, for alignment
10 | IMS evolution: SMS emergency | EU regulations require that Emergency should be accessible regardless of the service used (voice, SMS, video, …). 3GPP specifications already support Emergency Calls with voice and other media, but this does not include SMS. It is recommended to study how to support Emergency SMS over IMS (for EPS and 5GS), incl. e.g. how an SMS is routed to an emergency centre serving the UE location in roaming case. | Yes, requirements have been specified in (late) Rel-18 TS 22.101 | SA2 | no | CT1

## Slide 7: General requirements
As 5G Core deployments get more and more widespread, SA2 should plan for “spare capacity” to be used to fix any urgent deployment issue that may arise during the Rel19 timeframe
Rather then pushing for full-blown “Phase 3/4/…” enhancements of a feature, SA2 should carefully examine if there is enough MNOs/market justification for (max) 1 or 2 essential enhancements of any such feature
Keep tight alignment with RAN for SA2 items with RAN dependencies

## Slide 8: Summary
The document highlights TIM’s view on Rel-19 SA2 package, mostly based on the proposals submitted for information at SA2#157 (May ‘23)