## Slide 1: Rel-19 Items
CableLabs

## Slide 2: Overview
Rel-19 projects should address operators’ needs (e.g., by enabling more flexible deployment options to increase adoption of optional features)
Rel-19 projects should address different industry sectors e.g., balance projects on MNO/MVNO scenarios, eMBB/IIoT, etc.
Rel-19 projects should balance enhancements of existing features (e.g., ATSSS, WWC, XRM), new use cases (e.g., ATSSS-lite, metaverse) and forward-looking features (e.g., sensing/communication integration)

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | ATSSS Enh (S2-2306694, S2-2306692, S2-2307179) | Enhancements of ATSSS to support various deployment scenarios: Key issue: ATSSS over two NR (dual steer), separate MPTCP/MPQUIC proxy from UPF, ATSSS Lite | Yes, TR 22.841 (DualSteer) | SA2 | No | TBD
1 | WWC Enh (S2-2307401, S2-2307179) | Support QoS provisioning and policy for individual NAUN3 device behind RG and AUN3 device behind FN-RG Key Issue: Individual NAUN3 QoS/policy provisioning, support AUN3 behind FN-RG | Yes, TS 22.261 | SA2 | No | SA3 for security
1 | Indirect Network Sharing (S2-2306489) | Support RAN sharing with reduced overhead/enhanced architecture compared to MOCN Key Issue: architecture enhancements to support indirect network sharing via a host operator’s network function | Yes, TR 22.851 (NetShare) | SA2 | TBD | TBD
1 | Identification of Non-3GPP device behind WLAN AP (SWS-230057) | Enhance untrusted access procedure to address deployment requirements Key issue: network-controlled registration triggering, UE WLAN access information exposure to 5GC, UE subscription information exposure to AF | Yes | SA2 | No | SA3/SA5
1 | XRM (S2-2306753, S2-2307383, S2-2307179) | Enhancement of XRM via non-3GPP access, other enhancements Key issues: XRM support for non-3GPP, XRM over ATSSS, XRM Enh to support encrypted transport layer | Yes | SA2 | Yes | TBD
6 | Metaverse (S2-2307245) | Support end-to-end QoS control for mobile metaverse services | Yes, TR 22.856 (Metaverse) | SA2 | TBD | TBD
We also support new topics such as ambient IoT and integrated sensing/communication

## Slide 4: ATSSS Enhancements
Dual-Steer
  Support ATSSS over two NR accesses (single PLMN, PLMN + PLMN, PLMN + SNPN, SNPN + SNPN) + one N3GPP access
    Support ATSSS across multiple operators with single or multiple subscriptions
ATSSS-Lite
  Lightweight ATSSS between non-integrated Wi-Fi and 3GPP access
    Support steering/switching across non-3GPP access without gateway functions and 3GPP access
Separate MPTCP/MPQUIC proxy (+ PMF) from PSA UPF
  MPTCP/MPQUIC can be utilized regardless of MA-PDU session setup
  Allow flexible deployment of proxy function

## Slide 5: WWC Enhancements
Proposals
Enhance support of differentiated QoS/policy for each device behind RG:
  Device is identifiable by 5GC (e.g., based on MAC addr)
    Authentication of device may be done locally or by 3rd party server
  A PDU session can be shared by multiple devices behind the RG, where separate QoS flow may be configured for each device within the PDU session if necessary
  FN-RG and 5G-RG are supported. For 5G-RG, both wireline and NG-RAN connections are supported
Motivations
Various use cases such as parental control, prioritized service for work from home scenarios, wireless backup, etc require differentiated QoS/policy control for individual device behind CPE/RG
  Up to Rel-18, this is supported only for AUN3, 5G UE, N5GC and N5CW
  Rel-18 does not support individual QoS/policy control for a NAUN3 device
Limitations of Rel-16/18 procedures
  Scalability: 5G-RG may not be able to handle more than X number of AUN3 devices with limited number of PDU sessions support (e.g., X = 14)
  Limited device availability: Many legacy devices may not support authentication procedure required for AUN3, 5G UE or N5GC
  Limited deployment scenarios: Support for FN-RG and 5G-RG connection via NG-RAN are limited

## Slide 6: Indirect Network Share
MOCN in 5G
Pros – (1) Supports sharing of access network across participating operators.
Cons- (1) Requires separate direct connection from shared NG-RAN towards each participating operators CN (2) Does not scale with a number of participating operators and/or a number of shared NG-RANs (3) Not efficient with small cell scenarios
Indirect RAN sharing via host operator’s CN
Enables network sharing without the need of interfacing the shared NG-RANs to individual participating operators CN
Architecture enhancements to support inter-PLMN routing
Indirect RAN sharing via a host operator’s network function (e.g., a gateway)
No need to maintain individual interface (e.g., N2) from a shared NG-RAN to individual participating operator CN
Hosting operator gateway could aggregate/route traffic from shared NG-RANs before forwarding via individual interface to each participating operator’s core network
No impact on shared NG-RAN compared to MOCN
Interfaces between Host Operator CN and Participating CNs e.g., N14/N16
Interfaces between Host Operator CN
and Participating CNs e.g., N2/N3

## Slide 7: XRM Enhancements
Extend XRM support via non-3GPP accesses (trusted, untrusted, wireline)
  ECN marking for the purpose of L4S over non-3GPP access (e.g., L4S enabling at N3GPP access via SMF/PCF, Congestion level exposure from N3GPP to PSA, N3GPP access information exposure to AF, end-to-end L4S queue handling)
  Support of PDU Set based QoS handling over non-3GPP access
Study the impact of ATSSS multi-path protocols (MPTCP/MPQUIC) over end-to-end congestion control (L4S)
Support integrated handling of XRM traffic (e.g., L4S, PDU set) over 3GPP and non-3GPP accesses
Support of additional transport and media protocols for L4S and PDU Set handling
  L4S – RTP over QUIC, MASQUE
  PDU Set – RTP over QUIC, MASQUE, Media over QUIC (MOQ)

## Slide 8: Thank you