## Slide 1: Huawei views on Rel-19 SA
Huawei, Hisilicon

## Slide 2: Outline
This paper is to introduce Huawei’s thoughts on 3GPP Rel-19 SA items.
Rel-19 Timeline
Overview of Rel-19
Rel-19 content list from Huawei’s point of view.
Detail information on Rel-19 content

## Slide 3: 3GPP Rel-19 Timeline (Agreed at TSG#99 / March 2023)
RAN Rel-18
2022
Q2
Q3
Q4
Q1
2023
Q1
TSG#95
TSG#96
TSG#97
TSG#98
TSG#99
Q2
Q3
Q4
TSG#100
TSG#101
TSG#102
2024
SA/CT Rel-18
TSG#103
Q3
Q4
TSG#104
TSG#105
Q2
Q1
RAN1
frozen
ASN.1
frozen
SA2/Stage 2
frozen
RAN2/3/4
frozen
ASN.1
CT/SA ASN.1
frozen
SA/CT Stage3
frozen
RAN Rel-19
SA2 Rel-19
RAN Rel-19 preparation
SA2 Rel-19 preparation
RAN1/2/3 R19
RAN4 R19
Rel-19 timeline
Decision
SA stage2
First package
SA stage 2
Second package and coordination with RAN
SA/RAN Rel-19 workshop

## Slide 4: Rel-19 as the second release of 5G-Advanced
  Rel-19 is a core release for 5G-Advanced, critical to ensure healthy global 5G deployments in coming years
  Rel-19 projects should be commercially and deployment driven
  Strive for a good balance between use cases expansion, enhancements of existing use cases/features, and work on future-looking features
ELAA-MM
XR Pro
Ambient IOT
Sensing
URLLC
8T8R
UPLINK Enh.
Multi-carrier Enh.
Positioning
eRedcap
F1
F2
F3
F4
V2X
Multi-modality
FR1 HBF
EC
NGRTC

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Ambient IoT (See slide 9-10 for more details) | 5G system to support new IoT segment for battery-less devices. Key objectives: Architecture update to support Ambient IoT for all types of devices(passive, semi-passive, active) Ambient IoT device identification Registration and connection management of Ambient IoT devices Services for Ambient IoT (e.g small data transfer, Inventory service etc.) Charging Security | SA1 FS_AmbientIoT TR22.840 | SA2 | Yes | SA3 for security SA5 for charging
2. | Integrated Sensing & Communications (See slide 11-12 for more details) | Define e2e architecture to enable 5GS to support NR based sensing capability as a service to get information about objects in the environment. Key objectives Overall architecture and function enhancement to support new sensing service. Sensing service authorization and control Sensing measurement collection/result calculation Sensing result exposure Policy/Charging for Sensing Security | SA1 Sensing TS 22.837 | SA2 | Yes | SA3 for security, SA5 for charging

## Slide 6: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | NG-RTC+ (See slide 13 for more details) | Enhancements to the IMS network architecture, interfaces and procedures for the NG-RTC Support for interworking and roaming of IMS data channel Providing IMS data channel in an IMS emergency call Expose IMS real time communication (audio, video, text, data) to third party. Support use cases for metaverse (e.g. XR immersive communication among multiple users | Rel-19 SA1 FS_Metaverse TR 22.856 | SA2 | No | SA3, SA4
4 | EC+ (See slide 14 for more details) | To accelerating the EC deployment in large area, support to management the edge network information locally Enhancement of EAS discovery Consecutive traffic steering Enhancements of local traffic routing in non-roaming scenario Enhancements of local traffic routing in roaming scenario | No | SA2 | No | No
5 | XRM+ (See slide 15 for more details) | Extend PDU Set concept to cover more use cases Support for encrypted media traffic or traffic using proprietary protocols。Enhancements on traffic detection and QoS Flow mapping for mixed data flows, e.g., audio, video, haptic streams, multiplexed in a single media flow Study fast and efficient information exchanges between 5G system and the application layer Further support for multiple modality services | Rel-19 SA1 FS_Metaverse TR 22.856 | SA2 | Yes | SA3,SA4

## Slide 7: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
6 | AIML+ (See slide 16 for more details) | Enhance NWDAF to support intelligent recommendation to 5GC NFs, taking global information from multiple NFs into account | No | SA2 | No | No
7 | Advanced Industrial Internet of things (See slide 17 for more details) | URLLC enhancements Capacity and latency performance improvement (e.g. avoid padding transmission) Support BAT adjustment and survival time in UE-to-UE scenario Native support for duplication redundancy Support integration of 5G VN and legacy LAN Support time synchronization service for ad-hoc cooperative group and service assurance for high accuracy time synchronization service | TS22.104(URLLC+timing) ,TS22.261 (5G VN) | SA2 | Yes | No
8 | Mobile VPN (See slide 18 for more details) | User identify for non-SIM device behind 3GPP UE. Remote UE accessing private network | TS 22.261, TS 22.101, TS 22.115 | SA2 | No | SA3 for security SA5 for charging

## Slide 8: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
9 | Enhancement of EE for 5G networks and services (See slide 19 for more details) | Study the Enhancement of Energy Efficiency evaluation to consider multiple factors. Exposure of energy efficiency as a service Study the enhancement of energy consumption measurement to support estimation of carbon emissions | FS_EnergyServ TR22.882 | SA5 | RAN | No
Other inputs from SA3/4/5/6 may be provided in future meetings.

## Slide 9: Ambient IoT (1/2)
1) Asset/ goods inventory and tracking
Information (e.g., identity) is stored in a small size, ultra-low cost, and battery-less Ambient IoT device
Scenarios: Asset management in Manufacturing, warehouse logistics, healthcare, etc.
Information (e.g., temperature) is generated and transmitted by wireless sensor without battery replacement during long lifetime
2) Sensor data report
Design target for Ambient IoT
Motivations
Scenarios: Electric power, chemical, livestock farming, manufacturing
Reduce device cost and power consumption by 10-100 times than existing mMTC technologies

## Slide 10: Ambient IoT (2/2)
Key objectives
  identification of Ambient IoT devices
  Registration and Connection Management for Ambient IoT devices
  Ambient IoT services and data transmission
  Operator charging support
  Security aspects
A-IoT Tag
N2
TMF
NR
NEF
A-IoT AF
AMF
Architecture overview
  Potential architecture impact：
  AMF/TMF: Support Ambient IoT service management
  NEF: Ambient IoT service exposure/ data transmission
  N2 interface: Support RAN as ambient reader function
  N1 interface: Simplified NAS protocol
N1
Refer to S2-2307089
Architecture figure is an early consideration

## Slide 11: Integrated Sensing and Communication(1/2)
UE transmission
BS transmission
Sensing
Communication
Co- Base Station Hardware
Co-Spectrum, a few resource for sensing
t
f
COMM
COMM
COMM
COMM
COMM
COMM
…
…
COMM
COMM
COMM
COMM
COMM
COMM
…
…
COMM
COMM
COMM
COMM
Communication
t
f
COMM
COMM
COMM
COMM
COMM
COMM
SENSE
SENSE
…
…
COMM
COMM
COMM
COMM
COMM
COMM
SENSE
SENSE
…
…
As Is
ISAC To Be
Object
UE
Reflection

## Slide 12: Integrated Sensing and Communication(2/2)
UDM
SMF
AMF
(R)AN
Sensing
UE
UPF
DN
AF
Sensing
Function
Nudm
Namf
Nsmf
N4
N?
Uu
5GC
Reader Role
Sensing Service
Reader Role
NR
Sensing Object:
Reflecting sensing signal
NR
Sensing signal transmission and reflection reception
Sensing measurement data generation
5GC: communication, Sensing control and data calculation/report
Sensing service authorization
Sensing accuracy/type/area control
Sensing result as a service to expose/SaaS
Sensing data collection
Sensing Service, application layer
N2
3GPP Impact Overview
Impacts of NW centric sensing:
SA2: New Sensing function under full MNO control; NEF, AMF, SMF, UPF enhancements
RAN3: NGAP enhancements to support sensing service control from AMF; sensing data report to UPF/SF; Sensing data format
SA3: Security Aspects
ISAC Architecture
NEF
Nnef
Non-UE specific
Architecture figure is an early consideration

## Slide 13: NG-RTC+
Key objectives
  Define the enhancements to the IMS network architecture, interfaces and procedures for the NG-RTC
  Support interworking and roaming of IMS data channel
  Providing IMS data channel in an IMS emergency call
  Expose IMS real time communication (audio, video, text, data) to third party.
  Support use cases for metaverse (e.g. XR immersive communication among multiple users)
audio
video
data channel
IMS A
IMS B
DCSF
DCMF
DCSF
DCMF
IMS AS
IMS AS
TrGW
IBCF
TrGW
IBCF

## Slide 14: Enhancement of Edge Computing
1) Architecture enhancement for Localized EC network management
2) Enhancement of EAS discovery considering e.g. EAS load, multi EAS collaboration, N6 Delay
V-UPF
(PSA)
V-SMF
UPF
(ULCL/BP+L-PSA)
H-SMF
VPLMN
HPLMN
4) Flexible traffic routing in roaming/non roaming scenarios
Refer to S2-2307072
3) Consecutive traffic steering
5GC
AMF
UE
ULCL
SMF
NF
EASDF
NRF
DC for applications
PSA
L-PSA
APP
NF
L-PSA
APP
campus
DNAI 1
DNAI 2
DNS baseline info
L-PSAs
APPs

## Slide 15: XRM+
refer to S2-2307020
Extend PDU Set concept for more use cases, including:
  Content ratio based PDU Set handling;
  Cross-PDU Session PDU Set delivery for UE-to-UE service via DN；
  PDU Set concept across multiple service flows;
Support for encrypted media traffic or traffic using proprietary protocols, including:
  PDU Set identification and marking;
Enhancements on traffic detection and QoS Flow mapping for mixed data flows, e.g., audio, video, haptic streams, multiplexed in a single media flow;
Support for multiple modality services, including:
  Enhancements of Traffic Characteristics information to NG-RAN.
  Coordinated QoS handing for multi-modal service with multiple data flows, e.g. joint admission control and handover control, synchronization;
Fast and efficient information exchanges between 5G system and the application layer, including:
  Fast and efficient resource adjustment to adapt to dynamic application requirements;
  Fast and efficient QoS notification to adapt to dynamic network status changes.
  Notification of XR user experience assessment.

## Slide 16: AIML+
NWDAF
Expected
service experience
UPF
PCF
UPF
AMF
SMF
Final QoS decision
Recommended Bit Rate, Packet Delay and so on.
OAM
RAN
Collected RSRP, RSRQ, SINA
Motivation
Coordination among multiple NFs, to avoid less optimized or even conflict actions by each NF based on the NWDAF analysis, which may even impact the network stability.
Key Objective
How to provide intelligent recommendation to 5GC NFs, taking global information from multiple NFs into account.
For example, based on the analysis of network status and service experience requirements, the NWDAF provides recommendation on the QoS KPIs to the PCF for policy decisions and the QoS parameters adjustment.

## Slide 17: Mobile VPN
Key objectives
Authentication/authorization of the devices behind the relay UE
Support for differentiated QoS and policy for the devices behind the relay UE
Traffic routing between remote UE and the devices belonging to its VPN crossing different UPFs.
UPF
Scenario 1
NR
NR
User3 VPN
staff office
UPF
NR
User 3
User2
DN-AAA
5G CPE
User1
Scenario 2
Relay UE
Relay UE
5GC
Requirement: TS 22.101 26a User Identity
Refer to S2-2307163

## Slide 18: Advanced Industrial Internet of Things
URLLC enhancement
Timing Service
5G VN integrated with legacy LAN
URLLC capacity+( e.g. padding compression)
Support of native redundant UP paths without relying on upper layer protocols
Industrial co-movement
use case in TS 22.832
Time synchronization service for ad-hoc cooperative group
Support integration of 5G VN and legacy LAN.
Exposure of 5G capability for factory
Use cases: bank branches, chain stores, factory areas, enterprise campuses, and electric grids etc.
Service assurance for high accuracy Time Synchronization service
BAT adjustment and Survival Time enhancement in UE2UE scenario
Refer to S2-2307093

## Slide 19: Enhancement of EE for 5G networks and services
Key Objectives:
Study the Enhancement of Energy Efficiency evaluation to consider multiple factors.
Exposure of energy efficiency as a service
Study the enhancement of energy consumption measurement to support estimation of carbon emissions
Energy Consumption and Energy Efficiency Evaluation: enhancement of measuring Energy consumption and energy efficiency with considering multi-dimension factors （e.g. Coverage)
Energy saving management: keep balance between green energy supply and site energy demand to optimize the carbon efficiency and improve the overall green energy usage.
It is beneficial to have comprehensive view of 3GPP work on energy efficiency, energy saving and digital sobriety.
existing EE KPI in R18
Motivation

## Slide 20
Thank You!