## Slide 1: Rel-19 Architecture Enhancements for Energy Utilities
EUTC, EDF, Novamint, Samsung

## Slide 2: Outline
Where we are for supporting Energy Utilities:
  Requirements were identified in SA1 in Rel-18 as part of the Smart Energy Infrastructure (SEI) feature.
  Activities derived from SEI have been conducted in SA5 in Rel-18
  There are several SA1 requirements coming out of SEI which have impacts on architecture
  These requirements have not been addressed in Rel-18
What is expected:
  Support for SEI SA1 requirements that have not been implemented in Rel-18

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Architecture Enhancements for Energy Utilities | The study aims to study enhancements to enable support for SEI requirements that are not implemented in Rel-18, specifically 1. exposure of specific information regarding the status of the UE's serving RAN, as per the SA1 requirements. 2. exposure of specific (a restricted set of) subscriber configuration and the ability to request changes to it. 3. exposure of changes in QoS policy and configuration of a LAN-VN. | Yes, TS 22.261 | SA2 | No | 

## Slide 4: Architecture Enhancements for Energy Utilities
Motivation
  Requirements were identified in SA1 in Rel-18 as part of the Smart Energy Infrastructure (SEI) feature.
  These will enhance availability of 3GPP services, because Energy Utility service providers can identify anomalies and trigger proactive use of an alternative communication service, e.g. for multiple USIM devices, register with a different PLMN.
  Several SA1 requirements from SEI were not addressed in Rel-18 stage 2
Areas for study:
  Support for SEI requirements that are not implemented in Rel-18
    Support exposure of network analytic information to energy utilities as per the SA1 requirement concerning UE radio parameters known to the NG-RAN E.g. RAT type serving the UE, cell ID, RAN quality of signal information, assigned frequency band.
    Support for configuration management interfaces, e.g. to identify the IP and 5G VN configuration associated with a particular UE.

## Slide 5: SEI SA1 Requirements not implemented in Rel-18
Based on operator policy, the 5G system shall provide means by which an MNO informs a third party of changes in UE subscription information. The 5G system shall also provide a means for an authorised third party to request this information at any time from the MNO. NOTE 4: Examples of UE subscription information include IP address, 5G LAN-VN membership, and configuration parameters for data network access. NOTE 5: These changes can have strong impacts in the stability of the third-party service.
The 5G system shall provide a means by which an MNO can inform authorised 3rd parties of changes in the - RAT type that is serving a UE; - cell ID; - RAN quality of signal information; - assigned frequency band. This information listed above shall be provided with a suitable frequency via OAM and/or 5G core network. NOTE 6: The information aids the third party user to take proactive actions so that it can achieve high service availability in delivery of its services.
Based on operator policy, the 5G system shall provide means for authorised 3rd parties to request changes to UE subscription parameters for access to data networks, e.g., static IP address and configuration parameters for data network access.
Based on MNO policy, the 5G network shall provide suitable means to allow an authorised third party to - monitor changes in QoS policy that pertains to LAN-VN performance; - configure and receive information regarding the achieved performance for a specific UE; - configure and receive information regarding the achieved performance for a specific network; - receive notification of changes in specific configuration aspects of the UE in the VN (e.g., changes in group membership information.)

## Slide 6: Summary
In Release 18, SA1 specified Smart Energy Infrastructure (SEI) service requirements.
The required functionality, once standardized and deployed, will improve service availability for energy utilities and are crucial to support the smart grid operation
Architecture Enhancements for Energy Utilities are needed
We propose to support in Rel-19 the SEI SA1 requirements that have not been implemented in Rel-18