## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #106, Madrid, Spain
Dec 9th – 12th, 2024
RP-242422

## Slide 2: Executive Summary
Total 1294 Tdocs at submission deadline (excluding LSin received from other groups) in Q4
  10% LSs and related documents
  21% Maintenance: Rel-18 & earlier
  69% Documents to Rel-19 WIs
Updated endorsed guidelines endorsed in R3-247003
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-247004
R19 Ambient IoT SI is completed in RAN3.
RAN3#125bis | Oct 14th – 18th, 2024 Hefei, China
RAN3#126 | Nov 18th – 22th, 2024 Orlando, USA
RAN #106 | Dec 9th – 12th, 2024 Madrid, Spain

## Slide 3: Tdoc submitted to RAN3
In R19, the total number of contributions around 640 (less than R18) for each RAN3 meeting seems reasonable, quota rule works well.
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Tdocs for each Topic

## Slide 6: Overview of RAN3-led Rel-19 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
1021092 | Data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) Phase 4 WI | NR_ENDC_SON_MDT_Ph4-Core | 25/09/2025 | 30% | WID: RP-234038 | 50% | 
1050124 | New WID: Enhancements for Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN | NR_AIML_NGRAN_enh-Core | 25/09/2025 | 0% | WID: RP-242385 | 30% | 
1051125 | New WID on additional topological enhancements for NR | NR_WAB_5GFemto-Core | 25/09/2025 | 0% | WID: RP-242395 | 30% | 
1020083 | Study on enhancements for Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN SI | FS_NR_AIML_NGRAN_enh | 25/09/2024 | 80% | WID: RP-240323 | 100% | 
1020082 | Study on additional topological enhancements for NR SI | FS_NR_WAB_5GFemto | 25/09/2024 | 70% | WID: RP-240319 | 100% | 
WI: Black SI: Blue
Completed WI/SI: Red

## Slide 7: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-242423, which includes:
  80 CRs were agreed in Q3.
    8 Rel-16: 8 Cat.F CRs
    16 Rel-17: 9 Cat.F CRs, 7 Cat.A CRs
    56 Rel-18: 39 Cat.F CRs, 15 Cat.A CRs, 2 Cat.B CRs
      6 Non-Backwards-Compatible (NBC) CRs
        All Cat.F: Rel-17 Cat.F(R3-247080 in RP-243103), Rel-18 Cat.F(R3-247044, R3-247069, R3-247070, R3-247777, R3-247778 in RP-243104), Rel-18 Cat.A(R3-247081 in RP-243103)
        (Here is how 3GPP works with NBC changes)
    6 TEI18 Cat.F CRs with TEI identifier
      [PosL2RemoteUE] R3-247056
      [RedcapMBS] R3-247077, R3-247078
      [PosLocalCoords] R3-247085, R3-247086
      [2Rx_XR_Device] R3-247810
      *Details of each agreed TEI18 CR and corresponding identifier in Appendix
  11 endorsed draftCRs to RAN2 specs.

## Slide 8: TEI 18 – RAN3 Only CRs
[PosL2RemoteUE] (Cat.F) * This TEI identifier was introduced at RAN#102 by RAN2(CR pack: RP-233881)
[RedcapMBS] (Cat.F) * This TEI identifier was introduced at RAN#102 by RAN2(CR pack: RP-233882)
TDoc | Title | Source | Type | Spec | Version | Related WIs | CR | CR category | TSG CR Pack
R3-247077 | Correction on broadcast reception for eRedCap UE [RedcapMBS] | Huawei, Qualcomm Incorporated, ZTE, CBN, Nokia, CATT | CR | 38.413 | 18.3.0 | TEI18 | 1207 | F | RP-243107
R3-247078 | Correction on broadcast reception for eRedCap UE [RedcapMBS] | Huawei, Qualcomm Incorporated, ZTE, CBN, Nokia, CATT | CR | 38.473 | 18.3.0 | TEI18 | 1507 | F | RP-243107
[PosLocalCoords] (Cat.F) * This TEI identifier was introduced at RAN#102 by RAN2(CR pack: RP-233881)
TDoc | Title | Source | Type | Spec | Version | Related WIs | CR | CR category | TSG CR Pack
R3-247085 | Correction of TRP Geographical coordinates [PosLocalCoords] | Ericsson, Qualcomm Inc., CATT, Xiaomi, Huawei, Nokia, ZTE | CR | 38.455 | 18.3.0 | TEI18 | 0164 | F | RP-243108
R3-247086 | Correction of TRP Geographical coordinates [PosLocalCoords] | Ericsson, Qualcomm Inc., CATT, Xiaomi, Huawei, Nokia, ZTE | CR | 38.473 | 18.3.0 | TEI18 | 1467 | F | RP-243108
[2Rx_XR_Device] (Cat.F) * This TEI identifier was introduced at RAN#103 by RAN3(CR pack: RP-240618)
TDoc | Title | Source | Type | Spec | Version | Related WIs | CR | CR category | TSG CR Pack
R3-247056 | Support positioning of L2 UE-to-network remote UE [PosL2RemoteUE] | Ericsson, CATT, Xiaomi, ZTE, Huawei, Qualcomm Inc. | CR | 38.455 | 18.3.0 | TEI18 | 0163 | F | RP-243109
TDoc | Title | Source | Type | Spec | Version | Related WIs | CR | CR category | TSG CR Pack
R3-247056 | Support positioning of L2 UE-to-network remote UE [PosL2RemoteUE] | Ericsson, CATT, Xiaomi, ZTE, Huawei, Qualcomm Inc. | CR | 38.455 | 18.3.0 | TEI18 | 0163 | F | RP-243106

## Slide 9: Experience for GTW Usage in f2f meeting
RAN3 has 1 main meeting room and 1 breakout room in RAN3#125bis (1-way remote access)and RAN3#126 (2-way remote access). GTW is provided for breakout room with best effort.
In general, the number of remote participants for main session is quite limited, less than 10. The audio device test for remote access was performed before daily session starts.
MCC and IT support during the meeting are sufficient. Internet connection issue occured on Friday in RAN3#126.

## Slide 10: R19 SON/MDT WI
Progress in the last quarter
MRO Enhancements
  MRO for LTM:
    Add failure type to F1AP ACCESS AND MOBILITY INDICATION message. CU does not forward the RLF Report to DU if failure is due to wrong selection of prepared LTM cell.
    In ACCESS AND MOBILITY INDICATION message, the presence of the C-RNTI IE is kept optional.
    For failure due to inappropriate cell switch triggering, CU forwards RLF Report to the failure DU in case of too late LTM.
    For failure due to inappropriate cell switch triggering, CU forwards RLF Report to the source DU in case of too early LTM, or LTM to wrong cell.
  MRO for CHO with Candidate SCG(s):
    RLF report is enhanced to including Identifier of candidate PCell(s),Identifier of candidate PSCell(s) which met the configured execution conditions.
    The failure types defined for CHO in TS38.300 and for CPAC defined in TS37.340 are used as baseline. Clarification or amendment could be made on top of that if needed.
    In case of too late CHO execution, the last serving MN may need to send message to the candidate MN(s) which may need optimization.
    The serving MN which receives SCGFailureInformation from the UE performs the initial analysis.
    The serving MN forward the SCGFailureInformation to the respective MN which should perform the optimization if needed.
  MRO for S-CPAC:
    A TP that adds S-CPAC handling to the existing MRO for CPAC mechanism described in TS 37.340 was agreed in R3-245834.

## Slide 11: R19 SON/MDT WI
Progress in the last quarter
SON/MDT for NTN and Slicing
  Intra-NTN Mobility:
    For earth fixed case, there is no need to report the measured distance from the UE.
    UE reports the fulfilled CHO trigger conditions before RLF occurs in case of “time and measurement based trigger condition” or “location and measurement based trigger condition”, it is up to RAN2 to decide to reuse the existing IE or not.
    RAN3 assumes both geographical area and the mapped cell ID as Area Scope of logged MDT for NTN over NGAP are feasible and confirm with RAN2 whether the geographical area defined for MBS NTN can be reused for MDT NTN.
  Network Slicing:
    Not to enhance MDT area scope for logged MDT for slice.
    Futher discuss on two use case for slice-based cell reselection.
R18 Leftovers
  UHI/MHI:
    RAN3 agree to support a network-based solution for enhancing PSCell activation/deactivation.
  RACH Optimization for SDT:
    We will send an LS to RAN2 to inform about the previous agreement to report the time from the start of RA-SDT to the reporting of RA report.
Impacts and dependencies on other WGs
Reply LS to RAN2 on MHI enhancement solution for SCG deactivation/activation in R3-247906
LS to RAN2 on RAN3 agreements with impact on UE for Rel-19 SON/MDT in R3-247908.

## Slide 12: R19 AI RAN WI
Progress in the last quarter
Network Slicing:
Enhance the Data Collection Reporting Initiation procedure and Data Collection Reporting procedure to enable requesting and reporting of the predicted radio resource status per slice and predicted slice available capacity over the Xn interface.
Introduce Slice To Report List for Data Collection IE including PLMN ID and S-NSSAI in DATA COLLECTION REQUEST message.
First Bit (Predicted Radio Resource Status) can be reused for requesting predicted slice radio resource status with list of Slice in the DATA COLLECTION REQUEST message.
Introduce the new bit for Predicted slice available capacity in the Report Characteristics for Data Collection IE in the DATA COLLECTION REQUEST message.
Introduce a Predicted Slice Available Capacity IE in the DATA COLLECTION UPDATE message to report the requested predicted slice available capacity to the requesting node.
Source node can request per UE per S-NSSAI granularity for UE performance feedback.
Coverage and Capacity Optimization:
Transferring Future Coverage State and the associated Coverage Modification Cause in the NG-RAN NODE CONFIGURATION UPDATE message.
Transferring the predicted CCO issue via the CU configuration update procedure and transferring the Future Coverage State via the DU configuration update procedure over F1.
Introducing separate time information for future coverage state and predicted CCO issue.

## Slide 13: R19 AI RAN WI
Progress in the last quarter
Mobility Optimization for NR-DC:
Using the Data Collection Reporting Initiation procedure to configure the collection of UE performance at SN side. Introduce the Data Collection ID IE into the SN Addition Request message to identify a Data Collection Reporting context.
Split Architecture Support:
In split architecture, the Energy Cost of gNB is the sum of the Energy Cost of its gNB-DUs. Mapping rule is only configured at gNB-DU and shall be unified for all the gNB-DUs within a defined area.
Introducing Data Collection Reporting Initiation and Data Collection Reporting procedures over F1 interface to transfer measured EC from DU to CU.
Continuous MDT Collection:
RAN3 assumes that the OAM configures Management Based MDT for Continuous MDT towards the NG-RAN.
In R19, introducing the Continuous MDT functionality with a solution being applicable to legacy UEs and not only to Rel-19 UEs.
Impacts and dependencies on other WGs
SA5 updates their specification by enabling configuration of the mapping rule to support EC mapping for Energy Cost Reporting from gNB-DU.
Other important info
N/A

## Slide 14: R19 Topological Enhancement WI
Progress in the last quarter
WAB:
RAN3 to capture WAB in the stage2 spec based on TR 38.799
RAN3 to specify solutions to prevent the multi-hop WAB topology, where multi-hop WAB means that a WAB MT connects to a WAB gNB.
WA: Additional ULI for WAB consists of TAI and NR CGI, which are determined by the WAB-node, reflecting the WAB-node’s physical location. This solution is compliant with Opton1 and Option3. It is up to SA2 to support one of Opton1 and Option3 or both.
For multi-hop prevention in HO case, the target WAB-gNB should reject HO preparation including the S-NSSAI used for Backhauling.
For multi-hop prevention in initial access, to be further discussed whether Solution 1 or Solution 3 (or both) need to be selected
For WAB mobility, the “two logical gNB solution” can support UE’s AMF change during WAB-gNB mobility.
Femto:
Discuss and agreed the architecture and CP/UP protocol stack for NR Femto with/without NR Femto GW.
Support the transport of NG-U between the NR Femto and the 5GC may be optionally concentrated in the NR Femto GW
Support the access control by reusing the CAG mechanism for PNI-NPN
One NR Femto serves one or more cells.
Impacts and dependencies on other WGs
LS to SA2 agreed to ask SA2 to provide feedback on whether the single-gNB solutions can be achieved without CN impact.
RAN3 update the NR Femto Architecture to support NG-U concentration in NR Femto GW.

## Slide 15: R19 Mobility Enh WI
Progress in the last quarter
Current SSB information in Xn Setup and Configuration Update procedures can be reused for LTM preparation phase.
Introduce a new procedure for candidate gNB-initiated LTM cancellation.
The source CU can request candidate CU to provide CSI-RS configuration in HANDOVER REQUEST message, and candidate CU signals the CSI-RS configuration in HANDOVER REQUEST ACKNOWLEDGEMENT message.
Turn the WA into agreement: For inter-CU LTM mobility, a separate LTM request message (i.e. HANDOVER REQUEST message) is used for each candidate cell.
To support subsequent LTM, the LTM Configuration Update procedure is reused to establish UE association between the new source gNB and the other candidate gNB(s) after each inter-CU LTM Cell Switch.
Confirm the message name as LTM Cancel for candidate gNB-initiated LTM cancellation.
Turn the WA into agreement: Reuse the existing XnAP UE CONTEXT RELEASE message at the source gNB if no LTM candidate cell(s) exists in the source gNB.Continue to work on the solutions comparison and details.
Impacts and dependencies on other WGs
LS R3-247911 is sent to RAN1, RAN3 confirmed it is feasible to specify the signalling for coordination between serving cell and candidate cell(s) on the transmission of semi-persistent CSI-RS(s), and RAN3 will continue to work on the details.
RAN3 moves forward with Legacy framework with PDCP change/switch for inter-CU LTM in this release, not considering the PDCP anchor based solution.
Other important info
N/A

## Slide 16: R19 NR NTN WI
Progress in the last quarter
MBS broadcast service:
  RAN3 takes the assumption that geographical service area information can be transmitted from CN with the same format as defined in Uu.
  The current MBS broadcast procedures can be reused for NR NTN without any enhancement.
Regenerative payload:
  The supported TAIs of an on-board gNB could be provided to AMF by OAM/pre-configuration.
  The current mechanisms including, e.g. multiple TNLA association, are sufficient for TNL management during feeder link switch.
  RAN3 assumes that during the feeder link switch, AMF is not changed for the UEs. Whether there has any standard impact needs to be further checked.
Impacts and dependencies on other WGs
  N/A
Other important info
  N/A

## Slide 17: R19 IoT NTN WI
Progress in the last quarter
  Support of eNB as regenerative payload without S&F satellite operation needs to be clarified in RAN plenary.
Impacts and dependencies on other WGs
  N/A
Other important info
  N/A

## Slide 18: R19 Ambient IoT SI
Progress in the last quarter
For topology 1, Reader ID is included in the Inventory report and Command response message in addition of AIoT RAN node ID.
For topology 1, A-IoT RAN needs to store the A-IoT Device Identification received from the inventory request.
For topology 1, A-IoT RAN should be able to differentiate between command and inventory.
For topology 1, only one reader ID included in Inventory report and Command response message. If AIoT RAN node would receive multiple responses for the same AIoT device it can send multiple inventory report messages.
An AIoT enabled gNB could support both topologies, this is an implementation matter.
The RAN architecture should enable the coordination of the usage of the A-IoT radio resources among readers, for both T1 and T2.
NGAP is always be used between RAN and AIoT CN.
In RRC based solution, Reader selection may need coordination between A-IoT-enabled gNB and A-IoT CN.
For topology 2, the AIOT CN may get UE reader location via ULI in NGAP messages or via legacy LCS mechanism.
Impacts and dependencies on other WGs
No evaluation and down selection for T2 solutions have been performed which requires coordination among WGs.
Editor’s note: Whether and which of the following options on CN triggered A-IoT session resource allocation and UE triggered A-IoT session resource allocation will be finally considered needs further discussion involving other WGs as needed.
Other important info
This SI is completed in RAN3.

## Slide 19
Progress in the last quarter
On-demand SSB SCell operation:
  For RRC based signalling, the DU can decide activation/deactivation state of OD-SSB configuration per SCell and convey it to the CU included in the RRC container. There is no RAN3 impact.
  On-demand SIB1 for UEs:
  The UL WUS configuration will be transferred over Xn via a new class1 defined procedure.
  Cell A gNB can decide and signal to NES Cell gNB that it stops the UL WUS configuration broadcast in its SIB.
  The purpose of the new XnAP procedure is to enable an NG-RAN node1 to provide UL WUS configuration information to NG-RAN node2. The procedure uses non UE-associated signaling.
  Cell A stores the UL WUS configuration information after it has received it.
  A Class 2 procedure is to be introduced for Cell A gNB to signal to NES Cell gNB that it stops the UL WUS configuration broadcast in its SIB. The procedure uses non UE-associated signalling.
  Reuse the existing IE “Served Cell Information” IE to include UL WUS configuration from gNB-DU to gNB -CU in F1 Setup Request and gNB-DU Configuration Update procedures.
Impacts and dependencies on other WGs
  N/A
Other important info
  N/A
R19 Network ES WI

## Slide 20
Progress in the last quarter
The LP-WUS assistance information IE, which includes the CN assigned subgroup ID for LP-WUS, is introduced in the NG paging message, is introduced in the NGAP core Networking assistance information IE, and is introduced in F1 paging message. 
The gNB-DU is responsible to generate and broadcast the LP-WUS related configuration, including LP-SS configuration, LP-WUS configuration, and the entry/exit condition for LP-WUS monitoring.
NG-RAN node can acquire the total number of CN assigned subgrouping via OAM.
WA: the anchor gNB provides the new LP-WUS paging subgrouping assistance information IE into the Xn RAN paging message including CN assigned subgroup ID.
WA: Introducing LP-WUS subgrouping support indication per-cell in F1 paging message. This applies for both UE_ID based subgrouping and CN based subgrouping.
Impacts and dependencies on other WGs
The 2 WAs may depend on RAN2 progress.
Other important info
N/A
R19 LP-WUS WI

## Slide 21: R19 Duplex WI
Progress in the last quarter
RAN3 agrees to Exchange the following information over Xn interface and F1 interface:
  Semi-static cell-specific SBFD time and frequency location configuration with cell granularity (FFS on container or explicit IEs over XnAP and F1AP)
  Measurement resource configuration
  Strongest DL beam information (FFS on the details)
  CLI-mitigation request (FFS on the details)
The SBFD time and frequency location configuration with cell granularity in Served Cell Information NR IE shall be introduced in XnAP XN SETUP REQUEST message, XnAP XN SETUP RESPONSE message, XnAP NG-RAN NODE CONFIGURATION UPDATE message and XnAP NG-RAN NODE CONFIGURATION UPDATE ACKNOWLEDGE message.
Impacts and dependencies on other WGs
N/A
Other important info
N/A

## Slide 22: R19 AI PHY WI
Progress in the last quarter
Consider aggregated gNB case first, then split architecture. The existing LCS framework is re-used for AI/ML positioning.
Case 3b：
  Re-using the Measurement procedure defined in NRPPa to support requesting and reporting the related measurements to LMF for Case 3b.
  NG-RAN gets measurements (i.e., part A information as called by RAN1) from TRP and provides them to LMF.
Case 3a：
  The AI/ML model (inference and training functions) is at the gNB.
  LMF provides ground truth label and related data (i.e., part B information as called by RAN1) to NG-RAN. NG-RAN obtains measurements from TRP (i.e., part A information as called by RAN1).
  RAN3 will proceed with Option A: NG-RAN node performs monitoring metric calculation for its own model.
  Signalling of measurements as the inference output for case 3a can re-use the existing procedures for positioning measurement specified over NRPPa.
  WA: The LMF starts a NRPPa transaction. The gNB determines that data collection is needed.
Impacts and dependencies on other WGs
The details of the measurements are still pending and subject to further discussion in RAN1.
Reply LS to SA2 on AIML data collection in R3-247801.
Other important info
N/A

## Slide 23: TEI Corrections
Progress in the last quarter
R18 Positioning:
Correction to Requested DL PRS Transmission Characteristics, area-specific SRS activation and UE-specific SRS reservation.
Enable the LMF to request the gNB to perform measurements for UL-TDOA or Multi-RTT occurring within indicated time window(s) only or not. An additional parameter is proposed to indicate the start of the measurement time window.
Include helpful information on the reference signal that was used for measuring the UE Rx-Tx Time Difference.
Miscellaneous corrections on stage2 & stage3 for positioning.
R18 AI/ML for NG-RAN:
Correction to reflect that implementation specific aspects related to model performance feedback are out of scope.
OAM requirements for Energy Cost index.
Sending LS to SA5 to request clarification the definition of per-UE average UE throughput metric.
R18 SON/MDT:
Stage 2 clarification on CPAC failure and procedural description on CPAC Configuration
Stage 3 clarification on LBT Failure Information of NR-U
Stage 2 clarification on UHI
ASN.1 correction on CCO and Mobility Change procedure

## Slide 24: TEI Corrections
Progress in the last quarter
R18 IoT NTN:
RAN3 agrees for NB-IoT NTN UE, the coarse UE location reporting from MME to eNB is performed upon eNB request, per UE, and only once for UE during RRC connected state.
Based on eNB request, MME will provide Coarse UE Location Information to the eNB for a given UE.
R18 Mobility Enhancements:
Support of Early TA acquisition for the inter-DU scenario and intra-SN SCPAC in MN format, continue discussing L3 measurement based LTM support over F1.
  IAB:
Correction on stage 2 for IAB F1-C transfer in NR-DC to clarify there is only one IAB donor in this scenario
Correction on semantics description for IAB resource multiplexing
Correction on BAP mapping configuration on ASN.1 logic error
Correction on IE description of IAB resource coordination procedure to cover the scenario where the parent node of an IAB-node is an IAB-donor DU
XR and multi-modality
RAN3 replies SA2 that it is technically feasible to enhance NGAP to provide the MMSID to NG-RAN node.
RAN3 replies RAN2 and SA2 to confirm the usage of MMSID, while traffic synchronization can be further checked in RAN3 based on the progress in other WGs.
RAN3 replies SA2 that RAN3 has no consensus on whether to support dynamic PSI activation/deactivation from RAN to 5GC and expects SA2 to further discuss based on RAN3 feedback.
For UL PSI based discard, no further enhancements between MN and SN are needed in Rel-19.

## Slide 25: TEI Corrections
Progress in the last quarter
SDT network-based solution:
The network based solution is not supported in R18 taking the concerns into account.
  Renewable Energy:
Reply to SA5 that support of renewable energy at the RAN is valuable. There is no proper WI in RAN3 concerning this topic in R19.
  NR MBS:
Correction on configuration update for an inactive Multicast session
Correction on broadcast reception for eRedCap UE
Correction on N3mb path failure

## Slide 26: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and organizing social events during the meetings!
  Thanks Jiajun, Nianshan help to organize the basketball match with RAN2！
Seonggu (RAN WG3 Secretary)
  For impressive hard work and continous support!
Yan, Miaoqi, Alex, Philippe G, Georg...
  For their positive and hard work to complete R19 SI!
  For moderating some tough email discussions and good support!
All Rapporteurs and moderators
  For their efforts to rapporteur updates and TEI corrections!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!

## Slide 27: RAN3 Social Events in Heifei and Orlando
Notes: w

## Slide 28: RAN3vsRAN2 Basketball Match
LS to RAN2 triggered in R3-245824 in RAN3#125bis, the friendly match plans to be held in April, 2025.
Playing basketball requires a combination of physical and technical skills, same as in RAN3!
Notes: w