## Slide 1: Time and Frequency Interleaving for LTE-based 5G Terrestrial Broadcast
ABS, ABP, SJTU, CUC, Qualcomm, Rohde & Schwarz, Xiaomi, Vivo
3GPP TSG RAN Meeting #106
Madrid, Spain, December 8-12, 2024
Agenda item: 10.1.1
RP-242452

## Slide 2: To enable Direct-to-Mobile TV Broadcasting
Using broadcasting frequencies (UHF)
  470MHz – 694MHz (3GPP B107/B108)
Upgrading and reusing Digital Terrestrial Television (DTT) infrastructure to build standalone HPHT networks
  There are about 7,000 HPHT stations in China.
Operated by broadcasters
Providing public radio, television and warning services mainly to smartphones directly (and maybe other devices if possible).
DTT Transmitter (HPHT)
Release 14/16
FeMBMS
Dedicated carrier

## Slide 3: Do not impact LTE Equipment and Network for MNO
  Software difference:
    Exciter: downlink only, pre-configured channels, parameters and channel to physical resource mapping;
    No need to dynamically schedule resource for services.
DTMB - DTT Standard in China
  Hardware difference:
    Exciter: outputs RF signal connecting to Amplifier with SMA or other types RF cable;
    Amplifier: usually 1kW;
    Feed tube: Φ40/80mm;
Standard: Don’t seek to change the parts for LTE equipment and network. Just make some
extensions necessary for 5G Broadcast.
Network: 5G Broadcast network will be standalone HPHT networks.
Upgrade to 5G Broadcast

## Slide 4: Time and Frequency Interleaving is Missing from 5G Broadcast
Time interleaving is present in all modern broadcast standards as an essential feature to combat rapid fading and impulsive noise.[1] It have been demonstrated over the course of many years in real world deployments.
The benefits of frequency and time interleaving have been verified under 3GPP system in several contributions.[2-7]
During the work item on 5G terrestrial broadcast, time and/or frequency interleaving for 5G terrestrial broadcast was discussed even though it was not explicitly in the scope of the WID RP-191924. However, no agreement was reached may due to lack of time.

## Slide 5
5G Terrestrial Broadcast Trials in China
2023, Chengdu, 630~638MHz, 300W
2019, Beijing, 750~758MHz, 1000W

## Slide 6: Observation
The red line segments on the map show the effect of rapid fading and impulsive noise caused by the buildings or overpasses to some extend due to the missing of time and frequency interleaving function.

## Slide 7: Proposals
Add Time and Frequency Interleaving function for LTE-based 5G Terrestrial Broadcast.
  Only for MBMS-dedicated cell;
  Only for UEs which support receiving FeMBMS on MBMS-dedicated carrier in receive only mode;
A new work item for this in Release 19.

## Slide 8: References
[1] R1-1913095 Information on Time Interleaving in State-of-the-Art Terrestrial Broadcast Systems, EBU/BBC/IRT/ABS/NHK.
[2] R1-1912692 Numerology with 100us CP, Qualcomm Incorporated.
[3] R1-1912331 CRBI-based interleaver for 5G terrestrial broadcasting, ABS,SARI-CAS,Shanghai Jiao Tong University
[4] R1-1913343 On the performance evaluation of HARQ-based time-interleaving for LTE-based 5G terrestrial broadcast, EBU, BBC, IRT
[5] R1-1912690 Support of longer numerologies for rooftop reception, Qualcomm Incorporated
[6] R1-1911355 Time and Frequency Interleaver for LTE-based 5G Terrestrial Broadcast, EBU, BBC, IRT
[7] R1-1913439 On time and frequency interleaving for terrestrial broadcast

## Slide 9
Thank you！