## Slide 1: Views on MIMO Phase 6 WI for Rel-20
RAN#106
Madrid, Spain
December 09-12, 2024
RP- 242575
Agenda : 15.2

## Slide 2: High level views on NR Rel-20 MIMO WI
Further MIMO enhancement is not top priority for NR Rel-20. It can be a middle priority WI, if the number of TUs for NR Rel-20 allows.
If included in NR Rel-20, NR Rel-20 MIMO WI should target simple enhancements.
  Objectives with significant impact to specification should not be approved because the outlook of their successful commercialization is poor.
  If included in NR Rel-20, NR Rel-20 MIMO WI should target enhancements with potential benefits to fix real issues observed in current 5G eco-systems

## Slide 3: High-resolution UL MIMO precoders - Motivation
UL performance (coverage and cell edge data rate) of NR is a bottleneck of existing NR eco-system.
UL coherent MIMO can improve UL performance with beamforming gain.
Current UL coherent MIMO specification only supports QPSK based precoders.
The above motivate to introduce higher resolution UL precoders, e.g., 8PSK and 16PSK, in NR Rel-20.
  Intuition: High spatial resolution does not sharpen the beam width, but refine the beam steering granularity, which is the source of the performance gain.
Tx
QPSK precoder
Tx
8PSK/16PSK precoder
Rel-19
Rel-20

## Slide 4: High-resolution UL MIMO precoders - Justifications
Justification 1: Performance gain with high resolution precoders is decent, especially at cell edge.
  Observation 1: 10% gain (@50% cdf) is achieved with 0 dB antenna imbalance. Even with 3dB antenna imbalance, 7% gain is achieved (@50% cdf).
  Larger gain (~20%) observed at cell edge.
  Note: In the above simulation results, current RAN4 requirements (4dB power error margin and +/- 40 degrees phase error margin between SRS and PUSCH) on antenna coherence is followed. We did not tighten RAN4 requirements in the simulations.
Cell edge UEs
Tput Gain (16PSK/QPSK)
cdf of Tput Gain

## Slide 5: High-resolution UL MIMO precoders - Justifications
Justification 2: Specification impact of high-resolution precoders is small.
  RAN1 specification impact 1: introduce larger UL coherent and partial-coherent precoder codebooks in 38.211 for 2-Tx.
  RAN1 specification impact 2: “potentially” increase the bit-width for TPMI indication by 1 bit in DCI.
    Note: if considering only 8PSK precoders for 2-Tx, or not adding all 16PSK precoders for 2-Tx, the existing 7 reserved codepoints can be used to signal the added precoders without even increasing the bit-width in DCI.
  RAN 4 specification of Tx antenna coherence (amplitude and phase tolerance) is kept as it is. We don’t intend to tighten RAN4 requirements in Rel-20.
    Note: although it can bring larger gain, further tightening RAN4 requirements for high resolution precoders could require large amount of work in RAN4.
    The RAN4 specification impact is limited to updating the precoder Table reference.
Rel-15 2-Tx full coherent CB has 9 precoders, which requires 4 bits in DCI with 7 codepoints reserved.
The signaling of high resolution precoders can use the 7 reserved codepoints.

## Slide 6: High-resolution UL MIMO precoders - Justifications
Justification 3: The impact of high-resolution precoders to UE and gNB implementation is small.
Impact to UE implementation:
  The high-resolution precoding is still wideband UL precoding. The UE implementation only needs to take care of matrix multiplication with 8PSK/16PSK entries, which is trivial.
Impact to gNB implementation:
  The high-resolution precoding is transparent to gNB PUSCH demodulation and decoding as DMRS is precoded in the same way as PUSCH data.
  gNB scheduler’s TPMI selection algorithm need pick a precoder from a larger codebook than current codebook, which should not be difficult to do.

## Slide 7: Summary of the proposal
If NR Rel-20 includes MIMO WI, specify spatial high-resolution UL coherent precoders, e.g., precoders with 8PSK or 16PSK entries, for 2-Tx [RAN1].
  Note: Keep RAN4 requirements for UL Tx coherence (amplitude and phase tolerance) as is without tightening the requirements.