## Slide 1
3GPP TSG RAN Meeting #106 RP-242620
Madrid, Spain, December 9th – 12th, 2024
Agenda Item: 9.3.1.5
Source: vivo
Title: Discussion on OD-SIB1 impact on connected UEs in Rel-19 NES
Document for: Discussion and Decision

## Slide 2
Rel-19 NES On demand SIB1- Background
On-demand SIB1 was converted to normative work after RAN#105
References: RP-242354 Revised WID - Enhancements of network energy savings for NR
2. Specify support for on-demand SIB1 for UEs in idle/inactive mode [RAN1/2/3]
• Specify procedures and signaling method(s) for Case 2 [RAN1/2]
- Case 2: UE obtains UL WUS configuration from Cell A, UE transmits UL WUS on NES Cell, UE receives on-demand SIB1
from NES Cell
- Triggering method by UL WUS using PRACH
• Specify inter NG-RAN node signalling at least for the configuration of UL WUS [RAN3]
• Note 1: No modification of SSB will be discussed under this objective
• Note 2:
- UL WUS: Uplink wake-up signal
- Cell A: A cell that is periodically transmitting at least its own SIB1
- NES Cell: A cell that may transmit SIB1 transmission in response to UL WUS from a UE
• Note 3:
- RAN1 strives to minimize impact to legacy UE
- RAN1 specification impact to support this feature should be minimized

## Slide 3
Rel-19 NES On demand SIB1- RAN2 discussion
RAN2#128: RAN2 discussed handling of RRC connected UEs
References: R2-2410911 Report from session on V2X/SL, R19 NES and MOB
Background: If a UE is in RRC_CONNECTED with an active BWP configured with common search space with the field searchSpace-OtherSystemInformation and the UE has not stored a valid version of a SIB or posSIB, the UE needs to check the si-BroadcastStatus contained in SIB1 to determine if it acquires the SI message(s) directly or triggers OD-OSI request with DedicatedSIBRequest. However, the always-on SIB1 is not transmitted in an OD-SIB1 NES cell.
  On handling RRC connected UEs which requires SIB1 for acquisition of OSI, several potential solutions were identified, which can be categorized as:
    Option 1: Revise the WID to support RRC connected UE requesting OD-SIB1, with either Msg1 based method which is now under discussion, or RRC based method so that the UE can request OD-SIB1 with enhanced DedicatedSIBRequest or a new RRC message.
    Option 2: Address the issue without revising the WID, e.g. the UE can request the OD-OSI directly without checking the si-BroadcastStatus in SIB1
  Conclusion:
  Wait one cycle of RAN discussion (i.e. to see whether WID is updated or not to handle RRC connected UEs)

## Slide 4
Rel-19 NES On demand SIB1- RAN2 discussion
Option 1: Revise the WID to support RRC connected UE requesting OD-SIB1, with either Msg1 based method which is now under discussion, or RRC based method so that the UE can request OD-SIB1 with enhanced DedicatedSIBRequest or a new RRC message;
Option 2: Address the issue without revising the WID, e.g. the UE can request the OD-OSI directly without checking the si-BroadcastStatus in SIB1;
 | Pros | Cons
Option 1 | All cases and solutions can be discussed | RAN2 has not fully discussed and identified all the potential use cases for RRC connected UE requesting OD-SIB1, which may involve more discussion and specification work; RAN2 has to discuss whether to down-select from Msg1 based method and RRC based method;
Option 2 | No WID update, no TU change | May only focus on the simple solution.
Proposal 1: RAN2 to discuss how RRC connected UE acquires on-demand OSI with no WID update