## Slide 1: Support of Network Energy Savings in high/medium load cells in the Network ​
3GPP TSG RAN Meeting #106 RP-242636
Madrid, Spain, 9-12 December 2024
Source: Vodafone
Agenda Item: 15.2

## Slide 2: Shifting the focus of NES techniques for medium/load scenario
Justification
In Rel-18 and Rel-19 work items, most of the techniques specified aimed to reduce energy consumption in light to low load scenarios. For Rel-20 we prefer techniques that focus on medium to high-load scenarios, for both single and multicarrier:
  Single carrier: currently implemented energy saving techniques mean that if we have X+1 light/medium loaded carriers, we shut down 1 or more carriers to leave X medium/heavily loaded carriers. Typically, the remaining carriers are on the low frequency bands and FDD, and the UE is not using CA.
  Multicarrier: in a heavily loaded cell sector, techniques that save power when using CA are beneficial.
Objectives
Improvements of gNB PA efficiency in high-load scenarios (e.g. techniques D2-D5 in TR 38.864).
Use of AI/ML techniques for network energy saving based on traffic load e.g. Dynamic cell deactivation, cell power reduction, and antenna ports reduction by leveraging Rel-18 spatial/power adaptations and AI/ML beam management use case.
Any other techniques suitable for medium/high load scenarios.

## Slide 3: Thank you