## Slide 1: Views on Ambient IoT Work Items
Wiliot
3GPP TSG RAN Meeting #106 RP-242659
Madrid, Spain, December 9 - 12, 2024

## Slide 2: Rel-19 RAN1 SI Status
The November Working Group meeting was the final session under the SI phase. Nonetheless, some topics remain underexplored, and several areas lack clear resolutions or recommendations. Listing RAN1 highlighted open topics [R1-2410845] for down-selection:

## Slide 3: Timeline Considerations
With many critical design options left unresolved and no clear recommendations from the SI phase to several design options, completing the first phase of the WI in Rel-19 within just 3 WG meetings is highly challenging.
Considering that Rel-20 WIs need to be finalized by Q1 2027, any delay in finalizing Rel-19 WIs will impact the timeline for Rel-20.
To optimize TU utilization, a continuous plan for Rel-19 and Rel-20 is recommended:
  Gradual evolution of all device types between Rel-19 and Rel-20.
  Focus on a harmonized solution in Rel-19, based on relaxed and common requirements subset.
  In Release-20, address the missing performance options as applicable.

## Slide 4: Possible Directions for Rel 19 SI AIoT WI Conversion
We believe that standardizing all device types will significantly enhance the usability of ambient IoT. Currently, the usability of passive IoT devices is constrained by their limited 10-meter coverage, and evaluations indicate even shorter ranges.
To address the time limitations and ensure compatibility across all device types, we propose to support both passive and active devices for harmonized design in Rel-19 and enhance performance in Rel-20 (refer to RP-242660).
SI Rel 19
WI Rel 19
SI Rel 20
WI Rel 20
2026
2027
2025
Q1
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q4
Q2
2024

## Slide 5: Proposed RAN1 Rel 19 WI Scope
Specify signal design considering harmonized design for device 1/2a/2b including
  OOK Modulation
  Share all clock type requirements (the most relaxed, for each case)
Type 2 topology, for simplicity of network integration
  Prioritize D2T2 indoor with all deployment scenarios: A1,A2,B,C
Proximity based on solution 1
TDMA for Multiple Access
Manchester line coding for R2D, no line coding for D2R
Device (un)availability Direction 1
To support timely convergence and account for the harmonization of all device types, we propose that the down-scoping prioritizes the following: